## Slide 1: View’s on Rel-20 RAN1,2,3 led 5G A topics
3GPP TSG RAN Meeting #108
Prague, Czech Republic, June 9-13, 2025
RP-250889
Agenda 15.0
Source: Ericsson

## Slide 2: Summary for RAN Release 20 5G-Adv (RP-250812)

## Slide 3: Enhancements to AI/ML for air interface Moderator summary with Ericsson addition in Red
Moderator assumes the following for the purpose of TU planning:
Include CSI compression for two-sided model as part of Release 20 5G-Adv
  Final decision on whether to support CSI compressions for two-sided model as part of Release 20 5G-Adv will be made considering the outcome of Release 19 AI/ML air interface study item
  If final decision is to not include CSI compression, TU for Release 20 5G-Adv AI/ML air interface will be revised accordingly
No new use case / features in Release 20 5G-Adv AI/ML air interface
No 2nd priority cases from Rel-19 AI/ML positioning in Release 20 5G-Adv AI/ML air interface
Further discuss additional LCM specification support (e.g. data collection and model transfer/delivery) in RAN#108
[2] TUs in RAN1 and [2] TUs in RAN2 for Release 20 5G-Adv AI/ML air interface
[2] TU in RAN4 if “test decoder” standardized in RAN4

## Slide 4: NR MIMO Moderator summary with Ericsson addition in Red
Moderator assumes the following for the purpose of TU planning:
For Rel-20 5G-Adv MIMO, the scope should be limited and well justified by commercial needs
[1] TU in RAN1 and [0.5] TU in RAN2 for Release 20 5G-Adv MIMO
[0.5] TU in RAN4
Requires further down-selection, to 2 objectives, one for DL and one for UL
Plenary to do the down-selection
Notes: RAN4 TU split between RF, RRM and demod depending on what is decided. For our preferences, early CSI triggering impacts RRM and SRS mapping RF

## Slide 5: Ambient-IoT Moderator summary with Ericsson addition in Red
Moderator assumes the following for the purpose of TU planning:
Device 1 in D2T2
Device 2b in D1T1 and D2T2
Study on A-IoT for outdoor scenarios
  A-IoT to address use cases and scenarios that cannot otherwise be fulfilled based on 3GPP mIoT technologies; A-IoT positioned well below 3GPP mIoT technologies (NB-IoT, eRedCap) and positioned well below 6G eMBB/mIoT RAT unified design
Further discuss other aspects of Rel-20 A-IoT (e.g. DO-A traffic, unavailability direction 2) in RAN#108
[3~3.5] TUs in RAN1 and [2] TUs in RAN2 for Release 20 5G-Adv A-IoT
[1] TU in RAN3 and [2 RF, 0.5 RRM] TU in RAN4

## Slide 6: Coverage
Support RP-251467 WF on NR coverage enhancements for Rel-20
[0] TU in RAN4

## Slide 7: ISAC Moderator summary with Ericsson addition in Red
A set of possible objectives of Sensing/ISAC in Rel-20 are listed below:
  Study on gNB mono-static mode and possibly bi-static mode for UAV use case. [RAN3, RAN1, RAN4]
  Study the procedures and signaling support between RAN and CN, and the corresponding sensing measurements. [RAN3, RAN1]
  Performance evaluation for gNB sensing. [RAN1]
  Note: No new waveform/RS to be specified in RAN1 and no UE impact is expected.
  Note: Coordination with SA2 when needed.
  Note: gNB mono-static and bi-static is to be supported by the same RAN signaling scheme: No standardized signalling between gNBs for bi-static mode but shown in stage 2
[1] TU in RAN1 for 3 quarters, [1] TU RAN3 for 3 quarters

## Slide 8: NR NTN Moderator summary with Ericsson addition in Red
Conclusion for GNSS resilient operation
Study Item with checkpoint to determine whether we have normative work and the scope based on results of study item phase.
    Study should consider Rel-16 as baseline for discussion. Study should focus on NR NTN and be backward compatible with legacy UEs. Aim to minimize physical layer procedures impact to 5GA and avoid physical layer channel/signal changes.
    Objective to be narrowed down for RAN#108
No additional NR NTN enhancements with RAN1 impact can be considered at this point given limited 5GA TUs
Additional topic to be included in objective.
Specify necessary enhancements to support E-UTRA TN to NR NTN handover in RRC connected mode
TU estimate RAN2 (0.25 TU), RAN4 (0.5)
Deadline to complete the work (first half of release)

## Slide 9: Summary for RAN Release 20 5G-Adv (RP-250812)

## Slide 10: AI for Mobility
Support RP-250973 Discussion on normative working scope of AI Mobility in R20
[2 RRM] RAN4 TUs

## Slide 11: Mobility Moderator summary with Ericsson addition in Red
Specify LTM SCell improvements for further reducing interruption delays
  SCell activation
    Specify the necessary configuration and UE procedures for NW triggering of LTM SCell activation with LTM cell switch [RAN2, RAN3].
    Evaluate and specify as necessary the needed RAN4 requirements for this [RAN4].
NOTE: Reuse the candidate cell LTM measurement and reporting procedures where possible for the SCell improvements
NOTE: This objective is NOT applicable to non-co-located CA and is NOT applicable to C-LTM
NOTE: This objective is applicable to MCG and SCG
Dynamic L1 measurement and reporting configuration change
  Specify the necessary configuration and procedures for MAC CE based configuration selection among prior provided RRC configurations of UE L1 measurement and reporting LTM configuration [RAN2]
  Evaluate and specify as necessary the needed RAN4 requirements for this [RAN4].
NOTE 1: This sub-objective is applicable to C-LTM as well.
NOTE 2: For this objective, we strive to avoid RAN1 impact (including reporting)
NOTE 3: RAN1/RAN3/RAN4(?) involvement is based on LS if necessary
[0.5 RRM] RAN4 TUs

## Slide 12: NTN for IoT Moderator summary with Ericsson modifications in Red
Study and specify necessary enhancements to support Voice over NB-IoT-NTN via GEO:
  Until RAN#111, study and down select between UP or CP mode for supporting voice over IoT-NTN. Coordinate with SA2 as needed. [RAN2]
  Modifications to the initial access and RRC connection procedures including how to handle overload situations [RAN2]
  Support semi-persistent scheduling (SPS) for voice frames (e.g., 20 ms) and bundled voice frames (e.g., 40 ms, 80 ms). [RAN1, RAN2]
    Simulation assumptions and evaluations:
      NPUSCH Format 1 with 3.75 kHz and/or 15 kHz SCS using single-tone and/or multi-tone/NPDSCH with 15 kHz SCS.
      Assuming one or more than one Resource Unit (RU)/NPDSCH subframes depending on Transport Block size deemed to be suitable for transmitting a voice packet.
      Assuming the use of repetitions (e.g., the number of required repetitions can be based on a link-budget analysis).
      Assuming transmission on an anchor carrier and non-anchor carrier.
      Any NPDCCH/NPDSCH scheduling required e.g., for IMS.
      Note: Based on the feasibility identified from the evaluation, the options in the bullets above may be subject to down-selection.
Note: Only stationary UEs communicating over GEO satellites is in scope meaning for example enhancement of mobility procedures is not in scope.
TU allocation: RAN2 [0.5], RAN1 [0.5]

## Slide 13: Summary for RAN Release 20 5G-Adv (RP-250812)

## Slide 14: AI/ML for NG-RAN Moderator summary with Ericsson addition in Red
Rel-20 AI/ML for NG-RAN should be based on current 5G architecture and interfaces.
The objectives of AI/ML for NG-RAN in Rel-20 are listed below:
  Study the following new AI/ML based use cases and down-scope (1 or 2 use cases) in next plenary [RAN3]:
    QoE Optimization; prio 1
    Network energy saving
    Mobility (including Multiple-hop target node UE trajectory) prio 2
  Note: Other Leftovers depend on Rel-19 outcome, if any.
  Note: Coordination based on LSs with other working groups, when needed.
6 months for the Rel-20 Study Item on AI/ML for NG-RAN, followed by 12 months for the subsequent Work Item.