## Slide 1: Proposal on additional scope for Rel-20 mobility
Fujitsu, ETRI, KDDI, NTT DOCOMO, Verizon
3GPP TSG RAN Meeting #108
Prague, Czech Republic, June 9-13, 2025
Agenda Item: 15.2.3
Document for Discussion
RP-250979

## Slide 2: Motivation
Interference measurements are used for legacy L3 mobility, especially for inter-frequency scenario, and interference measurement is also useful for LTM to make the appropriate cell switch decision
  Candidate cells may be suffered from strong interference, and hence cell switch decision by RSRP may not be sufficient
Introduction of L1-SINR measurement has been proposed and discussed in RAN1 for Rel-18 and Rel-19, but no consensus was achieved
  In Rel-18, L1-SINR was dropped due to no support of CSI-RS
  In Rel-19, moderate number of supporting companies, including operators, proposed to introduce CSI-RS based L1-SINR, but no consensus was reached due to the following reasons
    Usefulness of interference measurement: dynamic fluctuation of interference
    Workload in RAN4
In Rel-20, L1-SINR measurement should be introduced by addressing the issues observed in Rel-18 and Rel-19

## Slide 3: Summary of the offline discussion
Reporting
  gNB scheduled reporting
    Fluctuation of interference measurement results can be managed by gNB implementation
    Discussion on filtering in RAN1 can be avoided
  Event triggered reporting
    Less overhead of the reporting
    RAN1 or RAN2 discussion on filtering is expected, resulting in more TU consumption
Support of inter-frequency scenario
  L1-SINR measurement is useful for inter-frequency LTM
  Intra-frequency L1-SINR measurement is also required for the comparison between intra-(including serving cell) and inter- frequency cells
CSI-RS vs SSB
  SSB is the most important reference signal for mobility, LTM started with SSB based L1-RSRP
  CSI-RS based L1-RSRP is useful for accurate measurement with narrow beams
  Interference measurement resource has been introduced for CSI acquisition in Rel-19, and it can be reused for L1-SINR based on both SSB and CSI-RS.

## Slide 4: Proposal
Specify support for L1-SINR measurement quantity for L1 measurements for LTM [RAN1,RAN2, RAN4]
  L1-SINR measurements to be included gNB scheduled reporting [and event triggered reporting
    Filtering of measurement results is up to UE implementation for gNB scheduled reporting
    [gNB configurable IIR filtering is introduced for event evaluation and reporting]
  Support of inter-frequency scenario
  Support of SSB (SS-SINR) and CSI-RS(CSI-SINR) with second priority
The following scope is additionally introduced for Rel-20 mobility enhancement
Note: yellow part is for further discussion at RAN#108: whether or not the workload of this part is acceptable

## Slide 5: Estimated additional workload to support L1-SINR (Alt 1. w/o event triggered reporting)
RAN1: additional 0.5 TU for 2 quarters
  Support of L1-SINR measurement and reporting based on legacy specs
RAN2: No additional TU
  Introduction of RRC parameters based on RAN1 agreements
RAN3: No additional TU
  RAN3 issues can be handled based on LS, if necessary
RAN4: additional 0.5 TU for entire Rel-20 period (i.e. 1.0 TU in total)
  Introduction of inter-frequency L1-SINR measurement
Max TU estimation for WI Mobility in RP-250803 : RAN2 [1 TU], RAN3[0.5], RAN4 [0.5]

## Slide 6: Estimated additional workload to support L1-SINR (Alt 2. w/ event triggered reporting)
RAN1: additional 0.5 TU for 3 quarters
  Support of L1-SINR measurement and reporting based on legacy specs
  Support of gNB configurable filtering
RAN2: No additional TU
  Support of L1-SINR for event evaluation and reporting– can be handled within the allocated 1 TU
  Introduction of RRC parameters based on RAN1 agreements
RAN3: No additional TU
  RAN3 issues can be handled based on LS, if necessary
RAN4: Additional 0.5 TU for entire Rel-20 period (i.e. 1.0 TU in total)
  Introduction of inter-frequency L1-SINR measurement
Max TU estimation for WI Mobility in RP-250803 : RAN2 [1 TU], RAN3[0.5], RAN4 [0.5]