## Slide 1
Huawei, HiSilicon
Rel-20 ISAC scope
3GPP TSG RAN#108 RP-251163
Prague, Czech Republic, June 9-13, 2025
Agenda Item: 15.3.2

## Slide 2
Scenarios and use cases from Rel-19 SA1
The use cases and requirements for integrated sensing and communications (ISAC) have been studied and specified in Rel-19 SA1. The use cases are categorized in 3 types of sensing services and 5 scenarios in TS 22.137.
  Sensing services: Object detection and tracking, environment monitoring and motion monitoring.
  Scenarios: UAV, Transportation, smart city, smart home and smart factory.
Object detection and tracking
Environment monitoring
Motion monitoring
Transportation
UAV
Smart city
Smart home
Smart factory

## Slide 3
Prioritized use case on UAV in Rel-20 RAN
It is observed that the service of low-altitude UAV detection has clear requirements for sensing and potential markets, and thus this case should be prioritized in Rel-20.
  Market：UAV detection and tracing is an essential part for low-altitude economy development from safety perspective. It is forecasted that the total market of low-altitude economy will reach ￥1000 billion in 2026 in China[1]. And in Europe the market of drone services could be worth €14.5 billion by 2030[2].
  Policy: Ministry of Industry and Information Technology of China issued the "Implementation Plan for Innovative Application of General-Purpose Aviation Equipment[3]". In the plan, the ability to reliably monitor UAV is needed for the development of low-altitude economy (see page 3 of [3]).
[1] Source: www.ndrc.gov.cn/wsdwhfz/202408/t20240821_1392498.html
[2] Source: transport.ec.europa.eu/news-events/news/drone-strategy-creating-large-scale-european-drone-market-2022-11-29_en
[3] Source:https://www.miit.gov.cn/zwgk/zcwj/wjfb/tz/art/2024/art_4ce8d09c15ee4fb1aefc3d5dfbbb6584.html
UAV intrusion detection
UAV trajectory tracing

## Slide 4
Standardization work for Sensing
Sensing
Communication
UE
RAN
Sensing signal transmission, echo signal reception and measurement
5GC
Third party
…
Computing target characteristics
(Position, Velocity, Size, etc.)
Sensing service application
RAN-CN
Interface
In SA#107, A new Rel-20 SA2 SID on Study on Stage 2 for Integrated Sensing and Communication was approved [1]
In ISAC, RAN/gNB is responsible of performing sensing and obtain sensing measurement, i.e. gNB-based mono-static sensing, and 5GC is responsible of handling sensing measurement and exposing sensing results to the third party.
The interaction between RAN and CN is necessary to support sensing service.
To enable sensing service in current network, necessary enhancement for RAN-CN interface is needed.
Sensing function
[1] SP-250401 New SID on Study on Stage 2 for Integrated Sensing and Communication

## Slide 5
Performance Evaluation by RAN1
  Sensing mode: gNB-based monostatic sensing mode.
  Resource multiplexing: allocating sensing and communication resources in time division multiplexing manner.
  Reusing some parameters for ISAC channel calibration for UAV.
Simulation Assumption |  | 
Carrier Frequency | 4.9GHz | 26GHz
Bandwidth | 100MHz | 400MHz
SCS | 30kHz | 120kHz
BS antenna config (M,N,P,Mg,Ng; Mp,Np) | (12,16,2,1,1;4,16) | (16,16,2,2,2;1,1)
Isolation from Tx to Rx | 70dB | 80dB
Target | UAV | 
ISD | 500m | 200m
Channel | R19 ISAC channel model | 
Sensing signal | NR ZC sequence with comb-2 mapping in frequency domain | 
The SA1 requirements in TS 22.137 for UAV |  |  |  |  | Simulation results | 
Sensing matric |  | Category 1 | Category 2 | Category 3 | 4.9GHz | 26GHz
Accuracy of positioning estimate | Horizontal [m] | 10 | 2 | 1 | 1.28 | 0.63
 | Vertical [m] | 10 | 5 | 1 | 1.31 | 0.42
Accuracy of velocity estimate | Horizontal [m/s] | N/A | 1 | 1 | 0.65 | 0.23
 | Vertical [m/s] | N/A | N/A | 1 | 0.7 | 0.1
Missed detection [%] |  | 5 | 0.1-5 | 2 | 3.6 | 4
False alarm [%] |  | 2 | 5 | 2 | 1.2 | 2
Observations:
gNB-based mono-static sensing can satisfy the SA1 requirements for UAV detection for certain categories.
RAN1 workload could be managed within 3 quarters, with exemplified simulation assumptions as above and reusing some parameters for ISAC channel calibration for UAV.

## Slide 6
RAN3 Impacts- Potential procedures and messages
 | Detailed impacts | Note
Sensing architecture | CP: NG-RAN connects with SF with or without AMF UP: whether the measurement data report is delivered over UP, e.g., via the GTP-U tunnel as a container, | Need cooperation with SA2
0 Sensing information exchange | Necessary sensing related info, e.g. sensing capability, location info, sensing area, authorization info, etc., are to be exchanged. | Some info, e.g. capability, location info, could also be based OAM configuration
1 Sensing measurement request | Define necessary info included in sensing measurement request message, e.g., sensing area, sensing requirement (e.g., measurement requirement, and reporting configuration (periodicity, or trigger event) etc.) | Need cooperation with SA2, e.g. on sensing area, point cloud definition
2 Sensing measurement | gNB-based mono-static sensing, no standard impacts | gNB internal implementation Performance evaluation by RAN1, if needed.
3 Sensing measurement report | Based on the request, to discuss the reporting mechanism: CP or UP results report, and discuss the sensing contents, e.g., Alt1: CP based Alt2: UP based | Need cooperation with SA2
RAN
1. Sensing measurement request
3b. Measurement data report
SF-C
SF-U
RAN
3a. Measurement data report
0. Sensing info exchange
2. Sensing measurement
Sensing function
* Whether step 1 and 3a between SF and RAN is via AMF, and whether step 3b is via UPF, need coordination with SA2.
5GC

## Slide 7
Proposals
Proposal 1: Support Rel-20 5G-A study and work for ISAC, focusing on UAV use case with gNB-based mono-static sensing mode.
  Proposal 2: The work on ISAC for Rel-20 5G-A is planned for a SI with duration of 9 months, followed by a RAN3-led WI.
  Proposal 3: Rel-20 5G-A ISAC study item includes the following objectives:
  Evaluate the performance of gNB-based monostatic sensing for UAV use case [RAN1]
    Channel model calibration assumptions for UAV in Rel-19 ISAC channel model SI is used as starting point.
    At least NR waveform/reference signals is used for evaluation.
    Additional details for sensing mechanism (Tx/Rx antenna setup within a TRP, adaptation in sensing waveform/signals) are left to gNB internal implementation and are up to company report.
  Study essential procedures and reporting quantities between RAN and CN for gNB-based monostatic sensing [RAN3, RAN1]
    Study the basic procedures and signaling exchange between RAN and CN [RAN3]
    Study the sensing reporting quantities to CN, i.e. one or more points with time and coordinate info [RAN3, RAN1]
    Note 1: definition in TS 23.032 could be considered as a starting point
    Note 2: coordination with SA2 is expected
    Note 3: no specification impact on inter-gNB coordination is expected