## Slide 1
3GPP TSG RAN Meeting #108 RP-251204
Prague, Czech Republic, June 9-13, 2025
Agenda item: 15.1.2
Source: vivo, CHTTL, Verizon, Spreadtrum, China Unicom, ETRI
Title: WF on open loop precoding for PUSCH in Rel-20 MIMO Phase 6
Document for: Discussion and Decision

## Slide 2: Proposal
For Rel-20 NR MIMO Phase 6
  For 2Tx non-coherent UE, support UL precoder cycling using non-coherent codebook subset with up to 2 PRGs.
    e.g. two precoders [1 0] and [0 1] are used for rank=1 transmission
    Applicable when the higher layer parameter txConfig in pusch-Config is set to 'codebook'
    Targeting non-coherent and non-ULFullPowerMode UE
    No enhancement on SRS, DMRS and PTRS

## Slide 3: Example
In the exemplary figure, number of PRBs scheduled for PUSCH is 12, size of each PRG is 6PRBs, where PRG#1 is mapped to antenna#1 and PRG#2 is mapped to antenna#2 (or vice versa) for rank=1 transmission.

## Slide 4: Appendix
Parameters | values
Wireless channel | 4GHz；TDL-C with 2Tx4Rx；30km/h Delay Spread=200ns
PUSCH | 30kHz；24PRB， 64QAM（CR=0.6）; 1layers DMRS: type1
Codebook | Scheme1: Rel-15 non-coherent codebook and power scaling (non full power) Scheme2: Rel16 FullPowerMode0 for 2 SRS ports Scheme3: UL precoder cycling using non-coherent codebook subset (i.e. [1 0], [0 1] only for rank=1) with up to 2 PRGs
Receiver | MMSE filter based channel estimation MMSE based equalizer
Observation:
Large performance gain can be observed with UL precoder cycling with 2 PRGs using 2 non-coherent precoders compared to Rel-15 power scaling (non full power)
Significant performance gain can be observed with UL precoder cycling with 2 PRGs using 2 non-coherent precoders compared to Rel-16 full power mode 0.
Potential Objective
  Frequency-selective open-loop precoder cycling for dynamic-grant PUSCH using the legacy UL 2TX non-coherent 1-layer precoders (for 1-layer transmission), assuming network-configured cycling pattern (via RRC) and UL PRG size, fully reusing the legacy PUSCH-DMRS, SRS, and PTRS resource design
    When configured, the number of PRGs is 2
    Applicable only for codebook-based UL transmission, targeting non-UL-full-power mode

## Slide 5: References
RP-241819, “WF on UL PRG for Rel-19 NR MIMO”, RAN#105
RP-250201, “Scope of MIMO phase 6 in 5G-A Rel-20” RAN#107