## Slide 1: Views on Rel-20 NG-RAN AI/ML Enhancements
RP-251347
Agenda : 15.3.1
RAN#108
Prague, Czech Republic
June 09-13,2025

## Slide 2
Background
In Release 18 AI/ML for NG-RAN WI, the following use cases were specified:
  AI/ML based Load Balancing
  AI/ML based Mobility Optimization
  AI/ML based Energy Savings
In Release 19 AI/ML for NG-RAN WI, the following new use cases and some leftovers from Rel-18 were addressed
  AI/ML based Network Slicing
  AI/ML based Coverage and Capacity Optimization
  Leftovers from Rel18 – AI/ML for NR-DC, AI/ML in Split gNB Architecture and Continuous MDT

## Slide 3
Background
In RAN#107, the initial scope for R20 AI/ML for NG-RAN endorsed as WF:
Rel-20 AI/ML for NG-RAN should be based on current 5G architecture and interfaces.
The objectives of AI/ML for NG-RAN in Rel-20 are listed below:
  Study the following new AI/ML based use cases and down-scope (1 or 2 use cases) in next plenary [RAN3]:
    QoE Optimization;
    Network energy saving
    Mobility (including Multiple-hop target node UE trajectory)
  Note: Other Leftovers depend on Rel-19 outcome, if any.
  Note: Coordination based on LSs with other working groups, when needed.
6 months for the Rel-20 Study Item on AI/ML for NG-RAN, followed by 12 months for the subsequent Work Item.
  For Release 20 AI/ML for NG-RAN WI, we propose the following new use cases.
  AI/ML based Mobility Optimization and LTM
  AI/ML based NES (not to discuss any leftover items again in R20)
  Proposal : Not to consider AI/ML based QoE for Rel 20, as there are no large scale commercial deployments of NR QoE.

## Slide 4
Objective | To optimize signaling overhead and efficient resource utilization of LTM mobility using AI/ML techniques for improved system performance |  | 
Motivation | Optimized selection of LTM candidate cells and radio resources AI/ML based prediction of candidate cell based on UE Trajectory Prediction, UE history, L3/L1 (Predicted) Measurement Reports, (predicted) resource status reports etc to - reduce reserving unnecessary resources in multiple candidate cells reduce RAN interface signaling reduce candidate cell rejection AI/ML based Optimized RACH and CG Resource Reservation for LTM in candidate cells | Optimized trigger for early synchronization and Cell Switch Command AI/ML based optimized early synchronization and cell switch by means of - Early TCI state activation TA validity time prediction Minimization of unnecessary UL TA pre-sync to candidate cells prediction of candidate cell SP-CSI-RS resource (de)activation for mobility management and CSI reporting. prediction of target cell for cell switch | Minimization of LTM reconfigurations/signaling overhead reduction Minimization of LTM reconfigurations and signaling using AI/ML techniques by LTM candidate cell configuration validity “optimization of subsequent cell switch” by configuring the right set of cells, that the UE may subsequently switch to would reduce the need for reconfiguration
Proposal | Study and enhance intra and inter gNB LTM (including conditional LTM) using AI/ML for both split and non-split gNB Architecture to improve signaling efficiency and improve LTM performance. |  | 
New Use Case – AI/ML based LTM

## Slide 5
Objective | To enhance and optimize Network Energy Savings with AI/ML |  |  | 
Motivation | Cell/beam (de)Activation AI/ML based prediction of Cell and beam (de)activation based on Resource status, mobility patterns etc and transfer of prediction over Xn and F1 interface for future RRM decisions like load balancing, mobility etc. | Cell DTX/DRX AI/ML based prediction of Cell DTX/DRX (de)activation based on resource status of the cell, energy consumption etc and transfer of prediction over Xn and F1 interface for future RRM decisions like load balancing, mobility etc. | NES handovers AI/ML based prediction of NES CHO trigger based on resource status, energy consumption etc and transfer of prediction over Xn and F1 interface to reduce CHO resource reservation and signaling overhead. | OD-SSB, OD-SIB1 AI/ML based prediction of duration a cell operates in OD-SIB1 and OD-SSB mode and transfer of the prediction over Xn and F1 interface to reduce signaling overhead and to enhance future RRM decisions on Mobility, CA etc
Proposal | a) Study and enhance AI/ML based Network Energy Savings for both split and non-split gNB. b) Do not consider leftover R19 energy prediction discussion in R20 |  |  | 
Enhancement – AI/ML based Network Energy Savings

## Slide 6
Summary Proposals
Mobility Use Case :
Proposal 1: Study NG-RAN AI/ML based intra and inter gNB LTM (including conditional LTM) for both split and non-split gNB Architecture to minimize signaling overhead and improve performance
  Candidate Cell selection and Radio Resource Reservation in candidate cells (i.e., RACH and CG Resources)
  Early Sync, SP-CSI-RS Resource (de)-activation, cell switch
  Minimization of candidate cell re-configuration based on validity and optimized subsequent cell switch(s).
Note: There is no overlap with RAN2 led AI/ML Mobility WI
NES Use Case:
Proposal 2a: Study and enhance AI/ML based Network Energy Savings for both split and non-split gNB
  Cell/beam (de)Activation, Cell DTX/DRX, NES handovers, OD-SSB and OD-SIB1 scenarios
Proposal 2b: Do not consider leftover R19 energy prediction with fine granularity discussion in R20
QoE Use Case:
Proposal 3: Do not consider AI/ML based QoE for Rel 20, as there are no large scale commercial deployments of NR QoE