## Slide 1: Additional requirements for 4.9GHz new band for US
Agenda Item: 9.1.5
Source: Fujitsu, FirstNet
Document for: Information
3GPP TSG RAN Meeting #108 RP-251355 Prague, Czech Republic, June 9-13, 2025

## Slide 2: Background for 4.9GHz new band for US
Justification
  On 22 October, 2024, the FCC released Amendment of Part 90 of the Commission’s Rules, WP Docket No. 07-100, Eighth Report and Order taking steps to ensuring that the 4940–4990 MHz band (4.9 GHz band) is efficiently and intensely utilized for nationwide public safety coverage in the US. The FCC previously provided a framework to coordinate operations in the 4.9 GHz band and to facilitate the integration of the latest commercially available technologies, including 5G.
  To allow for public safety operation in line with the framework identified by the FCC within the frequency range, 4940-4990 MHz, within 5G NR, a new NR TDD operating band needs to be defined as part of this work item.
The related WI has already proposed at RAN#107 in March (RP-250131)
There are slight differences in the RF requirements for 3GPP spec and CFR Title 47. The following slide will explain these differences.

## Slide 3: Additional requirements for US 4.9GHz (UE spurious emission mask)
3GPP (38.101-1 6.5.2.2)
CFR Title 47 (Part 90.210(m))
  For high power transmitters (greater that 20 dBm) operating in the 4940-4990 MHz frequency band, the power spectral density of the emissions must be attenuated below the output power of the transmitter as follows:
    On any frequency removed from the assigned frequency between 0-45% of the authorized bandwidth (BW): 0 dB.
    On any frequency removed from the assigned frequency between 45-50% of the authorized bandwidth: 568 log (% of (BW)/45) dB.
    On any frequency removed from the assigned frequency between 50-55% of the authorized bandwidth: 26 + 145 log (% of BW/50) dB.
    On any frequency removed from the assigned frequency between 55-100% of the authorized bandwidth: 32 + 31 log (% of (BW)/55) dB.
    On any frequency removed from the assigned frequency between 100-150% of the authorized bandwidth: 40 + 57 log (% of (BW)/100) dB.
    On any frequency removed from the assigned frequency between above 150% of the authorized bandwidth: 50 dB or 55 + 10 log (P) dB, whichever is the lesser attenuation.
    The zero dB reference is measured relative to the highest average power of the fundamental emission measured across the designated channel bandwidth using a resolution bandwidth of at least one percent of the occupied bandwidth of the fundamental emission and a video bandwidth of 30 kHz. The power spectral density is the power measured within the resolution bandwidth of the measurement device divided by the resolution bandwidth of the measurement device. Emission levels are also based on the use of measurement instrumentation employing a resolution bandwidth of at least one percent of the occupied bandwidth.

## Slide 4: Additional requirements for US 4.9GHz (Power limits)
CFR Title 47 (Part 90.1215)
  Except as provided in paragraph (f) of this section, the transmitting power of stations operating in the 4940-4990 MHz band must not exceed the maximum limits in this section.
    (a)
      …
      (2) High power devices are also limited to a peak power spectral density of 21 dBm per one MHz. High power devices using channel bandwidths other than those listed above are permitted; however, they are limited to peak power spectral density of 21 dBm/MHz. If transmitting antennas of directional gain greater than 9 dBi are used, both the maximum conducted output power and the peak power spectral density should be reduced by the amount in decibels that the directional gain of the antenna exceeds 9 dBi. However, high power point-to-point and point-to-multipoint operations (both fixed and temporary-fixed rapid deployment) may employ transmitting antennas with directional gain up to 26 dBi without any corresponding reduction in the maximum conducted output power or spectral density. Corresponding reduction in the maximum conducted output power and peak power spectral density should be the amount in decibels that the directional gain of the antenna exceeds 26 dBi.

## Slide 5
Thank you