## Slide 1: Support of GEO satellite voice call
3GPP TSG RAN Meeting #108 RP-251384
Prague, Czech Republic, June 9-13, 2025
Agenda: 15.2.2
Source: CMCC

## Slide 2: Voice over IoT-NTN
Background
GEO provides a unique advantage in terms of global coverage:
  In some cases (e.g. without TN coverage or the conventional TN communication infrastructure is destroyed), it is urgent to establish real-time interaction in a short time period
  Therefore to support real-time voice communication over NTN is essential.
In SA, GEO voice is agreed as WT#1 in SP-250400, where “both CP and UP based NB IoT NTN solutions will be studied, checkpoint will be set before the normative work to align with RAN scope”.
  SA2 is expected to reach a conclusion on this matter by SA2#172 in November 2025.SA2 has also output the TR 23.700-19 including IMS voice call over NB-IoT NTN via GEO satellite connecting to EPC, and in SA2 #169 meeting, they discussed and approved some solutions.
  SA1 has defined service requirements (TR 22.887) for IMS voice call using GEO satellite as following:
In RAN#107, IMS voice over GEO in IoT-NTN was captured as potential R20 topic in chair summary in RP-250812. study phase and check point are needed to down-select between CP or UP.
Scenario | UE type | Transmission data rate |  | Call setup time NOTE 1
IMS voice call using GEO | Handheld | UL | DL | [4-30] s NOTE 2
 |  | [1-3] kbit/s | [1-3] kbit/s | 
NOTE 1: call set up time refers to [4]; NOTE 2: the lower bound of 4s originated from the experience in terrestrial VoNR/VoLTE, while the upper bound of the 30s is derived based on the user’s patience suggestions (30s) in [13]; |  |  |  | 

## Slide 3: Voice over IoT-NTN
Motivation
Low data rate:The current IoT-NTN data rate can reach 1-2 kbps, however, to support voice call, a minimum of 4.75 kbps is required according to the 3GPP standards.
Long Propagation delay: Regarding the VoLTE voice, one cycle of transmission and reception is within 20ms, but due to the limited bandwidth and half-duplex scheduling of IoT-NTN, it is challenging to complete one transmission and reception within 20ms.
Lack of IMS voice function: Exisiting IoT-NTN does not support IMS voice services.
Current RoHC for voice cannot be supported in NB IoT device.

## Slide 4: Voice over IoT-NTN
Solutions
  Support of UP solution for signaling and data transmission of voice respectively
    To support CP solution, maybe new RB is needed to be introduced due to that only SRB1bis could be used for NAS message transmission per the current specification. Then RB handling needs to further discuss. Further, CP solution also has security issue.
    And if UP solution is adopted, legacy transmission solution based on DRB could be reused, and there is no security issue either.
    It could be seen that UP solution has smaller specification impact compared to CP solution. Therefore, it is better to support UP solution for voice call over GEO.
Support SPS
  For voice service, the packet size is fixed and the arrival interval meets certain rules of real-time services (e.g. a typical voice service cycle is 20ms). To address this feature, SPS is introduced in LTE, which transmits new data according to the pre-configured resources on the specified subframe, but in order to reduce the latency, dynamic scheduling is still utilized during retransmission.
  For voice over IoT-NTN, SPS could be supported.

## Slide 5: Voice over IoT-NTN
Solution
Support ROHC
  For NB-IoT, to improve bandwidth utilization is important, therefore, to support ROHC for voice packets could be discussed. And the existing ROHC mechanism for VoLTE could be considered.
Figure 1. An example ROHC for VoLTE
Objective
RAN
  Support of UP solution for signaling and data transmission of voice respectively
  Introduce of SPS in IoT-NTN for voice service
  Support of RoHC Profile0x0001 for PDCP header compression (RTP+UDP+IP for VOLTE packet)

## Slide 6: Thanks!