## Slide 1
0
Views on RF Topics for Rel-20
3GPP TSG RAN Meeting #108 RP-251387
Prague, Czech Republic, June 9-13, 2025
Agenda Item: 15.4.2
Source: CMCC
Document for: Discussion

## Slide 2
UE RF centric evolution
FR1 HPUE enhancement (PC2/PC1.5/PC1) for single carrier and EN-DC/NR-CA
  This item receives common interest, but needs discussion on the feasibility of some use cases and also need down-selection.
Power enhancement with relaxed UE Tx EVM and/or uplink throughput improvement with advanced BS receiver (AI based receiver is not precluded as the starting point)
  TBD on objectives should include Tx EVM relaxation, uplink throughput improvement, or both.
  Study phase is needed if it is considered and FFS whether to treat it in UE RF or demod package
  There are still concern on whether Tx EVM should be part of Rel-20 package for 5G-A.
Band/band combination requirements simplification and MSD simplification/optimization
  TBD on whether MSD work is for PC3 and/or HPUE as Rel-19 leftover work.
Tx requirements enhancement for U6G
Power classes framework
Optimize MPR/A-MPR
Requirement enhancement to support coherent UL MIMO
UL Tx switching enhancement
256QAM evolution
SRS enhancement
SL-U enhancement
MPR reduction by leveraging asymmetric ACLR
General consideration
In RAN#107, overall 12 topics were discussed for RAN4 Rel-20 UE RF. Even for each topics, there are multiple proposals. Considering the available TU for Rel-20 5G-Advanced is limited due to parallel tracks of 5G-Advanced and 6G. It is proposed to consider the features that can be implemented and commercialized in 5G-Advanced, meanwhile take the overall workload into account.

## Slide 3
FR1 UE HPUE enhancement
Motivation
For TN, 1Tx FDD PC2 was introduced in Rel-17. It is possible to supporting FDD PC1.5 with 2Tx by commercial UE which provide throughput gain by MIMO
For TN, 3Tx UL MIMO was introduced in Rel-19, it is possible to supporting PC1.5 3Tx for FDD and TDD
For TN, 4Tx(4*26dBm) UL for FWA can be supported
Consideration for Rel-20
Specify requirements for PC1.5/PC1 UE for TN single CC in NR FR1
  PC1 with 4Tx UL for FWA
  PC1.5 FDD with 2Tx
  PC1.5 TDD and FDD with 3Tx

## Slide 4
Power enhancement with relaxed UE Tx EVM and advanced BS receiver
Motivation
EVM is the key factor that impact MPR/A-MPR requirements for higher modulation orders. Relaxed EVM will help to enhance UL throughput with better MPR performance especially for dense urban area
Consideration for Rel-20
Specify RF requirements to support relaxed Tx EVM requirement for 64QAM and 256QAM
Specify BS performance requirements to verify BS capability under relaxed EVM from UE for 64QAM and 256QAM.

## Slide 5
NTN HPUE enhancement
Motivation
For IoT-NTN, PC1 HPUE has been introduced in Rel-19, it is possible to support higher power class, e.g. 33dBm
  According to our link budget analysis, when the NB-IoT based NTN UE transmits at 26 dBm, the system has only a 1 dB margin on the uplink, which is insufficient to meet the communication requirements for most scenarios.
Consideration for Rel-20
Specify requirements for higher power class for IoT-NTN UE, e.g. 33dBm

## Slide 6
THANK YOU！