## Slide 1
0
Views on RRM/Demod Topics for Rel-20
3GPP TSG RAN Meeting #108 RP-251388
Prague, Czech Republic, June 9-13, 2025
Agenda Item: 15.4.3
Source: CMCC
Document for: Discussion

## Slide 2
According to discussion in RAN#107, following list of high level candidate objectives are used as the starting point for RRM enhancement in Rel-20
  RLM/BFD relaxation for RedCap UE
  Fast SCell activation [and PSCell addition] enhancement
  Uplink only SCell (NES SSB-less SCell enhancement)
  FR2 multi-Tx and multi-Rx
  Enhanced RRM requirements for NES
  Enhanced RedCap with LTM
  R18 leftover on LTM RRM
  Interruption at NR SRS antenna port switching
  Parallel measurement
  Inter-frequency measurement enhancement for LTM
  On-demand deactivated SCell measurement
  A-TRS based RRM enhancement
  Dynamic RTD/TTD status update
  AL/ML beam prediction testing
  Handover interruption minimization
  Interruption-free DCI operation
  Extend OD-SSB to PSCell in NR-DC
The available TU for Rel-20 5G-Advanced is limited due to parallel tracks of 5G-Advanced and 6G. It is proposed to take commercial needs and overall workload into account to discuss Rel-20 RRM scope.
General consideration

## Slide 3
RLM/BFD relaxation for RedCap UE
Motivation
The relaxed RLM/BFD requirements are specified for non-RedCap UEs in Rel-17
RLM/BFD relaxation is beneficial for power saving, which is important for RedCap UEs
Consideration for Rel-20
It is proposed to specify RRM requirements to support RLM/BFD relaxation for RedCap UEs
  For 2Rx RedCap UEs, the Rel-17 relaxed RLM/BFD requirements are reused
  For 1Rx RedCap UEs, the Rel-17 relaxed RLM/BFD requirements can be used as baseline, e.g. to check whether relaxation criteria and scaling factor introduced in Rel-17 can be reused

## Slide 4
Interruption at NR SRS antenna port switching
Motivation
The legacy interruption requirements at SRS antenna port switching are applied with the condition that SRS resource(s) is only configured within the last 6 symbols of a slot. However, it is already supported that the start of SRS can be any symbol within a slot, which means some scenarios are not covered by existing interruption requirements
  This issue is also observed in Rel-19 MIMO WI about 6Rx capable UE
Consideration for Rel-20
It is proposed to specify interruption requirements at NR SRS antenna port switching to cover the case that SRS resource(s) is not within the last 6 symbols of a slot
  For the cases that SRS resource(s) is not within the last 6 symbols of a slot, legacy interruption requirements are reused

## Slide 5
Parallel measurement
Motivation
For concurrent gap, if two gaps are collide, UE is only required to perform measurement in one of the gaps
From deployment point of view, parallel measurements upon MG collision could help to reduce the impact on throughput while maintaining the benefit of concurrent MGs. It is benificial to consider parallel measurement upon gap collision
Consideration for Rel-20
It is proposed to specify RRM requirements to support parallel measurements upon MG collision

## Slide 6
Demod: Spatial Channel model
Motivation
Rel-19 FS_NR_demod_SCM study the spatial channel model methodology and the test feasibily of SCM based UE demodulation and CSI reporting requirements in SU-MIMO case
6G technologies will also require a trusted and verified spatial channel model to do the performance assessment and to define the requirements
Consideration for Rel-20
Based on the outcome from Rel-19 FS_NR_demod_SCM SI, introduce the SCM based requirements in both SU-MIMO and MU-MIMO scenario.
  advanced receiver can be considered in interference scenario

## Slide 7
THANK YOU！