## Slide 1: Consideration on Rel-20 Mobility
3GPP TSG RAN Meeting #108 RP-251432
Prague, Czech Republic, June 9-13, 2025
Agenda Item: 15.2.3
Source: Lenovo
Document for: Discussion

## Slide 2: Summary for Rel-20 Mobility (RP-250812)
The following objectives are considered as baseline for Rel-20
Specify LTM SCell improvements for further reducing interruption delays
  SCell activation
    Specify the necessary configuration and UE procedures for NW triggering of LTM SCell activation with LTM cell switch [RAN2, RAN3].
    Evaluate and specify as necessary the needed RAN4 requirements for this [RAN4].
NOTE: Reuse the candidate cell LTM measurement and reporting procedures where possible for the SCell improvements
NOTE: This objective is NOT applicable to non-co-located CA and is NOT applicable to C-LTM
NOTE: This objective is applicable to MCG and SCG
Dynamic L1 measurement and reporting configuration change
  Specify the necessary configuration and procedures for MAC CE based configuration selection among prior provided RRC configurations of UE L1 measurement and reporting LTM configuration [RAN2]
  Evaluate and specify as necessary the needed RAN4 requirements for this [RAN4]. ????
NOTE 1: This sub-objective is applicable to C-LTM as well.
NOTE 2: For this objective, we strive to avoid RAN1 impact (including reporting)
NOTE 3: RAN1/RAN3/RAN4(?) involvement is based on LS if necessary
No further RAN2 objectives are considered for Rel-20

## Slide 3: Mobility Enhancement
  SCell activation:
    According to the summary (see RP-250812), LTM SCell will be improved for further reducing interruption delays. Network triggering of LTM SCell activation with LTM cell switch will be specified. Furthermore, this objective is applicable to MCG and SCG.
    In Rel-18, we support Intra-CU MCG/SCG LTM. And Inter-CU MCG/SCG LTM are supported in Rel-19. We think that this objective for SCell activation is applicable to Intra-CU/Inter-CU MCG and Intra-CU/Inter-CU SCG. Therefore, we propose to clarify this objective for SCell activation is applicable to Intra-CU/Inter-CU MCG and Intra-CU/Inter-CU SCG.
Proposal 1: The objective for SCell activation is applicable to Intra-CU/Inter-CU MCG and Intra-CU/Inter-CU SCG.

## Slide 4: Mobility Enhancement
  SCell activation:
    If SCell index is included in LTM cell switch command, it is natural that MCG SCell can be activated during LTM MCG cell switch. And the SCG SCell can be activated during LTM SCG cell switch. It is not clear whether SCG SCell can be activated during LTM MCG cell switch.
    In Rel-19 Inter-CU MCG LTM, Inter-CU MCG LTM with SCG addition and SCG change without SN change is supported. Regarding the deactivated SCell in SCG, it is possible that SCG SCell can be activated for LTM Inter-CU MCG cell switch. In Rel-18 Intra-CU MCG LTM, MCG LTM with SCG release and MCG LTM without SCG change are supported. We don’t see any technique issue to support SCG SCell activation during LTM Intra-CU MCG cell switch. Therefore, we propose
Proposal 2: It is suggested to support that network triggering of SCG SCell activation with LTM MCG cell switch.

## Slide 5: thanks