## Slide 1
Sony’s View on RAN4 Rel-20 5G-A
Sony
3GPP TSG RAN Meeting #108
Prague, Czech Republic, June 9-13, 2025
RP-251529
Agenda item:15.4.1

## Slide 2: Overall thinking on RAN4 Rel-20 work
RAN4 can follow the same TU split as other WGs with respect to 5G vs. 6G in Rel-20
  The RAN4-led Rel-20 5G-A work needs to be carefully planned with consideration of the impact from other WGs as well as from the maintenance work.
    Rel-20 5G-A enhancements shall focus on the missing features for 5G NR that would enable new market segments and deployments.
    Enhancements that require extensive studies and may result in major changes in implementations should better be considered as part of the 6G track instead of the 5G-A track.
  RAN4 may allocate more TUs for 5G-A at the beginning of Rel-20, but it is expected the TU allocation for 6G to gradually increase over time.

## Slide 3: RAN4-led WIs on Rel-20 5G-A
(e)Redcap requires further complexity reduction to enable the use cases related to the low-end IoT market, while at the same time aim to bridge the transition from 4G IoT to 6G IoT. The following topics are considered as high priority for Rel-20:
  Support 3MHz CBW for (e)Redcap device, including both TN and NTN.
  Specify the mechanism(s) to enable single SKU designs (SAW-less front end) for HD-FDD eRedcap with 3MHz and 5MHz bandwidth.
  Specify relaxed RLM and BFD for (e)Redcap devices.
  Motivation and details on the proposals above can be found in the contribution RP-251530.
Based on the discussions during RAN#107 (RP-250817), at least the following topics can also be considered in Rel-20 as interest was expressed by industries:
  UE RF: FR1 HPUE enhancement (PC2/PC1.5/PC1) for single carrier and EN-DC/NR-CA, focus on FWA.
  OTA: Enhance test method for CA and wearable devices.
  Demod: Pending on the outcome of SI, if SCM based requirements would be specified in Rel-20, focus on SU-MIMO only.
  Cross area: Support 6MHz for selected frequency bands.
Prioritized Topics
Additional Topics