## Slide 1
(e)Redcap enhancement in Rel-20
Sony
3GPP TSG RAN Meeting #108
Prague, Czech Republic, June 9-13, 2025
RP-251530
Agenda item:15.4.4

## Slide 2: Background & Proposal
Redcap was specified in Rel-17 with the aim to reduce the complexity compared to legacy NR devices and target use cases like wearable devices, surveillance cameras etc.
In Rel-18, further simplification was done enabled the eRedcap devices to support use cases towards low-end IoT applications, although further complexity reduction is still required to fully meet the market demand., e.g., utility, low-end wearable devices.
Based on the discussion In RAN #107, it was summarized in RP-250817 that the following objective can be taken as a starting point for further discussions for Rel-20.
In this contribution, we propose the 3 objectives below on (e)Redcap enhancement as part of Rel-20 RAN4 work:
  Specify the 3MHz CBW for (e)Redcap device, including both TN and NTN.
  Specify the corresponding mechanism(s) to enable single SKU designs for HD-FDD eRedcap for 3MHz and 5MHz CBW.
    The public safety band protection, and that the corresponding spurious emission for UE co-existence level shall not be relaxed.
  Specify relaxed RLM and BFD for (e)Redcap devices.
  Detail motivation of each objective can be found in the following slides.
Background
Proposal

## Slide 3: Motivation on 3MHz CBW support for (e)Redcap
3MHz channel BW was specified for non-Redcap NR device in Rel-18, while the demand of 3MHz for (e)Redcap has also been raised in Rel-19 for n106 for utility applications [1].
Industry is seeking a low cost and low complexity replacement for existing cellular meters in Band n106 - 3 MHz networks using (e)RedCap enabled electric meters.
For utility applications and generally low-end IoT applications, single Rx and/or also HD-FDD can be a natural fit due to the reduced cost and power consumption. Therefore, it will be a great benefit for (e)Redcap devices if 3MHz CBW can be supported for (e)Redcap in Rel-20.
In addition, 3MHz CBW is under specification for NR NTN in Rel-19. Based on the demand from NTN operators, the 3MHz CBW can be specified in Rel-20 for Redcap NTN as well.
Specify the 3MHz CBW for (e)Redcap device, including both TN and NTN.
Motivation
Objectives

## Slide 4: Motivation on Single SKU design on eRedcap
The HD–FDD design of eRedcap offers the opportunity for SAW-less implementation to enable a single SKU (stock-keeping unit) design for global operation:
  the SAW-less design with single SKU improves the power efficiency of the RF front end.
  streamlines production, lowers inventory costs and achieves economies of scale through higher production volumes.
  facilitates further network deployments and ecosystem growth and enables the eRedcap device towards low-end IoT applications.
Currently, the single SKU implementation of eRedcap is very challenging in order to meet all RF requirements.
The industry's recognition of its importance has been demonstrated through a jointly submitted contribution [2].
Power efficiency improvement
Footprint size reduction
Specify the corresponding mechanism(s) to enable single SKU designs for HD-FDD eRedcap for 3MHz and 5MHz CBW.
  the public safety band protection, and that the corresponding spurious emission for UE co-existence level shall not be relaxed.
Motivation
Objectives

## Slide 5: Motivation on Relaxed RLM and BFD for (e)RedCap UEs
In Rel-17 the relaxed RLM and BFD was specified for non-Redcap UE which can reduce the power consumption in low mobility use cases and/or in good channel conditions [3].
Such a power consumption reduction mechanism will be more critical for IoT type of use cases, for example, utility applications, due to its stationary deployment and the low data rate use cases.
Therefore, it is proposed that to specify relaxed RLM and BFD for (e)Redcap devices in Rel-20.
MO without RLM/BFD measurement relaxation
MO with RLM/BFD measurement relaxation
Specify relaxed RLM and BFD for (e)Redcap devices.
Motivation
Objectives

## Slide 6: References
[1] RP-242812 Motivation for new WI on less than 5 Mhz (e)RedCap Support in Rel-19 Anterix
[2] RP-243007 Motivation on further complexity reduction for eRedcap devices enabling single SKU design (SAW-less) Sony, Nordic Semiconductor ASA, Semtech, Sequans Communications, vivo, OPPO, Itron
[3] RP-242982 Proposal for RRM objective on relaxed RLM/BFD for Redcap Ericsson, MediaTek inc., vivo