## Slide 1
Proposals for RAN-led 6G Study Items
RP-251617
3GPP TSG RAN#108
Prague, Czech Republic, June 9-13, 2025
ST Engineering iDirect – Public Information

## Slide 2: Outline
Introduction
PHY layer security
GNSS independence
Non-linear distortion
FEC error floors

## Slide 3
Introduction
Usage scenarios for IMT-2030 include
Ubiquitous connectivity
Hyper-reliable communication
Design principles include
Connecting the unconnected
Security and resiliency
In this contribution, we present four proposals to enhance the radio access technology for 6G.
Note: More details and references are provided in the docx.
Usage scenarios and design principles for IMT-2030 from ITU-R M.2160

## Slide 4
Physical layer security
Security in 5G systems
Encryption and authentication, e.g., TS 33.501
Current security issues
  5G broadcast and control channels are narrowband and can be easily jammed or eavesdropped
  Broadcasted DCI with DL/UL grants allows creating maps of network activity for different UEs in the network
Security in 6G
During the 3GPP Workshop on 6G, numerous companies advocated for enhanced encryption schemes
We propose to add a requirement to have (additional) channels with increased PHY layer security, e.g.,
  Make the 6G broadcast and control channels more resilient against jamming and eavesdropping
  Enable an option to hide network activity, and if possible, the network traffic

## Slide 5
GNSS independence
5G NTN systems (Rel-17 to Rel-19)
UE requires a GNSS receiver used for pre-compensation of timing and frequency offsets (for logon, and in connected mode)
GNSS can be easily jammed or spoofed, making the 5G NTN system unavailable
Proposed requirements on GNSS-free operation
The solution should work with LEO and GEO satellites
The solution shall not use the position of the UE or satellite
Rel-20 Study Item for 5G Advanced
Study item is being defined for GNSS resilient operation
For 6G: GNSS-free system that does not rely on the UE’s location at all
This might require waveform changes to PRACH
GPS jamming (from RP-250574)

## Slide 6
Non-linear distortion detection
NTN terminal architecture
PA in outdoor unit, margin on TX power estimations (vs TN UE with integrated PA)
TX power for GEO is critical to close the link budget
Linear modulation requires a high PA backoff to avoid non-linear distortion
5G NTN challenges
Spectral regrowth caused by PA’s non-linear distortion
Challenging TX power estimate at VSAT requires a margin on PHR
TX power control using backoff and calibrations
Proposal
Addition of a signaling waveform that allows the gNB to estimate the distortion caused by the non-linearity of the VSAT’s PA
PA
Filter
Up-convertor
BUC
Modem

## Slide 7
Improved FEC error floors
Current block error rate (BLER) requirements
10-2 for voice applications
10-5 for ultra-reliable communication
Adaptive modulation and coding (AMC)
Based on HARQ retransmission
Based on channel quality indicator, e.g., SNR
Quasi error-free mode for satellite communication
Requires a BLER of 10-7 in low-SNR scenarios
Base graph 5G NR LDPC Source: Nguyen, et al., “Efficient QC-LDPC Encoder for 5G New Radio,” Electronics, 2019

## Slide 8
Thank you!
Brecht DE BEELDE, PhD
Satcom technology and standardization engineer
bdebeelde@idirect.net
www.idirect.net