## Slide 1
Huawei, HiSilicon
Rel-20 MIMO Scope
3GPP TSG RAN#108 RP-251647
Prague, Czech, June 09-13, 2025
Agenda Item: 15.1.2

## Slide 2
General views on MIMO in Rel-20
Massive MIMO is widely deployment in 5G/5G-A, which is the key feature for obtaining high spectrum efficiency in 5G-A system. In Rel-20, MIMO enhancements are still required for commercial deployment, especially for the following two cases:
For TDD massive MIMO, the challenges of SRS coverage/ SRS channel estimation accuracy in the deployment need to be handled,
  Specify multiple SRS positions pattern in a frequency hop to enable channel interpolation, and specify Cross-slot SRS configuration between U and S slot to enable contiguous SRS symbols for repetition.
For Sing/Multi-TRP, SRS inter-cell interference and coverage are the key issues, which need to be addressed, especially for cell edge UEs,
  Specify long term channel covariance feedback to enhance SRS coverage and the capability of interference mitigation.

## Slide 3
Issue-1: SRS issues in TDD massive MIMO
TDD massive MIMO is the main deployment in 5G/5G-A, where the performance is highly relied on the accuracy of SRS-based channel acquisition. However, in current spec, the challenges include coverage/accuracy for SRS, especially for the cell edge UEs, and also UL transmission capacity/efficiency. Specifically, in current spec, there are following key issues,
To enhance the UE experience especially for cee UEs, the above key issues need to be addressed in Rel-20.
For current hopping pattern, SRS is repeated in the same frequency positions in a hop, so that only extra-polation for partial SRS can be used. The channel estimation performance of SRS is limited.
SRS is only transmitted in partial bandwidth, e.g., 4 or 6RBs
Frequency
Hopping period
Time
Frequency hop
Extra-polation only
SRS currently is configurated in last 2 symbols of S slot. The other SRS symbols only can be in the last symbols in U slot, which is non-contiguous with SRS symbols in S slot. So, for cell edge UEs, SRS repetition will be restricted no more than 2, i.e., coverage will be limited.
If SRS repetition is only configured on last symbols in U slot, then the last two symbols of S slot will be wasted, i.e., UL capacity losing.
SRS
…
SRS
DMRS
SRS
SRS
S slot
SRS
SRS
U slot
PUSCH (10 symbols)
SRS#0 (2 symbols)
SRS#1 (4 symbols)
//
In Current Spec
In Current Spec
1. SRS interpolation is not available
2. SRS repetition can not across S and U slot

## Slide 4
To address the key issues as mentioned, following SRS enhancements are proposed for Rel-20. For partial sounding with frequency hopping, introduce multi-starting SRS positions within a frequency hop to enable SRS interpolation. And, for SRS repetition, introduce cross S and U slots SRS resource to enable cross slot SRS repetition.
Enable channel interpolation in the Partial Sounding
  Spec impact: to introduce SRS repetition pattern with multi-frequency domain starting positions for SRS repetition in each SRS frequency hop for partial sounding to enable channel interpolation
Multi- frequency-domain starting positions in a Hop
Frequency equal-spaced SRS repetition pattern in a hop
Proposal for SRS Enhancements in TDD Massive MIMO
Hopping period
Frequency
Time
Proposal 1: Specify SRS enhancements in Rel-20:
      Multiple frequency-domain starting positions for SRS repetition symbols within each SRS frequency hop for RB-level partial frequency sounding.
      Cross-slot SRS between one U slot and one adjacent S slot within a single SRS resource set.
1.28x
SRS contiguous sparse hopping
1x
64T4R
7*3 RCE 80ms
1.36x
SRS contiguous sparse hopping
1x
64T4R
7*3 RCE 80ms
Cell average
Cell edge
Time
Cross-slot SRS resource
Cross-slot resource for SRS repetition
SRS
…
SRS
SRS
SRS
SRS
SRS
DMRS
S slot
U slot
PUSCH (10 symbols)
//
Enabling cross-slot (S and U slots) SRS resource repetition configuration:
  Spec impacts: Cross slot SRS resource repetition configuration: enable SRS configuration in the tail of S slot and head of U slot, ensures efficient utilization of uplink resources and avoid phase/power shifting
1x
1.18x
1.3x
2x repetition
4x repetitions
8x repetitions
1.25x
6x repetitions

## Slide 5
Issue-2: SRS Interference and coverage issue in S-/M-TRP Network
  For TDD massive MIMO, the performance rely on SRS channel estimation. However, SRS channel estimation is still with some challenge, especially for the cell edge UEs, due to the coverage issue and inter-cell SRS interference. To address coverage and inter-cell interference is the key to enhance the users’ experience performance for TDD massive MIMO system.
  The solution to mitigate inter-cell interference is UE feedback the long term channel covariance (including RHH and RUU) to Network, where RHH is the long term channel covariance for the required signal space for SRS channel estimation and RUU is the long term channel covariance from interfering UEs for interference. gNB can use the long term channel covariance information to filter out the interference and noise.
SRS Inter-cell interference for multi-TRP
Required SRS
Remote UE
Interference
UE
serving cell
Ruu
SRS Inter-cell interference for single-TRP
Rhh
UE

## Slide 6
  Scenario set up:
    5TRPs, 43 UEs distributed as the figure.
    Each TRP is with 64Tx, and UE with 4Rx
    3.7GHz and 30KHz is assumed
    Distance ~500m
Single-TRP
m-TRP
Simulation results with real channels:

## Slide 7
The procedure for Long term channel covariance feedback
  gNB use long term channel covariance matrix （and ） to filter out interference and noise (e.g., using MMSE/LMMSE: )) outside the signal space to assist SRS channel estimation, while the channel covariance matrix is based on DL signal measurement and UE feedback to guarantee the accuracy.
channel energy
Signal space
Interference + noise
Signal space
Filtered out part
UE calculates the long term channel covariance RHH
  where channel covariance could be calculated and average across time.
UE quantize the channel covariance: using DFT projection to matrix s, and select L largest coefficients to report, e.g.,
  is the DFT matrix
gNB recover channel covariance = , and use it to filter out interference and noise with MMSE/LMMSE channel estimation
UE feedback the long term channel covariance, as procedure:
  Note: = is the covariance of inter-cell interference, where the channel covariance matrix RHH from inter-cell UE 𝑖

## Slide 8
Proposal for Long Term Covariance feedback
Proposal 2: Specify long term channel covariance feedback in R20, specifically,
    Specify procedure for covariance matrix calculation, i.e. averaging in frequency and time domain [RAN4 or RAN1]
      is with dimension Nt/2*Nt/2, where Nt is number of antennas at gNB
      Example of time domain averaging: 320ms
    Specify procedure for covariance matrix quantization, i.e. projection base, reporting contents (how many values to report and number of bits per value) [RAN1]
      Example of projection base: where , N1，N2 is antennas in horizontal and vertical in a polarization
      Example of reporting contents: largest Nt/4 elements (real numbers), where each element is quantized to 4 bits
    Specify procedures for covariance matrix reporting, i.e. standalone CSI reporting for coefficients and bitmap of element position [RAN1]
      Example: Nt/4 * 4 + Nt/2=3/2 Nt bits per 320ms for per TRP
  No new codebook design, Reuse legacy CSI-RS

## Slide 9
During RAN#106 and RAN#107 discussion, for MIMO topic, there are a lot proposals. After checking with the details, we are supportive for the following proposed enhancements as well.
Early SRS/CSI/CSI-RS triggering for UE transitioning from IDLE/INACTIVE to CONNECTED mode and SCell activation in CONNECTED mode, while it is beneficial for latency reduction for Random access and Scell activation.
Reduce CSI-RS overhead, especially for 48, 64, and 128 CSI-RS ports, and we also supportive to reduce CSI-RS overhead for 8,16,32 port CSI-RS when it is used for beamformed CSI-RS cases.
The leftover issues for asymmetric DL sTRP/UL mTRP, i.e., spatial filter/pathloss offset configuration and PRACH beam indication.
Views on other proposals
Proposal 3: We are additionally positive for following proposals in Rel-20:
      Early CSI-RS/SRS/CSI triggering.
      CSI-RS overhead reduction.
      Leftover issues for asymmetric DL sTRP/UL mTRP

## Slide 10
Based on the above discussion, we have following proposals for Rel-20 MIMO scope:
Conclusions
Proposal 1: Specify SRS enhancements in Rel-20:
      Multiple frequency-domain starting positions for SRS repetition symbols within each SRS frequency hop for RB-level partial frequency sounding.
      Cross-slot SRS between one U slot and one adjacent S slot within a single SRS resource set.
Proposal 2: Specify long term channel covariance feedback in R20.
Proposal 3: We are additionally positive for following proposals in Rel-20:
      Early CSI-RS/SRS/CSI triggering.
      CSI-RS overhead reduction.
      Leftover issues for asymmetric DL sTRP/UL mTRP

## Slide 11
Appendix-1: Field Test for Phase Continuity
The simulation assumptions are listed as follows:
Field test for phase continuity with real PA:
Each frequency hop is 64 RBs
Partial sounding is 1/4
Multi starting position (enhanced)
Time
Frequency
64 RBs/hop
Subband (R15)
Time
Frequency
Parameters | Values
Carrier frequency | 3.5 GHz
Bandwidth and SCS | 25 MHz, 30 kHz
Channel model | 3GPP 38.901(UMA)
Network Topology | 7*3 Cell, 200 m ISD
UE distribution | 80% indoor，20% outdoor
UE speed | Indoor 3km/h，outdoor 30km/h
SRS period | 80 ms (20 ms * 4 hops) / 40 ms (10 ms * 4 hops)
BS antenna | 64TRX
UE antenna | 2T/4R
TDD configuration | D:U=4:1
Traffic Models | Full buffer

## Slide 12
Type I CSI | Wideband covariance calculation (per 20ms) | Precoding selection (per 20ms) | Complexity estimated as: 696320 per 20ms (CSI feedback periodicity)
Calculation procedure |  |  | 
Complexity estimation | Multiplication operations: 155648 Calculated as | Multiplication operations:540672, Calculated as | 
Type I CSI | Wideband covariance calculation (per 20ms) | Precoding selection (per 20ms) | Complexity estimated as: 696320 per 20ms (CSI feedback periodicity)
Calculation procedure |  |  | 
Complexity estimation |  |  | 
, , , ,
Long term covariance | Wideband covariance calculation (per 20ms) | DFT projection for quantization (per 320ms) | Complexity estimated as: 157760 per 20ms (averaged. wideband covariance calculated per 20ms, but DFT projection is only once for 320ms)
Calculation procedure |  |  | 
Complexity estimation | Multiplication operations: 155648 Calculated as | Multiplication operations:33792, Calculated as | 
Long term covariance | Wideband covariance calculation (per 20ms) | DFT projection for quantization (per 320ms) | Complexity estimated as: 157760 per 20ms (averaged. wideband covariance calculated per 20ms, but DFT projection is only once for 320ms)
Calculation procedure |  |  | 
Complexity estimation |  |  | 
Complexity comparison: The calculation procedure of long term covariance is very similar as Type I CSI feedback, while there is no precoding selection for long term covariance calculation, instead of DFT projection for quantization (only once in 320ms).
As shown above, the calculation complexity is less than Type I CSI calculation.
Appendix-2: Complexity Analysis for Long Term Covariance Feedback:

## Slide 13
Appendix-3: Simulation results for ISD 200m
3.5 GHz
30kHz
7*3 Cell
200m
80% indoor 20% outdoor
320ms for covariance reporting; 20ms for SRS periodicity
64T,4R
FTP3, 50% RU
Baseline: R19 without RHH / reporting
Single-Cell
With Single-TRP with RHH / reporting (
1X
Cell Average
Cell Edge
1X
1.13X
1.23X
1.29X
1.04X
1.07X
1.09X
Single-TRP with RHH reporting
1.02X
1.09X
m-TRP
Cell Edge
1X
1.6X
2.3X
Baseline: 3 TRPs without RHH reporting
3 TRPs CJT with RHH reporting
6TRPs coordination with RHH reporting (3 TRPs CJT+ 3TRPs ZF )
1X
1.33X
1.46X
Cell Average
Preliminary simulation results for ISD200:
Baseline: R19 SRS based measurement.
Gain for long term covariance feedback:
  For single TRP: 9% average gain, 29% cell edge gain could be observed.
  For multi-TRP: much more gain could be observed, 33% and 60% gain for average and cell-edge respectively for 3TRP coordination.

## Slide 14
3.5 GHz
30kHz
7*3 Cell
500m
80% indoor 20% outdoor
320ms for covariance reporting; 20ms for SRS / PMI periodicity
64T,4R
FTP3, 50% RU
Preliminary simulation results for ISD500:
The threshold for SINR is assumed as -10dB, i.e., CSI feedback is used as baseline for less than -10dB, and SRS transmission is used as baseline for more than -10dB.
Baseline: >-10dB use SRS, <-10dB use Type I feedback.
Gain for long term covariance feedback:
  For cell average, 7% and 9% gain for RHH only and RHH+RUU feedback, respectively
  For cell edge，44% and 46% gain for RHH only and RHH+RUU feedback, respectively
Appendix-3: Additional simulation results for ISD500:
Chart: 
| Cell Average | Cell Edge
Single-TRP with R19 SRS / TypeI PMI | 1 | 1
Single-TRP with R_HH reporting | 1.07 | 1.44
Single-TRP with R_HH /R_UU reporting | 1.09 | 1.46
Single-TRP with R19 SRS | 0.95 | 0.61
Single-TRP with TypeI (wideband) | 0.72 | 0.94
Single-TRP with eTypeII (subband 8RBs) | 0.79 | 1.18

## Slide 15
3.5 GHz
30kHz
7*3 Cell
1300m
80% indoor 20% outdoor
320ms for covariance reporting; 20ms for SRS / PMI periodicity
64T,4R
FTP3, 50% RU
Preliminary simulation results for ISD1300:
The threshold for SINR is assumed as -10dB, i.e., CSI feedback is used as baseline for less than -10dB, and SRS transmission is used as baseline for more than -10dB.
Baseline: >-10dB use SRS, <-10dB use Type I feedback.
Gain for long term covariance feedback:
  For cell average, 13% and 18% gain for RHH only and RHH+RUU feedback, respectively
  For cell edge，16% and 17% gain for RHH only and RHH+RUU feedback, respectively
Appendix-4: Additional simulation results for ISD1300:
Chart: 
| Cell Average | Cell Edge
Single-TRP with R19 SRS / TypeI PMI | 1 | 1
Single-TRP with R_HH reporting | 1.13 | 1.16
Single-TRP with R_HH /R_UU reporting | 1.18 | 1.17
Single-TRP with R19 SRS | 0.85 | 0.19