## Slide 1: Consideration on TPRs relating to ITU-R IMT-2030
Security Level:
3GPP TSG RAN#109 RP-252128
Beijing, China, September 15-18, 2025
Agenda Item: 8.2.1.2
Huawei, HiSilicon

## Slide 2
Background
According to the endorsed 3GPP 6G timeline [1], RAN#106 approved the new Study Item of “Study on 6G scenarios/use cases and requirements” (ITU focused part) [2][3]. In response to the received LS [4], a reply LS [5] was sent to ITU-R WP5D including initial considerations of possible minimum Technical Performance Requirement (TPR) items, and evaluation configurations of carrier frequency and bandwidth.
The discussion continued in RAN#107, the following two conference calls and RAN#108 meeting. RAN#108 meeting reached agreement on candidate TPR items, as well as target values for some of them including DL Spectrum efficiency, Latency, Connection density etc. The second reply LS was sent to ITU-R WP5D [6].
This document provides our suggestions on target value for remaining TPR items.

## Slide 3
Proposal
TPR items | IMT-2020 requirements | 3GPP’s agreement on IMT-2030 until RAN#108 | Proposed requirement values on remaining IMT-2030 items | Comments
1. Peak Data Rate | DL 20, UL 10Gbps | TBD | DL: 100~200Gbps UL: 50~100Gbps | Theoretical maximum data rate
2. Peak Spectral Efficiency | DL 30, UL 15bps/Hz | TBD on the values | DL: 60~90bps/Hz UL: 30~45bps/Hz | DL 8 layers/1024QAM, UL 8 layer/256QAM, and overhead optimization
3. 5th percentile user data rate | DL 100, UL 50Mbps | TBD on the values | DL: 500~1000Mbps UL: 50Mbps | DL: 3x IMT-2020 SE + wider bandwidth UL: see simulation in Annex
4. 5th percentile user Spectral Efficiency | Indoor Hotspot DL 0.3/UL 0.21 Dense Urban 0.225/0.15 Rural 0.12/0.045 | Indoor hotspot-IC/Dense urban-IC: – 3x of IMT-2020 for DL – TBD for UL Assuming 7GHz with: – BS: up to 1024 elements – UE: 4Rx or 6Rx or 8Rx Form factor and other operational considerations may limit the number of receiver antennas of UE | Rural-IC: – 3-5x of IMT-2020 for DL Indoor hotspot-IC/Dense urban-IC/Rural-IC: – 3-5x of IMT-2020 for UL | See simulation in Annex
5. Average Spectral Efficiency | Indoor Hotspot DL 9/UL 6.75 Dense Urban 7.8/5.4 Rural 3.3/1.6 | Indoor hotspot-IC/Dense urban-IC: – 3x of IMT-2020 for DL – TBD for UL Assuming 7GHz with: – BS: up to 1024 elements – UE: 4Rx or 6Rx or 8Rx Form factor and other operational considerations may limit the number of receiver antennas of UE | Rural-IC: – 3-5x of IMT-2020 for DL Indoor hotspot-IC/Dense urban-IC/Rural-IC: – 3-5x of IMT-2020 for UL | See simulation in Annex
6. Energy Efficiency | Qualitative | TBD | TBD | 
7. Area Traffic Capacity | 10Mbit/s/m2@Indoor Hotspot | TBD on values | 50~100 Mbit/s/m2@Indoor Hotspot | DL 3x IMT-2020 SE + wider bandwidth
Note: green highlighted parts were agreed in 3GPP RAN#107&RAN#108

## Slide 4
TPR items | IMT-2020 requirements | 3GPP’s agreement on IMT-2030 until RAN#108 | Proposed requirement values on remaining IMT-2030 items | Comments
8. User Plane Latency | eMBB: 4ms, URLLC: 1ms | IC: 4ms, HRLLC: 1ms |  | 
9. Control Plane Latency | 20ms | 20ms |  | 
10. Connection Density | 10⁶ (devices/km2) for mMTC | 10⁶ (devices/km2) for massive communication |  | 
11. Reliability | 1-10-5 | 1-10-5 with same IMT-2020 assumptions |  | 
12. Mobility | Indoor Hotspot-eMBB 1.5bit/s/Hz@10km/h Dense Urban-eMBB 1.12@30km/h Rural-eMBB 0.8@120km/h, 0.45@500km/h | Indoor Hotspot-IC: 2.25 (bit/s/Hz) @10 km/h Dense Urban- IC: 1.68 (bit/s/Hz) @30 km/h Rural-IC: [0.8~1.2] (bit/s/Hz)@120 km/h [0.45~0.675] (bit/s/Hz) @500 km/h NOTE1: Maximum velocity is up to 1000/1200km/h. Do not set spectrum efficiency target for this velocity for ITU TPRs. NOTE2: For Rural-IC, TBD on whether to include other velocities, e.g. 30km/h, 60km/h |  | 
13. Mobility Interruption Time | 0ms | TBD | 0ms, same as IMT-2020 | 
14. Bandwidth | 100MHz | 400MHz (same definition as IMT-2020) |  | 
15. Positioning | NA | Quantitative TPR, TBD on the values | Horizontal accuracy: [20-50cm]@90% for indoor, [3-5m]@90% for outdoor | See simulation in Annex
16. Sensing-related capabilities | NA | TBD | For Outdoor ISD=500m: Localization horizontal accuracy: 3m Localization vertical accuracy: 3m Velocity accuracy : 5m/s | See simulation in Annex
17. AI-related capabilities | NA | Qualitative TPR |  | 
18. Joint/composite requirement | NA | TPR related to data rate, latency, reliability, capacity etc. Applicable usage scenario: immersive communication | 6-12 XR users per TRxP for Dense urban ISD=200m | See simulation in Annex
Proposal: adopt the target value in table above for remaining items of IMT-2030 TPRs

## Slide 5
Reference
RP-240823, Additional Considerations for 6G Timeline, TSG Chairs, 3GPP TSG#103 Joint Session, March 2024
RP-243327 New SID: Study on 6G scenarios/use cases and requirements, CMCC, Verizon, NTT DOCOMO, INC., Deutsche Telekom, 3GPP RAN#106, December 2024
RP-243276 RAN Chair’s Guidance for 6G Study: ITU Focused, 3GPP RAN#106, December 2024
RP-243202 Liaison Statement to External Organizations Minimum requirements related to technical performance for IMT-2030 radio interface(s), source ITU-R WP5D, 3GPP RAN#106, December 2024
RP-243325 Draft Reply to ITUR_WP5D_TEMP_167 = RP-243202 on Minimum requirements related to technical performance for IMT-2030 radio interface(s) (to: SA; cc: -; contact: CMCC), 3GPP RAN#106, December 2024
RP-251825 Reply LS to ITU-R WP5D =RP-243202 on Minimum requirements related to technical performance for IMT-2030 radio interface(s) 3GPP TSG RAN Meeting #108, Prague, Czech Republic, June 9-13, 2025
“Working document towards a Preliminary Draft New Report ITU-R M.[IMT-2030.TECH PERF REQ]: Minimum requirements related to technical performance for IMT-2030 radio interface(s)”, Annex 5.14 to Chairman’s Report of the 49th meeting of Working Party 5D.
RP-251366 Consideration on TPRs relating to ITU-R IMT-2030, Huawei, HiSilicon, 3GPP TSG RAN#108, June 2025

## Slide 6
Annex: simulation results

## Slide 7
UL 5% user data rate
Based on ITU-R IMT-2020 evaluation methodologies (ITU-R M.2412), uplink 5th percentile user data rate is simulated with different uplink bandwidth in eMBB test environment of Dense urban. The evaluated carrier frequency is replaced from 4GHz to 7 GHz, and the max UE transmission power is increased from 23dBm to 26dBm. The MIMO configuration is 768 antenna elements (24,16,2,1,1,8,16) for BS and 4 antenna elements for UE.
Test environment |  | Bandwidth (MHz) | UL 5th percentile SE (bit/s/Hz) | UL 5th percentile user data rate (Mbps) assuming 50% UL time ratio
UL | Dense urban | 20 | 1.36 | 13.6
 |  | 100 | 1.17 | 58.5
 |  | 200 | 0.64 | 64

## Slide 8
Spectral efficiency
Based on ITU-R IMT-2020 evaluation methodologies (ITU-R M.2412), spectral efficiency is simulated for three eMBB test environments of Dense urban, Rural and Indoor. The evaluated carrier frequency is replaced from 4GHz to 7 GHz. The extended MIMO configuration is BS up to 1536 Tx/Rx antenna elements, UE up to 16 Tx/Rx antenna elements.
The simulation results are summarized in table below. The total overhead (control channel, reference signal etc.) is counted as 20%. The effect of real channel estimation is considered. Compared with ITU-R IMT-2020 requirements, spectral efficiency results higher than 5 times IMT-2020 REQ are observed with different extended MIMO configurations at 7 GHz.
eMBB test environments |  | ITU IMT-2020 REQ (Average/Cell edge SE, bps/Hz) | Spectral efficiency of different MIMO configurations@7GHz (Average/Cell edge SE, N x ITU IMT-2020 REQ) |  |  |  | 
 |  |  | 768*x8 | 768*x16 | 1536*x8 | 1536*x16 | 768*x4
DL | Dense urban | 7.8/0.225 | 4.9x/5.6x | 7.3x/9.4x | 6.6x/8.1x | 9.2x/13.1x | -
 | Rural | 3.3/0.12 | 11.3x/9.6x | 18.6x/16.7x | 16.1x/14.2x | 23.9x/26.6x | -
 | Indoor | 9/0.3 | 4.6x/5.1x | 6.4x/8.1x | 6.3x/8.8x | 8.2x/13.2x | -
UL | Dense urban | 5.4/0.15 | 13.5x/6.9x | 14.7x/8.8x | 16x/12.3x | 16.7x/14.8x | 12.4x/5.2x
 | Rural | 1.6/0.05 | 30.7x/8.8x | 33.4x/11.8x | 37.6x/18.1x | 39.7x/23.4x | 28.3x/6.8x
 | Indoor | 6.75/0.21 | 10.7x/20x | 12.4x/26.2x | 15.7x/45x | 16.4x/49.5x | 8.9x/14.5x
* for outdoor (Dense urban and Rural)
BS 768 = (M, N, P, Mg, Ng; Mp, Np) = (24,16,2,1,1,8,16)
BS 1536 = (24,32,2,1,1,8,32)
For indoor hotspot
BS 768 = (8,16,2,1,1,8,16), 256 antenna elements
BS 1536 = (8,32,2,1,1,8,32), 512 antenna elements
For outdoor and indoor, UE 8 = (2,2,2,1,1,2,2), UE 16 = (2,4,2,1,1,2,4)

## Slide 9
Positioning
To investigate the proper requirement for positioning accuracy, simulations are conducted in three scenarios: InF-SH (Indoor Factory with Sparse clutter and High base station height), Indoor office (or hotspot as called in ITU), and Urban Macro. The positioning method of UL-TDOA and single-BS positioning is used in the indoor and outdoor simulation, respectively, with 200MHz SRS bandwidth at carrier frequency around 7GHz.
As results below, the simulation in InF-SH is able to achieve the positioning accuracy of 0.20m@90% CDF for central UE (UE located inside the red box). The result of Indoor office/hotspot is 0.46m@90% CDF due to less LOS BS sites compared with InF-SH scenario. The result of Uma is 2.5m@90% due to visibility of single-BS and NLoS conditions.
Accordingly, it is proposed to consider Horizontal accuracy of [20-50cm] @90% for indoor scenario and [3-5m]@90% for outdoor scenario as requirement for positioning accuracy TPR.
 |  | InF-SH | Indoor Hot Spot | UMa
Frequency |  | 6.7GHz | 6.7GHz | 6.7GHz
Bandwidth |  | 200MHz | 200MHz | 200MHz
Layout | Room Size (L x W x H) | 300m x 150m x 10m | 120m x 50m x 3m | N/A
 | ISD | 50m | 20m | 500m
 | BS number | 18 (6 x 3) | 12 (6 x 2) | 1
BS Parameters | BS height | 8m | 3m | 25
 | BS Power | 23dBm | 23dBm | 56dBm
 | BS Antenna Number | 1 | 1 | 256TRX 1536AE
UE Parameters | UE height | 1.5m | 1.5m | 1.5m
 | UE Power | 23dBm | 23dBm | 23dBm
 | UE Antenna Number | 1 | 1 | 1
Case |  | 67% | 80% | 90%
InF-SH, 7GHz, UL-TDOA, 200MHz | All UE | 0.06 | 0.15 | 0.34
 | Central UE | 0.05 | 0.09 | 0.20
Indoor Hot Spot, 7GHz, UL-TDOA, 200MHz | All UE | 0.18 | 0.43 | 0.95
 | Central UE | 0.09 | 0.17 | 0.46
Case1 InF-SH, ISD=50, BS height=8m
Case2 Indoor hotspot, ISD=20, BS height=3m
Central UE
Central UE
Simulation of indoor scenarios (InF-SH and Indoor hotspot)
Simulation of outdoor scenarios (UMa)
500m
UMa ISD500m
Positioning method
Geometry-based: Single-BS RTT+AoA
AI-based: Single-BS AI positioning
  Rel-19 AI/ML positioning extension
RTT+AOA: 14.9m@90%
Single-BS AI pos: 2.5m@90%
Simulation configurations

## Slide 10
Sensing
Sensing localization accuracy and velocity accuracy are simulated based on the urban grid geometry defined in TR37.885 as below. There are 9 buildings (the green blocks in the figure) with four lanes in between, the lane width is 3.5m. The size of each buildings is 413m (length) x 230m (width) x 20m (height). All BSs are located on the rooftop of the buildings, all sensing targets (vehicles) are located on the street, and the UEs are located on the sidewalk road.
The simulations are conducted at 7 GHz carrier frequency and 400MHz bandwidth, including 2 cases of BS-UE bistatic LOS and BS-UE bistatic LOS+NLOS. The cooperation among multiple BSs of same or different sites is applied.
Layout: Urban grid as TR37.885 ISD=500 m
Localization accuracy
Velocity accuracy
Simulation configurations
ISD | 500m
BS number | 5
BS height | 25m
UE number | 128 (inter distance ~17m)
UE height | 1.5m
Frequency | 7GHz
Bandwidth | 400MHz
Antennas number | 16*32
Target number | 36 ST
Target Velocity | 60km/h

## Slide 11
Composite requirements (for XR use case)
Using the evaluation methodology of 3GPP study on XR (Extended Reality) evaluations for NR in TR38.838, XR capacity is evaluated for eMBB dense urban test environment at 4GHz and 7 GHz.
The simulation results are in figures below for DL and UL respectively.
Application |  | DL I/P-stream | UL pose/control | UL I/P-stream
Frame per second/Sampling Frequency |  | 60 FPS | 250 Hz | 60 FPS
Average data rate |  | R = 30 Mbps = 2 | 0.2 Mbps | R = 10 Mbps = 2
Packet delay budget |  | 10ms | 10ms | 30ms
Packet success rate |  | 99% | 99% | 99%
GOP size |  | K = 8 |  | K = 8
Packet size | Distribution | Truncated Gaussian Distribution | Fixed Size | Truncated Gaussian Distribution
 | I-stream Mean | 111112 Bytes | - | 37037 Bytes
 | P-stream Mean | 55556 Bytes | - | 18519 Bytes
 | STD | 0.105*mean | - | 0.105*mean
 | Max | 1.5*mean | - | 1.5*mean
 | Min | 0.5*mean | - | 0.5*mean
Jitter | Distribution | Truncated Gaussian Distribution |  | Truncated Gaussian Distribution
 | Mean | 0 ms |  | 0 ms
 | STD | 2 ms |  | 2 ms
 | Range | [-4, 4] ms |  | [-4, 4] ms
Application |  | DL I/P-stream | UL pose/control | UL I/P-stream
Frame per second/Sampling Frequency |  | 60 FPS | 250 Hz | 60 FPS
Average data rate |  |  | 0.2 Mbps | 
Packet delay budget |  | 10ms | 10ms | 30ms
Packet success rate |  | 99% | 99% | 99%
GOP size |  | K = 8 |  | K = 8
Packet size | Distribution | Truncated Gaussian Distribution | Fixed Size | Truncated Gaussian Distribution
 | I-stream Mean | 111112 Bytes | - | 37037 Bytes
 | P-stream Mean | 55556 Bytes | - | 18519 Bytes
 | STD | 0.105*mean | - | 0.105*mean
 | Max | 1.5*mean | - | 1.5*mean
 | Min | 0.5*mean | - | 0.5*mean
Jitter | Distribution | Truncated Gaussian Distribution |  | Truncated Gaussian Distribution
 | Mean | 0 ms |  | 0 ms
 | STD | 2 ms |  | 2 ms
 | Range | [-4, 4] ms |  | [-4, 4] ms
Traffic model: GOP (Group-Of-Picture) based I/P-Stream traffic model from 3GPP TR38.838
BS 64: (M, N, P, Mg, Ng; Mp, Np) = (12,8,2,1,1,4,8), 192 antenna elements
BS 256: (M, N, P, Mg, Ng; Mp, Np) = (24,16,2,1,1,8,16), 768 antenna elements