## Slide 1: RP-252158 3GPP TSG RAN Meeting #109 Beijing, China, September 15-18, 2025 Source: Anterix, Rakuten Title: Views on Rel-20 RAN4 RRM 3 MHz (e)Redcap Document for: Approval Agenda Item: 9.1.4.4

## Slide 2
Proposals led by RAN4 (not spectrum related)
Agenda 9.1.4.4: RRM Topics
RP-251879 (RAN #108) WF for RAN4 led REL-20 topics – specifically (e)Redcap enhancements
  The proposed WI for (e)RedCap enhancements is crucial for addressing immediate market needs for migrating LTE IoT devices to 5G, with recommendations to proceed with a dedicated work item to ensure
  Wide Industry Support - Anterix, Nokia, Southern Linc, Futurewei, Itron, Sony, T-Mobile, Qualcomm, Rakuten Mobile, Semtech, Nordic Semiconductor, Aalyria Technologies, Novamint, Viasat, Immarsat, Ericsson, Oppo
  In preparing a WI we note that there is some “potential” work to be done in other WGs
  Possible minimal work for RAN1 if necessary to specify cell edge performance issues
  Likely minimal work for RAN2 on data rates, removing 3 MHz restrictions for certain UE/capabilities
Example Bands: n106, n85, n26, n28 & NTN n255, n253, n251, n250
Remove UE BB bandwidth restriction for 5 MHz BB bandwidth

## Slide 3
Proposed Features and Impacted TS/TR
Specify core RRM requirements while minimizing specification impact to support operation in 3 MHz (15 PRB) channel bandwidth led by RAN4.
  Support 15 PRB implementations of 3 MHz channel bandwidths, FR1, 15 kHz SCS
Utilize existing (e)Redcap 2 Rx capabilities defined in Rel-17, Rel-18 and Rel-19 unless otherwise specified.
  1 Rx and/or 1 Tx antenna support, No CA/DC, Reduced modulation: Max 64-QAM DL, 16-QAM UL, Reduced MIMO, Power-saving: eDRX, small data transmissions, RRM measurement relaxations, Standalone (SA) only, HD/FD-FDD operation, Early UE identification support, Small data transmission optimizations, NTN support
Add Radio Link Monitoring (RLM) and Beam Failure Detection (BFD) for connected mode (e)Redcap UE power saving.
Mostly RAN 4 led items such as
  Specify necessary RRM performance requirements (RAN4)
  Specify necessary UE RF requirements, demodulation performance and CSI reporting requirements (RAN4)
  Specify necessary BS demodulation performance requirements (RAN4)
  Specify necessary BS conformance tests (RAN4)
Impacted existing TS/TR |  |  | 
TS/TR No. | Description of change | Target completion plenary# | Remarks
38.202 | NR; Services provided by the physical layer | RAN#114 | Core part
38.211 | NR; Physical channels and modulation | RAN#114 | Core part
38.212 | NR; Multiplexing and channel coding | RAN#114 | Core part
38.213 | NR; Physical layer procedures for control | RAN#114 | Core part
38.214 | NR; Physical layer procedures for data | RAN#114 | Core part
38.300 | NR; NR and NG-RAN Overall description; Stage-2 | RAN#114 | Core part
38.304 | NR; User Equipment (UE) procedures in idle mode and in RRC Inactive state | RAN#114 | Core part
38.306 | NR; User Equipment (UE) radio access capabilities | RAN#114 | Core part
38.321 | NR; Medium Access Control (MAC) protocol specification | RAN#114 | Core part
38.331 | NR; Radio Resource Control (RRC) protocol specification | RAN#114 | Core part
38.413 | NG-RAN; NG Application Protocol (NGAP) | RAN#114 | Core part
38.101-1 | NR; User Equipment (UE) radio transmission and reception; Part 1: Range 1 Standalone | RAN#114 | Core part
38.133 | NR; Requirements for support of radio resource management | RAN#114 | Core part
38.101-4 | NR; User Equipment (UE) radio transmission and reception; Part 4: Performance requirements | RAN#114 | Perf. part
38.104 | NR; Base Station (BS) radio transmission and reception | RAN#114 | Perf. part
38.133 | NR; Requirements for support of radio resource management | RAN#114 | Perf. part
38.141-1 | NR; Base Station (BS) conformance testing Part 1: Conducted conformance testing | RAN#114 | Perf. part
38.141-2 | NR; Base Station (BS) conformance testing Part 2: Radiated conformance testing | RAN#114 | Perf. part

## Slide 4
TU and WG Timeline
Request 0.25RD/0.25RF TUs with ~12 months duration is appropriate for RAN4 TUs allocated to (e)Redcap
Target WI complete by Dec 2026
Minor work in RAN1 and RAN2
  Estimate 0.1 TU in each WG for two meetings
Works well within proposed Rel-20 TU budgets

## Slide 5: Thanks
Emil Olbrich
eolbrich@anterix.com