## Slide 1: Motivation of New WI Proposal on Network Assisted Interference Cancellation and Suppression for LTE
Copyright © MediaTek Inc. All rights reserved.
RP-132018
TSG-RAN Meeting # 62
Busan, South Korea, December 3 - 6, 2013
MediaTek Inc

## Slide 2: Progress (1/2)
Significant progress since SI approved in RAN#59
  Deployment scenarios
  Candidate NAICS receiver types (i.e., ML/R-ML, SLIC, CWIC, E-LMMSE-IRC, WLMMSE-IRC)
RAN4
  Defined several typical geometry profiles and a dynamic interference on/off model under FTP traffic
  Observed that E-LMMSE-IRC/SL-IC/R-ML/CWIC all achieve noticeable performance gain over Rel-11 LMMSE-IRC receiver in most scenarios, and the gains depend on the different interference profiles.
    SL-IC/R-ML has larger gain compared to E-LMMSE-IRC in many cases with genie-aided interference information.

## Slide 3: Progress (2/2)
RAN1
  Conducted system simulation that can takes into account all the possible realistic conditions with corresponding occurrence probabilities
  Preliminary system level results indicated that E-LMMSE-IRC/SL-IC/R-ML all showed noticeable gains over baseline MMSE-IRC receivers, which is aligned with the observations from link level evaluation.
    System evaluation was based on validated link abstraction methods or using embedded actual link level simulation.

## Slide 4: Current status on network assistance (1/2)
RAN1
  Compared to requiring NAICS receivers to detect all interference parameters, some network signalling/coordination can be beneficial for reducing receiver complexity and/or improve performance with increased robustness under intra-cell and inter-cell interference scenario.
    The interference transmission parameters that can be considered for signalling and that for receiver detection are for further study.

## Slide 5: Current status on network assistance (2/2)
RAN4
  There is no consensus yet on the feasibility and performance of blind detection receivers.
    Comparing blind detection receivers with genie-aided receivers, there is varying degree of performance degradation from minimal to noticeable, depending on operation assumptions.
  The next focus will be the evaluation of the performance and complexity of blind detection of interference parameters, including which parameters to be blindly estimated by the Ues and which will be NW-assisted.

## Slide 6: Open Issues (RAN1: 60-70% completion level)
  The transmission parameters that can be considered for signalling and that for receiver detection are FFS, after taking into account the following aspects:
    Receiver performance and complexity impact, comparing network assistance with UE blind detection (RAN4, see below)
    Feasibility of assistance signalling and the impact of associated signalling overhead on system performance (RAN1/2)
    Network performance impact if any network coordination is assumed that introduces scheduling constraints (RAN1).
  System level results are still limited, especially in terms of
    Performance after taking into account assistance signalling overhead and after considering backhaul latency of more than 2 msec in inter-cell NAICS in scenarios 1 and 2a
    Performance under imperfect CRS interference cancellation and imperfect blind detection of interference parameters

## Slide 7: Open Issues (RAN4: 70-80% completion level)
  There is no consensus on the feasibility and performance of blind detection receivers and it is agreed that RAN4 should study the performance and complexity of blind detection of interference parameters, including which parameters to be blindly estimated by the UEs.
  Due to lack of time, the following aspects in SID had only limited or no discussion:
    Intra-cell MU-MIMO, since intra-cell interference focused on SU-MIMO only so far
    Other types of channel collision than PDSCH-to-PDSCH (e.g. PDCCH/EPDCCH-to-PDSCH), which was considered as first priority.
    No comparison of NAICS with respect to Rel-11 non-linear receivers required for FeICIC has been done: No discussions/agreements on whether Rel-11 non-linear receivers required for FeICIC are applicable as a baseline for NAICS.

## Slide 8: Motivations
In order to be able to translate the promising gains into actual performance improvement in commercial deployment as early as possible, it is proposed to start the work item phase targeting Rel-12
  What it means is to close the SI and have one-step approval of TR36.866 version 1.1.0
SI already concluded that network assistance signalling of interference transmission parameters can reduce receiver complexity and possibly improve performance, as well as any physical layer changes if necessary to achieve the system level gain

## Slide 9: Proposed WI Scope
  Specify necessary network assistance signalling of interference transmission parameters to reduce receiver complexity and possibly improve performance, as well as any physical layer changes if necessary to achieve the system level gain
    Identify the interference transmission parameters for signalling and those for receiver detection, taking into account the following aspects:
      Receiver performance and complexity impact, comparing network assistance with UE blind detection (RAN4)
      Feasibility of assistance signalling and the impact of associated signalling overhead on system performance (RAN1/2)
      Network performance impact if any network coordination is assumed that introduces scheduling constraints (RAN1).
    Consider a phased approach with a first focus on higher-layer based assistance signalling, regardless of whether the associated interference parameter is higher-layer configured or dynamic.
      Some dynamic assistance signalling can be considered as a second focus if sufficient additional system-level gain is shown.

## Slide 10: Alternative that can also be considered
Extend the SI for 1 more quarter, with the sharpened focus below in order to complete it in time for Rel-12
  Identify the interference transmission parameters for signalling and those for receiver detection, taking into account the following aspects:
    Receiver performance and complexity impact, comparing network assistance with UE blind detection (RAN4)
    Feasibility of assistance signalling and the impact of associated signalling overhead on system performance (RAN1/2)
    Network performance impact if any network coordination is assumed that introduces scheduling constraints (RAN1).
The above focus is aligned with the WI objectives and also currently captured as open issues
  Also widely agreed as next focus in RAN1 and RAN4 regardless of WI or SI

## Slide 11
Copyright © MediaTek Inc. All rights reserved.
www.mediatek.com