## Slide 1: Consideration on MDT Further Enhancements
CMCC
RP-150192
TSG RAN meeting #67
Shanghai, P. R. China, 9-12 March, 2015
Agenda Item: 13.1.2
Document for: Discussion and Decision

## Slide 2: Background(1/2)
Coming with LTE commercial deployment
  VoLTE （MMTEL voice) -> one of the most basic service
  SINR -> basic criterion for network performance assessing

## Slide 3: Background(2/2)
VoLTE
  Deployment of VoLTE road map of most operators is this year
SINR
  Be used to detect coverage problems and access network performance

## Slide 4: Motivation(1/3)
The general motivation of MDT
  Decrease the cost of drive testing
  Avoid additional emission of CO2
  Extend time and space for drive testing

## Slide 5: Motivation(2/3)
However current MDT still cannot match the requirement of LTE commercial deployment
  Lacking VoLTE related measurement and corresponding collection
  Lacking SINR-like measurement and its collection

## Slide 6: Motivation(3/3)
In order to guarantee the successful LTE deployment in an efficient manner,
We propose to start a SI for MDT further enhancement for LTE network.

## Slide 7: Objective(1/2)
Study MMTEL voice and video related measurements and corresponding collection. E.g.,
  To assess performance: delay/jitter, packet loss rate (PDCP)
  To shot problem: handover failure when VoLTEing
  To figure out hotspot area for MMTEL voice and video traffic: traffic logging

## Slide 8: Objective(2/2)
Study SINR-like measurement and collection
  I.E., UE based SINR measurement with sufficient accuracy or BLER
Consider provision of additional feedback from UE
  handling diverse capabilities that impact MDT measurement results (e.g. new type of assistance information such as IDC, etc)

## Slide 9: General principles
Introduction of solutions for further MDT improvements should be based on analysis of the applicability, usefulness and feasibility
Further, the following principles should be followed when developing the solutions for MDT enhancements:
  Principles established for MDT, e.g. in TS 37.320, applies.
  Duplication of the existing functionality should be avoided.
  Impact to end user experience and system performance needs to be kept acceptable
  UE complexity and memory requirements for MDT support need to be carefully considered

## Slide 10: Proposals
Proposal 1: Start the further enhancement of MDT (feMDT) SI in R13
Proposal 2: feMDT should focus on studying MMTEL voice and video traffic related measurements and measurements collection
Proposal 3: feMDT should take SINR related measurements and measurements collection into consideration
Proposal 4: feMDT should consider provision of additional feedback from UE handling diverse capabilities that impact MDT measurement results