## Slide 1: Motivation for New SI: Interference coordination for semi-static refarming between UMTS and LTE
China Unicom
RP-150266
3GPP TSG RAN#67
Shanghai, P. R. China, 9 – 12 March 2015
Document for : approval
Agenda Item: 13.1.1

## Slide 2: Motivation for UMTS and LTE semi-static spectrum refarming
F1
F2
F3
F4
UMTS
LTE
U1
L2
Area of iRAT handover
Signal
Interference
Uplink
Some UMTS bands are refarmed per cell according UE penetration.
The inter-RAT inter-band interference between cells that are refarmed from UMTS to LTE and neighbor UMTS cells on the same band, should be evaluated.
Interference coordination between two RATs may be needed.
Benefits
  Earlier U->L refarming means better spectral efficiency and better UE QoE
  Zero buffer zone between neighbor U and L intra-freq cells to maximize spectrum utilization
  Avoid UL throughput loss due to neighbor sites’ UE transmission power
  Exempted from manual planning of static refarming schema

## Slide 3: Conclusion from the RAN3 Study on semi-static spectrum refarming
There was a study item named MRJC (Multi-RAT Joint Coordination, SID is RP-132086) in RAN3.
RAN3 has achieved the following agreements for spectrum refarming. Details are captured in TR 37.870.
  For the scenario and use cases, RAN3 agreed that spectrum holes may exist in long term, short term, and in space.
  For the possible solutions, RAN3 identified two alternatives:
    Static spectrum refarming
    Semi-static spectrum refarming
  And RAN3 concluded that
    RAN3 has discussed the scenario and possible solutions for spectrum holes.
    It was concluded that the planned schemes for static or semi-static spectrum reallocation can be configured via OAM, as described in section 6.1.2 in TR37.870.
    The inter-RAT interference should be taken into account when spectrum reallocation is applied especially if no (or a small) buffer zone is planned.
    However, RAN3 could not assess the impacts of the inter-RAT interference as they are out of its scope, nor conclude on possible solutions. Interference aspects could be evaluated in more appropriate RAN WGs.

## Slide 4: Proposal of a New SI
A short study item led by RAN1 is proposed, with the following objectives
  Analyze the inter-RAT and intra-band interference between the two RATs for spectrum refarming.
  Identify radio measurements to evaluate the inter-RAT and intra-band interference.
  Identify solutions to coordinate the inter-RAT and intra-band interference.

## Slide 5
Thank you!