## Slide 1: Way forward on new UE categories in Rel-12 and 13
NTT DOCOMO, INC., AT&T, MediaTek, ACER, ASUS, CHT, HTC, ITRI, LGE, Panasonic, Sharp, Hitachi
3GPP TSG-RAN#67
Shanghai, China, 9 - 12 March 2015
Agenda: 14
RP-150367
Revision of RP-150207

## Slide 2: Way forward
Introduce a new UE category for DL 750 Mbps from Rel-12.
  The corresponding CR is prepared for RAN#68.
Introduce new UE categories for 1 Gbps or beyond from Rel-13
  The target rate will be continued to discuss and decided until RAN#69 (so that the corresponding CR can be prepared for RAN#70).

## Slide 3: Rationale for 750 Mbps category
Market demand for high frequency bands
  E.g., 3DL CA with low and high frequency bands.
    20 MHz with 2 layer MIMO (low) and 40 MHz with 4 layer MIMO (high).
    B1/3+B42+B42 is being specified in RAN4.
Support of 2 layer MIMO up to 5 CCs.
  The current specification supports the 2 layer MIMO configuration up to 4 CCs (300/450/600 Mbps).
  As 2 layer MIMO is a typical configuration applicable to all frequency bands, support for 5CCs (i.e., 750 Mbps) is deemed as necessary.
==> 750M is worthwhile introducing the almost frozen release, i.e., Rel-12.

## Slide 4: Rationale for 1G and beyond from Rel-13 (new slide)
Achieving the 1G rate requires 256QAM and 4x4 MIMO.
  Assuming the available band combination so far (up to 3DL CA).
However, there is no formal conclusion on the gain of 256QAM + 4x4MIMO in the study of SCE (TR 36.872).
A technical challenge to support the increased number of MIMO layers in intra-band contiguous CA has been discussed in RAN2/4 but yet to be concluded
A strong concern to increase L2 buffer was expressed by UE vendors during the Dual Connectivity work.
  Even if the objective is to increase the peak rate!
==> Given that technical feasibility and gain is questionable so far, it is NOT worthwhile introducing to the almost frozen release.
==> Introduction to the “open” release (Rel-13) is sensible