## Slide 1: Elevation Beamforming/Full-Dimension (FD) MIMO for LTE and AAS work in RAN4
Ericsson
RP-151003 AI 13.1.1

## Slide 2: New RAN4 Requirement methodology needed Example issue
Long list of fundamental issues to sort out – emissions just one of them
Current methodology assumes measurement ports which may not exist for AAS
Currently total allowed unwanted emissions level for a BS increases linearly with the number of antennas
  More antennas for operator A may mean more interference for operator B
Risk for large amounts of unwanted emissions despite fulfilling requirements!
Fundamental new RAN4 methodologies needed! -- can’t be squeezed into a tight Rel-13 timeline

## Slide 3: General
Without proper RAN4 requirements, FD-MIMO specifications will just be for testbeds and demonstrators and not commercially deployable
FD-MIMO systems will be Active Antenna Systems
  Cannot connect >8 antennas and radios using cables!
RAN4 needs to build FD-MIMO requirements into the AAS specifications
  No AAS specification available to build upon until the end of release 13

## Slide 4: General
The release 13 AAS specification will not be suitable for array sizes > around 8 TRX (see R4-152053)
Main consequences of not doing RAN4 work for FD-MIMO properly:
  Interference to other networks from deployed AAS
  Reduced UL performance and resulting increased interference to other operators from UEs transmitting at higher power
  Not guaranteed TX signal quality for MIMO and high data rates

## Slide 5: Proposal
RAN4 work for FD-MIMO is extensive
RAN4 should first complete the baseline AAS specification in release 13
  AAS lays important pieces of a fundamental framework needed for further work
Explicitly note that RAN4 requirement coverage is for up to 8 ports in Rel-13
  Do not then need significant RAN4 TUs for Rel-13.
RAN4 develops FD-MIMO requirements for >8 ports in release 14
  RAN1 may support >8 ports in release 13, but not RAN4
  Similar approach to carrier aggregation; RAN1 supports 5 CC, RAN4 up to rel-12 max 3CC.

## Slide 6: Annex – technical details
(See also R4-152053)

## Slide 7: Need for RAN4 requirements - emissions
Currently total allowed unwanted emissions level (requirement) for a BS increases linearly with a number of antennas
  FD-MIMO systems could be built with cheap small components but cause large amounts of unwanted emissions
  Operators deploying such systems would cause interference problems to other operators
Total emissions can increase when antennas are present even if current per radio requirements are passed
  Can lead to operators causing interference even though emissions pass

## Slide 8: Need for RAN4 requirements - Sensitivity
Current receiver sensitivity requirement not designed for large arrays
Need to capture self interference in highly integrated systems
Current requirements do not capture this
  BS may pass requirements but have poor sensitivity
  Reduced coverage and UL performance for the owner operator
  UE power must be increased to compensate -> Interference to other operators

## Slide 9: Need for RAN4 requirements – TX signal quality
Current EVM requirements are only tested with no antenna connected
When antenna is connected, coupling effects cause EVM to increase
Much worse than expected performance despite apparently passing requirements

## Slide 10: Need for RAN4 requirements – BS classes
Not clear at all that the current framework for classifying BS with the associated assumptions for setting requirements (MCL) is appropriate for large arrays
Consequence – susceptibility to blocking, interference etc. not properly captured or known
Operators may face unexpected performance problems once deployed

## Slide 11: Need for RAN4 requirements - testing
Testing is at an “antenna connector”
  Difficult to identify where this is for highly integrated systems
  Easy to measure signals at the wrong point and get misleading results
Whole system performance is not captured
  Just capture single radio performance, not composite radio, array and antenna performance
Cannot always build antenna connectors in large arrays
  Makes FD-MIMO difficult to implement