## Slide 1
Motivation for new WI proposal: Carrier aggregation in unsynchronized networks for LTE
RP-162167
Agenda: 10.1.2
www.huawei.com
Huawei, Hisilicon
Notes: 讲解：
我希望向大家汇报三方面的情况。
行业趋势与华为战略
2013年经营业绩
未来（行业有希望，运营商选择我们，员工热情奋斗）

## Slide 2
Motivation
  Carrier aggregation and dual connectivity are efficient methods for data aggregation to improve user throughput.
    When CA is deployed, frame timing and SFN need to be aligned across cells that can be aggregated.
    Dual Connectivity can be deployed if frame timing and SFN are not aligned across cells . However, the UE needs to support at least two UL carriers on PCell in MeNB and PSCell in SeNB respectively.
    Single carrier has better UL coverage performance than two UL carrier transmissions
  UE capable of only one UL CC cannot support Dual Connectivity / Carrier aggregation in case of unsynchronized network (i.e. the frame timing and SFN are not aligned across cells)
Scenarios | Synchronized Network Ideal backhaul | Unsynchronized network Non Ideal or Ideal backhaul
UE capable of two UL carriers | Carrier aggregation | Dual connectivity
UE capable of single UL carrier | Carrier aggregation | Not supported
  In order to improve user throughput and UL coverage, it is meaningful to support data aggregation for the UE capable of only one UL CC in case of unsynchronized network (i.e. the frame timing and SFN are not aligned across cells).

## Slide 3
Enhancements to support Carrier aggregation in unsynchronized networks
  Main Issue: Subframe timing mapping
    Since the frame timing and SFN are not aligned between serving cells, the timing difference between PCell and SCell needs to be configured for HARQ timing / DRX /Measurement GAP operations.
    Adjustment of sub-frame mapping may be needed, e.g. due to clock drifting, TA value change, UE processing time

## Slide 4
Objective
  In order to improve per-user throughput and UL coverage, data aggregation for the UE capable of only one UL CC in case of unsynchronized network (i.e. the frame timing and SFN are not aligned across cells) needs to be supported, including:
    Removal of the SFN alignment requirement between serving cells for CA (i.e. 30.26 ms ) (RAN2, RAN4)
    SFN offset and sub-frame time difference acquisition (RAN2, RAN3)
    Sub frame mapping configuration and adjustment for HARQ timing / DRX operation / measurement GAP operation etc. (RAN2, RAN4, and RAN1)

## Slide 5
Copyright©2015 Huawei Technologies Co., Ltd. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
Thank you !