## Slide 1
Source: Samsung
Motivation for new SI: NR-based V2X services
Agenda Item: 9.1, Document for: Discussion and Decision
RP-170162
3GPP TSG RAN Meeting #75
Dubrovnik, Croatia, March 6th - 9th, 2017

## Slide 2: Motivation
25 new use cases agreed by SA1 (22.886), which covers much diverse requirements
  Extremely low latency (e.g. 3 or 5ms), high reliability (e.g. 99.999%), large data rates (up to 1Gbps) and large communication range
 | Platooning | Advanced driving | Extended Sensor | Remote driving
Payload (Bytes) | [50]~[6500] | 450~[6500] | [1600] | 
Tx rate (message/sec) | 2~50 | 10~50 |  | 
Max latency (ms) | 10~25 500 | [3]~[100] | 3~100 | [20]
Reliability (%) | 90~99.99 | [99.99]~[99.999] | 90~99.999 | [99.999]
Data rate (Mbps) | 12k~[65] | [10]~[53] DL: [0.5] UL: [50] | [10]~1000 | UL: 25 DL: 1
Communication range | [5~10] sec * (max. relative speed) [m/s], 80m | [5~10] sec * (max. relative speed) [m/s], 500m | 50~1000m | 

## Slide 3: Motivation
LTE-based V2X support was specified in Rel-14 to provide functionalities needed to for the use cases defined in [SA1 TR: TR 22.885]
  Target to TBS (<=1200 Bytes), latency (20, 50, 100ms), message rate (50, 20, 10~1 per second), reliability (>=95%), Communication range (4 sec * (max. relative speed) [m/s])
  Not good enough for high time/frequency error and high vehicle speed (500km/h)
  Only broadcast is supported
  Support for short period is not optimized

## Slide 4: Motivation
Starting NR Phase-1 normative work in Rel-15, there is increasing interest in studying technologies for NR-based V2X services, at least including
  OFDM waveform with larger SCS and shorter TTI, or flexible SCS/TTI
    Larger SCS is more robust to frequency error and doppler
    Smaller DMRS overhead
  NR support for URLLC and eMBB
    High reliability, high data rate, low latency
The most stringent requirements of advanced V2X use cases can only be supported by NR V2X. The new NR features could provide even better performance than LTE V2X for the early V2X use cases, hence more competitive to other RATs
It is preferred to optimize NR V2X design for all V2X use cases for overall competitive power

## Slide 5: Objectives for NR based-V2X services
To define the evaluation methodology for NR-based V2V, V2I/N and V2P services with use cases defined in [SA1 TR: TR 22.885] and advanced use cases defined in [SA1 TR: TR 22.886] to compare the performance of different technical options
  The related work should start from the agreed evaluation methodology captured in [RAN1 TR: TR 36.885 Study on LTE-based V2X Services]. [RAN1]
For the use cases defined in [SA1 TR: TR 22.885] and the advanced use cases defined in [SA1 TR: TR 22.886], identify and evaluate necessary mechanisms to meet identified requirements for robustness, latency, overhead and capacity: [RAN1, RAN2, RAN3]
  Mechanisms for NR sidelink, including physical channel structure for robust operation in cases of high Doppler and large time/frequency error, reliable synchronization by GNSS, gNB and other UE(s), efficient resource pool structure and resource allocation to mitigate impact of half duplex constraint, reduced in-band emission and reduced resource collision
  Mechanisms for UE type RSU
  Mechanisms for QoS, congestion control and mobility management
  Mechanisms to enable efficient coexistence and inter-working with other technologies including LTE-based V2X and IEEE802.11p-based V2X
For the use cases defined in [SA1 TR: TR 22.885], identify and evaluate necessary improvements of NR V2X with respect to LTE V2X. [RAN1, RAN2, RAN3]