## Slide 1: 3GPP RAN #75 6th to 9th March 2017, Dubrovnik, Hungary
V2X Evolution Timeline and Scope
Qualcomm, LGE, Cohere Technologies

## Slide 2: Context
We refer to a context where there is interest for
  LTE V2V enhancements
  Evolution of 3GPP V2X exploiting the technologies introduced for NR
Referring to discussions ongoing on draft reflector

## Slide 3: Set 1: Potential Rel-15 Work Item for 3GPP V2X Phase II
Starting: March 2017 (RAN#75)
Scope:
  New PC5 functionality which can co-exist in the same resource pools as Rel-14 functionality, and use the same scheduling assignment format, which can be decoded by Rel-14 UEs, without causing significant degradation to Rel-14 operation:
  Higher order modulation
  Carrier Aggregation
  Transmission latency reduction (reduced time between packet arrival at layer 1 and transmission on the radio)
  Coexistence between UEs using mode 3 and mode 4 resource provisioning
  [subject to study] Tx diversity
  [subject to study] Short TTI
    Our view: The technical feasibility/value of sTTI as an “evolutionary item” is not clear since PSCCH will occupy a sub-frame.
LTE V2V enhancements

## Slide 4: Set 2: Potential Rel-15 Study Item for 3GPP V2X Phase III
Starting: TBD
  Our view: Small #TU can be allocated to start the simulation assumption work starting Mar. 17.
  Our view: Joint approval of Phase 1 WI and Phase 2 SI is important to show to the external world that 3GPP V2V technology continues to improve with new features & use cases
Tentatively comprising:
  New PC5 functionality that would benefit from having less design constraints than 5G V2X phase 1, and therefore benefiting from different resource pools on the same carrier or a different carrier from Rel-14 V2V
  Potentially some higher layer features
  Positioning using ranging (taking into account any advice from SA3)
A Work Item for set 2 (5G V2X Phase 2 normative phase) would follow as required
  Our view: Rel.16 WI needs be targeted to show constant evolution of cellular V2X work especially after a relatively limited R-15 evolution
More “unconstrained” design leveraging NR concepts

## Slide 5: Conclusion
Jointly approve Phase II WI and Phase III SI for V2V/V2X
  Important to show cellular V2X is addressing both short-term enhancements and long-term new features and use cases
V2V Phase III study item should start in March 17
  Time Unit allocation can be small to start off with and focus on simulation assumptions
Phase III normative work should target R-16 specification
  Important to show strong progress & continued evolution
Show continued evolution of the 3GPP V2V platform with every Release