## Slide 1: Motivation for New SI on NR support for high speed scenario
3GPP TSG RAN Meeting #75 RP-170260
Dubrovnik, Croatia, March 6-9, 2017
Agenda Item: 9.1

## Slide 2: NR High Speed Train Scenario
  Layout
  Option 1: Macro only
  Option 2: Macro + relay
  Carrier frequency for macro link
  Around 4 GHz
  Around 30 GHz
  Carrier frequency for relay link
  Around 4 GHz
  Around 30 GHz
  Around 70 GHz
Assumptions*
Scenario description
*3GPP TR 88.913, “Requirements for next generation access technologies,” V14.0.0, Oct. 2016.
Supporting very high traffic volume with very high mobility on high speed train (HST)

## Slide 3: Performance Requirements
*3GPP TS 22.261, “Service requirements for the 5G system (Stage 1),” V1.1.0, Jan. 2017.
Requirements for high speed train scenario (from 3GPP SA1*)

## Slide 4: Layout Options for HST
Macro only
Macro + relay
High carriage penetration loss
Individual handover
Higher UE power consumption and requirements
No carriage penetration loss
Group handover
Less UE power consumption and requirements (same as indoor UE)

## Slide 5: Spectrum Options for HST
Scarce available spectrum
NLOS-dominant
Lower path-loss
Abundant available spectrum
LOS-dominant
Higher path-loss
Large array gain at the same aperture size
Around 4 GHz
Around 30 GHz
Macro link carrier frequency candidates

## Slide 6: HST Challenges
Severe Doppler shift/spread
Frequent handover
Doppler shift is proportional to
  Speed
  Carrier frequency
Handover frequency
Proposal: In NR, a study is needed to solve these HST-specific technical challenges

## Slide 7: Objectives
Mobility
Define NR HST evaluation methodology, considering:
Data rate and spectral efficiency
Coverage
Various HST deployment environments including urban, rural, and tunnel scenarios
Antenna configuration, RRH configuration
Latency
Identify NR HST evaluation assumptions, considering
Investigate necessary solutions to enable NR HST support
Link-level solutions for improving efficiency and robustness to the high speed
  Numerology/frame structure design
  Doppler estimation and compensation
Efficient initial access and random access solutions
  Cell search
Solutions for Scheduling, handover, and mobility management
Network-wide solutions for high mobility, i.e., SFN, additional/supplementary link support
Waveform design
Reference signal design
Multi-antenna support with high mobility
RACH procedure