## Slide 1
Motivation for a New WID: Further enhancements on Voice and Video for LTE
3GPP TSG RAN Meeting #75 RP-170325
Dubrovnik, Croatia, March 6-9, 2017
Document for: Discussion
Agenda Item: 10.1.2

## Slide 2
Motivation
The explosion of video traffic now and in near future comes from:
more and more higher definition of the video content, e.g. from 720P to 1080P and 4K;
more and more new businesses based on video, especially real-time video, e.g. mobile surveillance, video conference and video direct broadcasting etc.
LTE is now the most popular platform to deliver these video contents. While LTE is not optimal designed for video delivery, 3GPP has started to consider the video related optimization in Rel-14, and further enhancements are expected to meet all the challenges in the future video dominated eMBB age.

## Slide 3
Motivation-1/4
Problem of uncompressed header
During an ongoing VoLTE session there are cases where the RoHC compressor may send uncompressed header. For example:
At the beginning of a session, as part of initial context establishment.
In case of VoLTE packet failures at PHY (after HARQ; no ARQ at RLC or application layer for VoLTE), the receiver may send RoHC feedback to notify a bad synchronisation of the RoHC context. The header compressor at the TX side transmits the full header information as part of the “Refresh and re-initialization” of the RoHC context.
In case of periodic refresh of the RoHC context, for instance when RoHC mode is uni-directional.
In the above cases the coverage of UL voice data transmission will be impacted, especially when the available UL bandwidth is limited. Existing mechanisms are not sufficient to improve the VoLTE performance when UL voice data carrying uncompressed header need to be transmitted.

## Slide 4
Motivation-2/4
QoS related enhancement to enable the differentiated handling of video data
The video data uses high compress ratio codec (e.g. H.264, H.265), which causes the importance of different video data parts to be quite different. For instance I-frame and RTCP packets for lost RTP packets are usually much more important than other frames(e.g. P-frames), and the loss of these critical data will result in a sequence of damaged pictures.
Currently in LTE these critical packets are transmitted on the same video bearer (GBR or non-GBR), which is neither resource efficient nor experience optimal for video transmission.
When the video bearer queue is highly loaded (e.g. in case of UL radio congestion) , these critical packet may be dropped, which will cause serious video quality degradation.

## Slide 5
Motivation-3/4
Long backhaul latency reduction for video
During the SI on Context Aware Service Delivery in RAN for LTE, RAN has identified issue related to long backhaul latency. The issue may arise in cases where the distance between the RAN and the node hosting the application content is long or the number of routers on this route is high.
In these cases long transportation latency may be experienced. Consequently certain kinds of service, such video, may be impacted significantly due to the long latency.
The study concludes that: the local caching can be used to address the issue on backhaul long latency. The local caching is feasible, if principle defined in section 5.1 of [TR 36.933] are respected. How to make it should be considered in the normative work with respect existing architecture.

## Slide 6
Motivation-4/4
Video transmission issue cases
During the SI on Context Aware Service Delivery in RAN for LTE, RAN has identified the video transmission issue. The Operator video is a video service under the LTE operator’s control. It is usually transmitted over a dedicated EPS bearer or using a dedicated QCI.
However, there might be cases where an operator decides not to apply any dedicated QoS to a video service. These video services are named “Over-The-Top” (OTT) video and are video services that LTE operators have no control on. Such service traffic is usually treated in the same way as normal internet traffic, e.g. transmitted via default bearer, which may lead to poor QoE.
It is also concluded that it may be beneficial for the UE to provide its buffer status to the RAN and it is up to RAN implementation on how to use such information for resource management optimisation. RAN2 should evaluate the benefits of this solution.

## Slide 7
Objectives of Work Item-1/3
Enhancement to improve the VoLTE performance when UL voice data carrying uncompressed header need to be transmitted[RAN2]:
  Specify mechanism(s) for a UE to detect and inform the network about UL voice data carrying uncompressed header.
  Specify mechanism(s) to separate the transmission of UL voice data carrying uncompressed header and compressed header.
  Specify mechanism(s) to decouple the user payload transmission and the uncompressed header transmission.
  Specify network configuration/control of the mechanism(s).

## Slide 8
Objectives of Work Item-2/3
Enhancement to solve the problem of critical data discard related to video transmission in order to improve the perceived video quality by the UE:
  Specify mechanism(s) for the UE access stratum to be aware that a PDCP SDU relates to upper layer critical data, e.g. using marking solution and application frame level identification [RAN2];
  Specify mechanism(s) for the UE L2 to be aware that a packet relates to upper layer critical data, and L2 differentiated handling for different prioritized video data [RAN2];
  Specify mechanism(s) for the UE L1 to be aware that a packet relates to upper layer critical data and multi-prioritized packet /service coexistence in one scheduling, pre-emptive scheduling within retransmission and other L1 differentiated handling for different prioritized video data [RAN1].
  Specify mechanism(s) for the eNB to be made aware that the UE has upper layer critical data within its buffers so that the eNB can take the information into account in UL scheduling decisions. [RAN2, RAN1]
  Specify network configuration/control of the mechanism(s). [RAN2]

## Slide 9
Objectives of Work Item-3/3
Long backhaul latency reduction for Video service. Specify solution for local caching for UE assistance video request
  How UE to provide any assistance information to RAN, e.g., based on service type. [RAN2]
  How RAN should perform UE eligibility check to guarantee UE credibility/integrity. For example the eligibility check may be achieved by new S1 procedure or reuse existing S1 procedure with new IE. [RAN2, RAN3]
  Analyse potential impact of UE mobility on the local caching solution to avoid additional UE eligibility check for UE in mobility state between different eNBs. E.g., whether to transfer UE eligibility check information from source eNB to target eNB during HO. [RAN3]
  How to comply the principle defined in section 5.1 of [TR 36.933] with respect existing architecture. [RAN3]
  Note: the solution shall not rely on user data detecting and storing in the eNB;
UE video playout buffer status reporting [RAN2]
  Specify UE video buffer status (i.e. playout status and playout buffer status) reporting mechanism(s).

## Slide 10
THANK YOU