## Slide 1: Motivation for New Work Item on Further Enhanced LAA for LTE
Intel Corporation
RAN #75, Dubrovnik, Croatia, March 06-09, 2017
AI 10.1.1
RP-170430

## Slide 2: Motivation
Unlicensed spectrum and scheduled UL access are not a good match!
  Scheduled UL access in unlicensed spectrum has to go through multiple steps:
    UE to send SR
    LBT performed by eNB to send UL grant (especially in case of self-carrier scheduling)
    UE scheduling (internal contention amongst UEs associated with the same eNB)
    LBT performed only by the scheduled UE (susceptible to lose channel occupancy due to 4 ms latency)
LAA UL performance needs improvements.

## Slide 3: UL Autonomous Transmission
LAA UL performance improvement via Wi-Fi like simple UL access!
  UL autonomous transmission enables LAA UEs to embark channel sensing and transmission by themselves without a grant from eNB.
  Previously mentioned quadruple steps become one step UL access (sense and transmit).
  It will naturally well-coexist with neighboring WLAN as the channel access mechanism of autonomous UEs are not different from that of Wi-Fi STAs.
UEs autonomously start LBT and transmit, if having UL traffic.

## Slide 4: UL Autonomous Transmission
UL autonomous transmission can help to balance the UL performance between LAA and Wi-Fi.
  Indoor, DL:UL = 50%:50% traffic

## Slide 5: Objective
The detailed objectives of the work item are to specify for the following functionalities:
  UL autonomous transmission for LAA SCell(s) (with one or more UL carriers in unlicensed band) using Frame Structure type 3 [RAN1, RAN2, RAN4]
    Study and specify if necessary, support for partial/extended subframe.
    Study and specify if necessary, how to support link adaptation for autonomous PUSCH transmission including potential modifications on UCI.
    Study and specify if necessary, mechanism to detect the autonomous transmission.