## Slide 1: Way forward on V2X evolution for Rel-15 and beyond
Vodafone, Deutsche Telekom, Ericsson, Huawei, Nokia
RP-170450
3GPP TSG RAN#75
Dubrovnik, Croatia, 6th – 9th March 2017

## Slide 2: Background (1)
Motivation
The 3GPP LTE V2X feature completed in Rel-14 provides a solid foundation of V2V communications, including vehicle safety applications
There is a desire to provide an evolution path from this foundation by extending it step-by-step into the full 5G-V2X feature, with additional functionality to support new applications and use cases.
Requirements
Input from the automotive industry via 5GAA is expected in order to review and confirm the details and timeframes of the requirements provided by SA1;
Such input is expected to set the detailed requirements for the functionality specified in future releases of 3GPP V2X, as well as the timeframe / release in which each aspect is specified.

## Slide 3: Background (2)
Interoperability
3GPP-V2X terminals would continue to support the Rel-14 functionality in order to provide full interoperability for the original vehicle safety applications.
Meanwhile, vehicles supporting a given extension of a later Release will be able to exploit additional functionality (e.g. new features introduced) between them; communications using the new functionality would not be able to be received by legacy (Rel-14) UEs.
Co-existence and backward compatibility
For the additional functionality, different levels of compatibility / co-existence with the initial Rel-14 functionality can be identified:
  New functionality which can co-exist in the same resource pools as Rel-14 functionality, and use the same scheduling assignment format, which can be decoded by Rel-14 UEs, without causing significant degradation to Rel-14 V2V operation
  New functionality which would benefit from the use of different resource pools from Rel-14 V2V
  New functionality which would operate on a different carrier from Rel-14 V2V

## Slide 4: Proposal (1)
Step 1: Rel-15 work item for 3GPP V2X Phase 2
Starting: March 2017 (RAN#75)
Scope:
  New PC5 functionality which can co-exist in the same resource pools as Rel-14 functionality, and use the same scheduling assignment format, which can be decoded by Rel-14 UEs, without causing significant degradation to Rel-14 operation:
    Higher order modulation
    Carrier Aggregation
  Transmission latency reduction (reduced time between packet arrival at layer 1 and transmission on the radio)
  Coexistence between UEs using mode 3 and mode 4 resource provisioning
In addition, feasibility and gains of the following PC5 functionality can be studied assuming the features would co-exist in the same resource pools as Rel-14 functionality; subsequent to the conclusion of this study, a decision could be taken on whether or not to specify these features as part of this step.
  Tx diversity
  Short TTI

## Slide 5: Proposal (2)
Step 2: Rel-15 study item for 3GPP V2X Phase 3
Starting time for TU allocation expected to be mainly around December 2017;
RAN plenary could consider whether to approve this SI at the same time as the Rel-15 WI in Step 1, with the TU allocation starting later.
Tentatively comprising:
  New PC5 functionality that would benefit from having less design constraints than 3GPP V2X phase 2, and therefore benefiting from different resource pools on the same carrier or a different carrier from Rel-14 V2V
  Potentially some higher layer features
  Positioning using ranging (taking into account any advice from SA3)
Step 3: WI for 3GPP V2X Phase 3
Based on the outcome of the SI in step 2, consider starting a WI for 3GPP V2X Phase 3 after completion of the SI (e.g. in Rel-16), if a need is identified.