## Slide 1: Motivation for work item on NB-IoT operation in unlicensed spectrum
Ericsson
RAN #75, Dubrovnik, Croatia, March 6 - 9, 2017
AI 10.1.1
RP-170510

## Slide 2: 3GPP NB-IoT technology
Rel-13/14 NB-IoT
  Supports diverse use cases
  Huge 3GPP-powered eco system
  Designed for licensed spectrum operations
  Achieves highest quality of services
MTC/
IoT
Smart metering Smart grid management
UTILITIES
Fleet Management Goods tracking
TRANSPORT & LOGISTICS
Smart parking Smart bicycles
SMART CITIES
Smoke detectors Alarm systems Home automation
SMART BUILDINGS
Wearables Kids/Elderly tracker Medical monitoring
CONSUMERS
Process monitoring & Control
INDUSTRIAL
Waste management City lighting
Maintenance monitoring

## Slide 3: 3GPP NB-IoT in unlicensed spectrum
Several LPWAN technologies using unlicensed spectrum are already deployed.
  Well proven business case.
Opportunities for 3GPP systems to use NB-IoT in unlicensed spectrum
  Supplement spectrum holdings in different geographical markets
  Reduce licensed carrier loads
    Offloading low power (e.g. 14 dBm) devices or low priority traffic to unlicensed bands.
  Complement existing infrastructure for new use cases
    E.g., smart agriculture or forest monitoring in extreme rural areas.
Increase NB-IOT eco system which helps lower cost
MTC/
IoT
Smart metering Smart grid management
UTILITIES
Fleet Management Goods tracking
TRANSPORT & LOGISTICS
Smart parking Smart bicycles
SMART CITIES
Climate-Agriculture monitoring Live stock tracking
AGRICULTURE
Smoke detectors Alarm systems Home automation
SMART BUILDINGS
Flood monitoring & alert Environmental monitoring (Water, air, noise, etc)
ENVIRONMENT
Wearables Kids/Elderly tracker Medical monitoring
CONSUMERS
Process monitoring & Control
INDUSTRIAL
Waste management City lighting
Maintenance monitoring

## Slide 4: Standalone versus License-Assisted
 | Standalone | Licensed-assisted
Enable more use cases and deployments | Yes | No
Expand operators spectrum asset | Yes | Yes
Offloading | DL and UL | Only UL
Fill in coverage hole | Yes | No
Standalone mode offers higher values

## Slide 5: Objectives for uNB-IoT WI
Prioritize and identify suitable operating bands in unlicensed spectrum below 1 GHz.
  The US ISM band 902-928 MHz, and European SRD band 863-870 MHz may serve as good examples.
  Prioritize bands that do not require LBT.
  This does not preclude operation in further bands in later releases.
Adapt standalone NB-IoT operations to relevant unlicensed spectrum regulatory requirements
  Reuse existing NB-IoT designs as much as possible to benefit from existing eco system.
  Solutions should be band-agnostic to the maximum extent possible.

## Slide 6
3GPP mMTC technology suite
Based on Release 13
PERFORMANCE
COVERAGE/ BATTERY
LTE CAT-1
(with EC, PSM, eDRX)
LTE CAT-M1
(with EC, PSM, eDRX)
EC-GSM-IoT PSM + eDRX
NB-IOT CAT-N1 + PSM + eDRX
VEHICLE/ASSET TRACKING
Unlicensed LPWAN
100 bps
1 Mbps
10 Mbps
10+ years
ENVIRONMENT MONITORING
10 km
10s kbps
VOICE SERVICES CONNECTED ELEVATORS
KIDS/ELDERLY/PET/VIP TRACKING
SMART GRID MANAGEMENT
<$5
Use case DIVERSITY
SMART METERING, SMART BUILDING, HOME AUTOMATION
SMART CITY LIGHTING, WASTE MANAGEMENT
NB-IoT-U will cover any claimed gaps, if existing, between 3GPP and unlicensed LPWANs.
Notes: 2016-03-23
6
Concept and status report for M2M: Narrowband LTE
No single technology can cover all IoT use cases, in addition to the three technologies just mentioned.
We are also seeing a large interest in LTE Cat-1. Cat-1 was standardized in release 8 and was intended to be the least complex LTE chipset category. Therefore it has been shown to be a good starting point for IoT applications in LTE networks and a gap filler for some IoT use cases, but a complement for other use cases with more higher expectations on performance. It has data rates at 10 Mbps in the downlink. Power saving mode (PSM) is applicable to all 3GPP based technologies and together with extended discountinous reception (eDRX) it helps to reach 10 years battery life time for diverse use cases.
Furthermore we also have a number of technologies operating in unlicensed spectrum already available on the market. Two examples are Sigfox and LoRa. With operation in unlicensed spectrum follows certain restrictions such as lower transmit power and antenna gain than in licensed spectrum which limits coverage. Furthermore there is no way of controlling which other deployments and technologies with which the spectrum is shared long term; making it more challenging to guarantee the reliability of the network as well as provide quality of service. These solutions therefore work best when confined to local areas where the risk of interference is minimized, while cellular is better able to provide quality of service at long range because of using licensed spectrum. In unlicensed spectrum there is also restrictions on how to access the spectrum to allow fair sharing which restricts capacity primarily in the downlink and can be limiting for certain use cases.
Cat-M1, NB-Iot and EC-GSM-IoT can reuse existing 3GPP network footprints, e.g., LTE and GSM hardware respectively, and only requires new software. Management systems etc can be reused which reduces the operational costs and the time for roll out.
2016-05-30
6

## Slide 8: Example band: US 902-928 MHz
Observation: frequency hopping over 50 channels maximizes transmit power while retaining NB-IoT channel BW per hop
 | Channel BW | # of hopping channels | Dwell time | EIRP
Frequency Hopping | < 250 kHz | 50 | 0.4 s per 20 seconds | 36 dBm
Frequency Hopping | > 250 kHz | 25 | 0.4 s per 10 seconds | 30 dBm
Digitally Spread | 500 kHz | No restriction | No restriction | 36 dBm
Other | No restriction | No restriction | No restriction | -1.23 dBm
 | Channel BW | # of hopping channels | Dwell time | EIRP
Frequency Hopping | < 250 kHz |  | 0.4 s per 20 seconds | 36 dBm
Frequency Hopping | > 250 kHz |  | 0.4 s per 10 seconds | 30 dBm
Digitally Spread |  | No restriction | No restriction | 36 dBm
Other | No restriction | No restriction | No restriction | -1.23 dBm
Support for uNB-IoT UL and DL

## Slide 9: Example band: EU 868 MHz
Observation: stringent BW limits and duty factor requirements.
Note: ERP = EIRP – 2.15 dB
 | Channel BW | Duty Cycle | ERP
868-868.6 MHz | No limit | < 1% | 14 dBm
868.7-869.2 MHz | No limit | < 0.1% | 14 dBm
869.3-869.4 MHz | <25 kHz | No limit | 10 dBm
869.4-869.65 MHz | <25 kHz | < 10% | 27 dBm
869.7-870 MHz | No limit | No limit | 7 dBm
1 uNB-IoT DL carriers
Up to [3] uNB-IoT UL carriers