## Slide 1: Motivation for WI on Architecture Evolution for E-UTRAN
China Unicom, Orange, China Telecom, Huawei, HiSilicon
3GPP TSG RAN Meeting #75
Dubrovnik, Croatia, Mar 6 – 9, 2017
Document for: Discussion
Agenda Item: 10.1.3
RP-170729

## Slide 2: Motivation
There would be one high layer option for NR CU and DU function split, which should be standardized in stage 2 and stage 3 in normative phase.
To achieve better integration of the LTE eNB with gNB, the converged architecture for LTE and NR is preferred.
    The higher layer split of LTE CU/DU could well support for tight interworking between LTE and NR.
    This architecture will utilize the transport network in an efficient way and minimize the impacts on legacy LTE transport network.
    It is easier for further network upgrading when LTE CU/DU deploy in operator’s network.
  To fulfil with operator NR deployment schedule, the LTE architecture evolution should be finalized within the time line of R15
Fig.1 A simplified architecture for LTE CU/DU split

## Slide 3: Scope of new WI
To make the progress of standardization, a short-term study phase is started first and the detailed objectives of the study item (to be completed by RAN#76) are:
  Confirm the requirements and deployment topology of LTE CU/DU functional split for a network containing LTE and NR;
  Select the preferred architecture option to use in the above deployment topology, with the aim to support the converged architecture for LTE and NR considering option 2 i.e. PDCP/RLC split as the baseline;

## Slide 4: Scope of new WI (Cont.)
After the short-term study item, the work item phase should work on specifications and detailed objectives of the work item are:
  Specify the higher layer function split architecture, functionalities, interface for LTE-CU and DU
    Specify the higher layer functions split for LTE CU and DU;
    Specify the interface and relative functionalities to support CP and UP between LTE CU and DU;
  To align with the NR CU/DU higher layer split progress, specify the enhancements on the coordination between LTE-CU and NR-CU
    Specify the interface and relative functionalities both CP and UP between LTE CU and NR-CU;
  Specify the possible function improvements, including but not limited to
    Intra-system and inter-system mobility handling
    Positioning
    …

## Slide 5: WI time budget proposal
leading WG | WI or SI | Title | latest WID/SID | rapporteur | REL | target | 75 March17 REL-14 freeze | 88bis | 97bis | 95bis | 82bis | 82bis | 89 | 98 | 96 | 83 | 83 | 4 | 76 June17 | 90 | 99 | 97 | 84 | 84 | 5 | 77 Sep.17 | 90bis | 99bis | 97bis | 84bis | 84bis | 91 | 100 | 98 | 85 | 85 | 6 | 78 Dec.17
RAN3 | SI | Architecture Evolution for E-UTRAN |  | China Unicom | R15 | Sep. 17 |  |  |  | 1 |  |  |  |  | 1.5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
RAN3 | WI | Architecture Evolution for E-UTRAN |  | China Unicom | R15 | Jun. 18 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 1.5 |  |  |  |  |  | 1 | 1.5 |  |  |  | 1 | 1.5 |  |  |  | 
92 | 101 | 99 | 86 | 86 | 7 | 79 March18 | 92bis | 101bis | 99bis | 86bis | 86bis | 93 | 102 | 100 | 87 | 87 | 8 | 80 June18 REL-15 freeze
 | 1 | 1.5 |  |  |  |  |  | 1 | 1.5 |  |  |  | 1 | 1.5 |  |  |  |