## Slide 1: Motivation for new SI on NR SON
CMCC, Nokia, Samsung
3GPP TSG-RAN Meeting #76
West Palm Beach, USA, June 5 - 8, 2017
Document for: Approval
Agenda Item: 9.1
RP-170994

## Slide 2: LTE: lessons learned (1)
Early system deployments:
  Fewer base stations, at bigger distances
  Not much experience in practical coverage availability (e.g. terminal capabilities)
  Unstable terminal implementations
Consequences:
  Manual planning of the network is much more time consuming and still produces many errors in terms of mobility and neighbour configuration
  Fewer base station population is more likely to be overloaded

## Slide 3: LTE: lessons learned (2)
SON proved to help operators mitigate problems of first deployments of LTE:
  Problems with network planning: PCI allocation and ANR
  Problems with the mobility configuration: MRO
  Problems with limited coverage: MRO
  Problems with load distribution: MLB
It is expected that similar situation will be faced when NR is deployed!
Hence, similar SON functionality is needed for NR!

## Slide 4: Proposals for NR
The use cases based on the experience of LTE shall be the starting point for the study:
  Automation of cell ID allocation and of neigbour relations mapping
  Automation of mobility configuration and its correction
  Automation of load balancing
However, NR brings about a few new features. Therefore:
  RAN network slicing shall be taken into consideration when discussing the use cases
  CU-DU split shall be considered where applicable, e.g. with the study on the automation of the mobility configuration
If any completely new use case is found during the study, it shall be addressed, too.

## Slide 5: Proposed schedule
It is prefferable to start the study in paralel to the NR WI
  It enables offering SON benefits to operators sooner
  It helps avoiding creating limitation in the NR; for example adding features needed for SON is easier at early stages of the system development
Therefore, we propose to start the NR SON SI in paralel to the first NR WI
However, the NR SON SI is planned until the end of the year to be able to take into account the agreements made in the NR SI and WI

## Slide 6
Thank you!