## Slide 1: 3GPP TSG RAN Meeting #77 RP-171795 Sapporo, Japan, September 11 - 14, 2017
Agenda Item: 9.3.2
Source: ZTE, Sanechips
Title: Calibration work for self-evaluation SI
Document for Discussion

## Slide 2: NR MIMO calibration
The 3-Phase NR MIMO calibration is organized for evaluation of NR MIMO features in NR SI. A CR R1-1715256 has been submitted to RAN1#90 to update results in TR38.902 which is expected to be the final update.
  Phase 1: Calibration is to check the link and system level channel models with basic beamforming behavior in terms of SNR/SINR distribution. Link level evaluation assumptions for this item can be found in R1-1701823. Link level calibration results for this item can be found in R1-1715252. System level evaluation assumptions for this item can be found in R1-1703534. System level calibration results for this item can be found in R1-1715251.
  Phase 2: Calibration is to check the link/system level performance through observing the metrics of BLER, spectrum efficiency and outage. Link level evaluation assumptions for this item can be found in R1-1703535. Link level calibration results for this item can be found in R1-1715254. System level evaluation assumptions for this item can be found in R1-1703536. System level calibration results for this item can be found in R1-1715253.
  Phase 3: Calibration is to check the additional link (if necessary)/system-level features including UE movement, UE rotation and channel blockage in terms of coupling loss, ASA, SINR and spectral efficiency. System level evaluation assumptions for this item can be found in R1-1701828. System level calibration results for this item can be found in R1-1715255.
Observation 1: Further calibration effort can be done in the self-evaluation SI on top of this NR MIMO calibration.

## Slide 3: The scope of calibration works for self evaluation
Channel calibration: InH_x, Umi_x ,UMa_x and RMa_x (defined in ITU report M.[IMT-2020 EVAL])
  RMa_x: It has higher complexity than before. Because of introducing Rural-eMBB Low mobility large cell(LMLC) in ITU, the range of path loss is different from 36.873, 38.900 and 38.901.
Observation 2: It is suggested to carry out calibration on RMa and other missing scenarios.
 | x=a |  | x=b
Available frequency range | 0.5-6 GHz | 6-100 GHz | 0.5-100 GHz
InH_x | 36.873 | 38.901 | 38.901
UMa_x | 36.873 | 38.901 | 38.901
UMi_x | 36.873 | 38.901 | 38.901
RMa_x | 36.873 |  | 38.901 [0.5-30GHz]

## Slide 4: The scope of calibration work for self evaluation
Calibration on uplink
  SLS and LLS of some test environments have been calibrated in the NR MIMO for eMBB on DL only.
  Uplink calibration for uplink system performance:
    UL system calibration is not included in the NR MIMO calibration
    In order to follow initial submission and ITU requirements, we should evaluate UL performances as well as DL.
    This is necessary for some features e.g. evaluate the influence of uplink sharing between LTE(e.g. 900MHz) and NR (e.g. 3.5GHz).
Calibration on Link to system mapping (L2S) for SLS
  Provided that channel coding (e.g. LDPC for eMBB) is stable, L2S calibration work can be kicked off.

## Slide 5: Initial calibration results for RMa_x
Observation 3: In ITU, Both Rma_x(x=a) and Rma_x(x=b) are similar.
Observation 4:To have more calibration across companies for Rural and other test environments; and more detail will be discussed in the RAN1.

## Slide 6: Simulation assumptions for RMa_x
Parameters | Assumptions | Parameters | Assumptions
Carrier frequency for evaluation | 700MHz /4GHz | BS noise figure | 5dB
Mode | DL only | UE noise figure | 7dB
Channel Model | RMa_X (36.873 and 38.900) | Thermal noise level | -174dBm/Hz
BS antenna height | 35m | UE density | 10 UEs / TRxP
Total transmit power per TRxP | 49 dBm for 20 MHz; 46 dBm for 10 MHz | UE antenna height | 1.5m
Inter-site distance | 1732m | Percentage type | 100% lowloss
Device deployment | 50% indoor, 50% outdoor (in‑car) Randomly and uniformly distributed over area | UE speeds of interest | Indoor users: 3km/h; Outdoor users (in-car): 120 km/h;
Note: All simulation assumption are follow report ITU-R M.[IMT-2020 EVAL]

## Slide 7: Proposal
Proposal 1: Considering workload, the NR MIMO calibration should be reused and continue in this self-evaluation SI at least for eMBB.
Proposal 2: A new set of calibration is set up in this SI which are not covered by NR MIMO calibration, including at least rural test environment, uplink SLS and link-to-system (L2S) mapping.

## Slide 8: Thank you