## Slide 1
Some more scenarios and objectives to be considered in the NR positioning SID proposal
CMCC
3GPP TSG RAN Meeting #77 RP-171845
Sapporo, Japan, Sep 11- 14, 2017
Agenda item: 9.1

## Slide 2: Background
Positioning Market aspect
  Positioning for eMBB: Location-based service (LBS) is already popular in normal life. Positioning ability has been a crucial factor for operators to improve user experience
  Positioning for vertical industry: Emerging 5G deployment for vertical industries, such as URLLC services (ground vehicle, drone, etc), smart home, factory monitoring, also demands improved positioning performance in those scenarios.

## Slide 3: Observations
Positioning technical aspect
  Study on positioning technologies should focus more on challenging scenarios and strive to combat the bottleneck factors to meet the higher positioning accuracy and latency requirement
  In this contribution, challenging scenarios are additionally proposed from operator perspective

## Slide 4: Outdoor deployment scenario 1
Use case 1-1: Ground Cellular UE Positioning
Use case 1-2: Stationary UE Positioning
Challenging factor:
GNSS coverage are not always available, especially in NLOS environment due to shadowing
Timing estimation accuracy is limited in NLOS
Challenging factor:
Extreme high accuracy in stationary scenario, such as monitoring building tilt angle to detect
Requirement:
Accuracy of [5]m under outdoor NLOS environment for conventional ground UE
Requirement:
Extreme high accuracy of millimeter level
sensor
sensor
Monitoring building tilt angle to early warn geological hazards
For network planning optimization
Location based service
Scenario 1: Outdoor UE positioning via Outdoor Base stations

## Slide 5: Outdoor deployment scenario 1
Remote sensing
Agricultural irritation and monitoring
Logistics delivery
Use case 1-3: Ground Vehicle Positioning
Use case 1-4: Drone UE Positioning
Challenging factor:
High speed UE, with up to 250km/h
GNSS coverage are not always available, especially in NLOS environment due to shadowing or in tunnels
Challenging factor:
High Doppler
Vertical domain positioning
GNSS coverage are not always available, especially during taking off and landing, or surrounded by buildings
Requirement:
High accuracy of 0.5m-1m under outdoor NLOS and high Doppler environment
Automotive industry partners expect more reliable and GNSS-independent positioning technologies
Requirement:
Accuracy of 0.1m for agricultural monitoring or logistics delivery by 2020
Accuracy of 1m for surveillance, entertainment, etc by 2020

## Slide 6: Outdoor deployment scenario 1
Bottleneck Problem:
  Timing estimation is not accurate enough in NLOS environment due to shadowing
  3D positioning accuracy especially vertical domain positioning accuracy was not guaranteed
  High doppler and fast position change due to higher speed of vehicular and drone UEs poses more challenges for accurate positioning
Corresponding objectives:
  How NR new features, including massive antenna, large bandwidth, flexible numerology can improve performance in outdoor scenarios
  Study specific solutions for outdoor high Doppler cases and 3D-positioning, as well as extreme high accuracy solutions in stationary scenario
    Study both RAT-dependent and hybrid positioning, including IMU/mmWave radar, and combination of high-resolution mapping etc, to reduce the dependency on GNSS

## Slide 7: Outdoor deployment scenario 2
Use case: Residential area, emergency searching, etc,
where indoor BS coverage are limited
Requirement： [3-5]m in horizontal, and [3]m (storey level) in vertical domain
Bottleneck Problem:
  Indoor access points may not be deployed or available, only outdoor base stations are available
  Low received signal strength due to high penetration loss
  Inaccurate timing estimation due to complex diffraction and reflection environment
  GNSS coverage is limited
Corresponding objectives:
  How NR new features, including massive antenna, large bandwidth, flexible numerology can improve performance in such scenarios
Scenario 2: Indoor UE positioning via Outdoor Base stations

## Slide 8: Indoor deployment scenario
Challenging factor:
GNSS coverage are limited for indoor scenario
Indoor small cell deployment limits the use massive MIMO antennas
Typical access points are many distributed RRU connecting to a single BBU of or even passive antennas
Expectations:
Accuracy of [1]m under indoor LOS and low moving environment
Relaxed accuracy of [3-5]m in horizontal, and [3]m (storey level) in vertical domain under other environments
Use cases:
Shopping mall, for identifying , ad pushing, etc
Smart home
Scenario 3: Indoor UE positioning via Indoor Base stations

## Slide 9: Indoor deployment scenario
Bottleneck Problem:
  GNSS coverage is limited
  Complex indoor environment due to diffraction and reflection
  Small cells are typically deployed thus limiting the usage of massive MIMO antennas
  Current techniques cannot perform positioning for passive antenna systems
Corresponding objectives:
  Identify benefit of large bandwidth to indoor positioning accuracy
    Positioning accuracy for band-limited UEs and possible solutions
  Study specific solutions for distributed RRU or indoor passive antennas

## Slide 10: Summary of scenarios and expectations
Urban or suburban macro cell deployments, including
  Outdoor deployment scenario targeting outdoor UEs, supporting high accuracy 3D and high Doppler positioning under both LoS and NLoS condition, and possibly extreme high accuracy in stationery environment
    R-1: Accuracy of [5]m under outdoor NLOS environment for conventional ground UE
    R-2: Extreme high accuracy of millimeter level in stationary environment
    R-3: High accuracy of 0.5m-1m under outdoor NLOS and high Doppler environment for ground vehicles
    R-4: Accuracy of [0.1]m for agricultural monitoring or logistics delivery by 2020
    R-5: Accuracy of [1]m for surveillance, entertainment, etc by 2020
  Outdoor deployment scenario targeting indoor UEs, supporting the ability to locate UE under complex indoor reflection environments
    R-6: [3-5]m in horizontal, and [3]m (storey level) in vertical domain
Indoor small cell deployments, including
  Indoor deployment targeting indoor UEs, supporting very high positioning accuracy in LoS condition and proper performance under complex indoor reflection environments
    R-7: Accuracy of [1]m under indoor LOS and low moving environment
    R-8: Relaxed accuracy of [3-5]m in horizontal, and [3]m (storey level) in vertical domain under other environments

## Slide 11: Proposed modification of SI objective
1. Evaluation on different positioning technologies [RAN1].
For RAT dependent technologies,
  Use the evaluation assumptions and scenarios in TR37.857 as a starting point including:
    Indoor and outdoor deployment scenarios covering but not limited to Urban and Suburban areas
        For outdoor macro deployment scenarios, both outdoor and indoor UE positioning should be supported, especially for indoor UE positioning where indoor access points may not be deployed or available
    System parameters including operating bands below and above 6GHz
    User dropping
    Performance metrics to evaluate vertical and horizontal positioning and the overall positioning accuracy and latency
        For outdoor deployment scenario targeting outdoor UEs, consider high accuracy 3D positioning accuracy under high Doppler and fast changing LOS and NLOS environment
        For outdoor deployment scenarios targeting outdoor UEs in stationary environment, consider extreme high positioning accuracy (millimetre level)
        For outdoor deployment scenarios targeting indoor UEs, accuracy of [3-5]m in horizontal, and [3]m (storey level) in vertical domain
  Define additional evaluation assumptions and scenarios, if needed.
    For outdoor deployment scenario targeting indoor UE positioning, consider the impact of indoor complex reflection environments besides impact of high penetration loss
    For indoor small cell deployment scenario, consider distributed RRU or even passive antenna deployment
  Evaluate the positioning technologies.

## Slide 12: Proposed modification of SI objective
2. Study of potential positioning solutions for RAT dependent technologies and hybrid of those to achieve the objectives in TR 38.913 and TS 22.261 [RAN1].
  For RAT dependent technologies, the study is based on measurement of NR signals for downlink and uplink transmission
    Sufficient leverage of massive MIMO for outdoor macro deployment scenarios
    Sufficient leverage of large bandwidth and flexible numerology for all scenarios, especially on achievable 3D-positioning accuracy in high Doppler scenario
      Evaluate the impact on band-limited users on achievable positioning accuracy
    Study specific solutions for distributed RRU and passive antennas
  For RAT independent or hybrid positioning technologies,
    For outdoor UE positioning, consider both combination with GNSS based techniques, as well as combination with IMU/mmWave radar, and high-resolution mapping etc, to reduce the dependency on GNSS
    For indoor UE positioning, consider combination with WLAN, IMU/Sensor and/or fingerprint mapping based positioning techniques

## Slide 13
Thanks !