## Slide 1: WF on scenarios prioritization for NR in Rel-15
Huawei, HiSilicon, Orange, Apple, MediaTek, CATT, CATR, China Unicom, China Telecom, III, Coolpad, ASTRI
3GPP TSG RAN plenary meeting #77 RP- 172018
Sapporo, Japan, 11 – 14 Sep, 2017
Agenda item: 9.2.1

## Slide 2: Background
For NR non-standalone deployments, design has been on-going for the following scenarios of LTE/NR dual connectivity (EN-DC option 3/3A/3X)
  Basic EN-DC
    NR in a new band (e.g. 3.5 GHz or mmw) with dense NR TDD deployment to ensure NR coverage. UE supports simultaneous LTE UL and NR UL in different frequency bands. Solutions identified to ensure NR-PUSCH coverage for small TB size design to carry RLC-feedback and CSI-feedback.
  EN-DC with non-simultaneous uplink
    For combinations of uplink carriers with intermodulation issues. Simple HARQ feedback timing adjustments already identified in WGs, TDM between NR UL and LTE UL ensured by scheduling.
  EN-DC with SUL (supplemental uplink)
    For reusing LTE macro sites for NR TDD deployment in a new band (e.g. 3.5 GHz band) while maximizing NR uplink coverage, maximizing DL capacity on the NR TDD carrier, improving latency. Solutions already identified in WGs: SUL RACH configuration, power control for path loss correction
  EN-DC with SUL and UL sharing from network perspective (LTE/NR coexistence)
    Using the UL portion of the LTE FDD band may be the only available placement of the SUL NR carrier, and allows for higher utilization of generally lightly loaded uplink spectrum. Resources are split between LTE UL and NR UL by proper network and UE configuration (e.g. configuring reserved resources). Subcarrier alignment and corresponding UL raster already been agreed in WGs.
  EN-DC with SUL and UL sharing from UE perspective (LTE/NR coexistence)
    Practical constraints on spectrum, coverage and CAPEX require a DC UE to support using the shared UL frequency for NR UL and LTE UL, especially when LTE coverage is ensured on a single LTE band. This scenario is more likely to be required in early deployments compared to #3 and #4 above.
    Additional impact: identification of UE RF/BB architectures, potential switching/transient times
Additional impact for all scenarios: RAN4 requirements for corresponding band combinations, some of which are already identified in RAN4

## Slide 3: Background
For NR standalone deployment, design has been on-going for the following scenarios:
  Basic NR standalone connected to 5G-CN
    Target June 2018
  NR standalone with a SUL carrier in a low frequency band
    Additional impact compared to EN-DC with SUL: RACH and power control configurations in RMSI, SUL PCell mobility. Band combinations with SUL already identified in RAN4.
  NR standalone with a SUL carrier and UL sharing in a LTE band (LTE/NR coexistence)
    No additional impact: reuse solutions for EN-DC with SUL in shared UL + NR SA with SUL carrier. Band combinations with SUL already identified in RAN4.
  NR standalone with DL sharing in a LTE band (LTE/NR coexistence)
    Impact already identified and solutions agreed in RAN1 (SS block, mini-slots, Xn/eX2 messages)

## Slide 4: Proposals
Specify support for SUL with and without UL sharing for both non-standalone and standalone deployments by Dec 2017
  Simultaneous operation of NR SUL and LTE UL by TDM on the shared bandwidth shall be supported from UE perspective, in addition to support from the network perspective in LTE/NR dual connectivity deployments
  For standalone NR with SUL with and without UL sharing, the Dec 2017 target is for L1/L2 aspects
Try to finish RAN4 spec for those Band combinations for supporting SUL with and without UL sharing before 2017 Dec
  If delayed at least by 2018 June