## Slide 1: Source: China Telecom, CATT
Motivation for Study on
Enhancement for High Layer CU-DU Split
3GPP TSG RAN Meeting #78 RP-172494
Lisbon, Portugal, December 18 - 21, 2017
Agenda Item: 9.1.3
Document for: Decision

## Slide 2: Background
For high layer function split, it was agreed to standardize option 2-1 in release 15. With the introduction of CU/DU split, some issues arise as follows:
  Intra-gNB/inter-DU handover would be very frequent which may introduce extra interruption time
  For inter-DU duplicated transmission/fast re-transmission, there may be unnecessary resource utilization
  Intra-gNB CA could not be supported if the two cells are located in different DUs
Furthermore, there are some new requirements in further 5G network deployment, the enhancement for high layer CU/DU split should be studied in Rel-16
Enhancement for HL CU/DU
handover interruption time
Support of inter-DU CA
Multiple Connectivity
Reduction of radio resource utilization

## Slide 3: Minimization of inter-DU handover interruption time
  The interruption time during inter-DU handover procedure would impact the system performance seriously
    Scenario : Since NR cell would be deployed in HF with continuous coverage, the handover between DUs may happen frequently
  5G KPI Requirement for Mobility interruption time(TR38.913)
  The interruption time means the shortest time duration supported by the system during which a user terminal cannot exchange user plane packets with any base station during transitions.
  The target for mobility interruption time should be 0ms.
How to reduce the handover interruption time for inter-DU scenario should be studied

## Slide 4: Reduction of radio resource utilization
Inter-DU duplicated transmission
  It is agreed in RAN2 meeting that duplicated transmission should also be supported.
  For duplicated transmission within two DUs, duplicated resources would be allocated to the UE which maybe unnecessary, especially for DRB with AM mode.
  For intra-CU/inter-DU duplication scenario, if some RLC PDU segments are lost in one leg, currently, the whole PDCP PDU will be re-transmitted in another leg. However, it is possible that other part of the data which share the same PDCP SN has already been transmitted successfully in the first leg. In this case, it is not necessary to re-transmission these data to save radio resources.
The reduction of radio resource utilization for duplicated transmission and fast re-transmission should be considered.

## Slide 5: Support of inter-DU CA
CA is also supported in NR era
With the introduction of CU/DU split, there may be cases that two adjacent DUs have overlapping coverage and so they may have the chance to aggregate for better performance.
Considering the coverage performance of sub-6 GHz is much more than that of above 6GHz, therefore the inter-DU CA scenario will be also existed in 5G era.
Further enhancement on how to support inter-DU CA is needed

## Slide 6: Support of multiple DUs connectivity
Currently, one gNB may include multiple DUs, it is not supported for one UE to connect to two or more gNB-DUs at the same time.
However, considering the requirement of 5G,i.e.the target for peak data rate should be 20Gbps for downlink and 10Gbps for uplink, it is beneficial that UE could utilize the resources in two DUs to enable the high rate data transmission.
Support of multiple DUs connectivity should be considered.

## Slide 7: Objective of this SI
The objectives of this SI are to:
  Identifying detailed solutions to minimize the interruption time of inter-DU handover.
  Identifying detailed solutions to minimize the utilization of radio resource for inter-DU duplicated transmission /fast re-transmission.
  Identifying detailed solutions to support intra-gNB/inter-DU CA to aggregate radio resources from two DUs for better performance.
  Identifying detailed solutions to support multiple DUs connectivity for EN-DC/NGEN-DC scenario.
  Study the necessary protocol functions and/or messages related to the possible identified solutions.
Time Budget: Mar,2018~Dec,2018

## Slide 8
THANKs FOR YOUR ATTATION
Notes: 模板来自于 http://docer.wps.cn