## Slide 1: 3GPP TSG RAN Meeting #79 Chennai, India, March 19 - 22, 2018 Agenda item: 10.1.1 Document for: Discussion
On Rel-16 eMTC scope
RP-180357

## Slide 2: Further eMTC evolution in Rel-16
Guideline in Rel-16 eMTC work:
System efficiency enhancement
Power consumption enhancement
Coverage extension enhancement
Positioning enhancement
Connectivity to 5GC

## Slide 3: System efficiency enhancement for eMTC
Enhancement for standalone eMTC
  Study the suitable scenario for standalone eMTC, e.g, for scenario that co-exists with NR
  Supported bandwidth
  Removal of reserved legacy PDCCH area will allow more capacity improvement
  Control channel MPDCCH narrowband (1.4Mhz) support
Dynamic HARQ timing for eMTC
  Current pre-configured UL/DL HARQ timing negatively impacts system scheduling performance, introduction of dynamic HARQ timing can reduce blocking
  Improve resource utilization
Multi-subframe scheduling support for eMTC
  Further reduction in control overhead

## Slide 4: Further power consumption enhancement
SC-PTM enhancement
  Reduce redundant reception on UE and unnecessary power consumption due to repetition without feedback or without differentiation for the first time transmission and the repeated ones
RRC connected and idle mode power consumption enhancement
  Connected mode MPDCCH detection optimization
  Reduce idle mode power consumption with enhancement on paging , i.e., with additional consideration on stationary or low-mobility UEs, or with trade-off between paging reliability and minimum repetition numbers
  Reduce idle mode power consumption for mobility measurement, i.e, measurement optimization for mobility UE

## Slide 5: Coverage Extension Enhancement
Target small portion of the deployed UE in deep coverage hole and low power class UE
  Existing coverage extension methods still cost heavy power consumption
Coverage can be extended via in-coverage relay node
  Focus on single-Hop Relay
    Minimize legacy network impact
    Considering different relay node scenario

## Slide 6: Positioning enhancement
Rel-14 eMTC only supports basic OTDOA positioning functions. However, the bandwidth of the PRS limits the accuracy that can be achieved
Positioning enhancement
  UTDOA support
  Positioning accuracy improvement
  Positioning power consumption reduction

## Slide 7: eMTC eNB connectivity to 5GC
Connectivity to 5G Core Network for the eNB supporting eMTC
  Support for 5G-CN functions, e.g.:
    Flow based QoS.
    New security scheme (if any).
  Simultaneous support for UEs connected to EPC and UEs connected to 5G-CN in the same cell
  Enhancements for core network node selection functions, e.g. assist to perform initial NAS selection and NAS routing

## Slide 8: Thank you