## Slide 1: Summary of email discussion on LTE enhancements (other than IoT, MIMO, broadcast)
Source: SoftBank (Email discussion moderator)
3GPP TSG RAN Meeting #80
La Jolla, CA, USA, 11th – 14th June 2018
Agenda Item: 10.1.1
Document for: Discussion
RP-180757

## Slide 2: Outcome of email discussion
Item | Contact company | Motivation & Goal | Draft WID/SID
Uplink enhancements for WTTc | Huawei | Confirmed | Ready but not so stable RP-180762
HRLLC enhancements | Ericsson | Not confirmed | Not available
Aerial Vehicles | Huawei | Not confirmed | Not available
even further mobility enhancement | China Telecom | Confirmed | Ready and almost stable RP-180762
Advanced receivers for LTE V2X | Intel | Confirmed | Ready and stable RP-180763
High speed scenario | NTT DOCOMO | Confirmed | Ready but need to resolve some issues RP-180764
Low Complexity 4Rx | Qualcomm | Confirmed | Not available
WID/SID proposals for 4 items are ready!

## Slide 3: Time Budget
 |  | 3Q 2018 |  |  |  |  | 4Q 2018 |  |  |  |  |  |  |  |  |  | 1Q 2019 |  |  |  |  | 2Q 2019 |  |  |  |  |  |  |  |  | 
 |  | R1 | R2 | R3 | R4RF | R4RD | R1 | R2 | R3 | R4RF | R4RD | R1 | R2 | R3 | R4RF | R4RD | R1 | R2 | R3 | R4RF | R4RD | R1 | R2 | R3 | R4RF | R4RD | R1 | R2 | R3 | R4RF | R4RD
Title |  | 94 | 103 | 101 | 88 | 88 | 94bis | 103 bis | 101 bis | 88bis | 88bis | 95 | 104 | 102 | 89 | 89 | 96 | 105 | 103 | 90 | 90 | 96bis | 105 bis | 103 bis | 90bis | 90bis | 97 | 106 | 104 | 91 | 91
LTE uplink enhancements for WTTc | Dec 2018 | 2 |  |  |  |  | 2 |  |  |  |  | 2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Core part: even further Mobility enhancement in E-UTRAN | Mar 2019 |  | 1 | 1 |  |  |  | 1 | 1 |  |  |  | 1 | 1 |  | 1 |  | 1 | 1 |  | 1 |  |  |  |  |  |  |  |  |  | 
Perf. Part: even further Mobility enhancement in E-UTRAN | Mar 2019 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 |  |  |  |  | 1 |  |  |  |  |  |  |  |  |  | 
Study on Advanced Receivers for LTE V2X | Jun 2019 |  |  |  |  | 1 |  |  |  |  | 1 |  |  |  |  | 1 |  |  |  |  | 1.5 |  |  |  |  | 1.5 |  |  |  |  | 1.5
Core Part: Further performance enhancement for LTE in high speed scenario |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Perf. Part: Further performance enhancement for LTE in high speed scenario |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Not ready
Note: Confirmation by WG chairs has not been finished

## Slide 4: Uplink enhancements for WTTc

## Slide 5: eUL - motivation & goal
Motivation - confirmed through the email discussion
  For DL, optimization for stationary UEs such as CPE type UEs was performed in Rel-15. Similar optimization should be considered for UL.
Goal - confirmed through the email discussion
  Study the potential enhancements for UL taking into account the characteristics of stationary UEs such as CPE type UEs (i.e.no battery issue, non-stringent size limitation etc.)
  The gain and standard impact shall be analyzed

## Slide 6: eUL – moderator’s proposal
Result of discussion on SID objectives
  SID is not so stable
    Positive comments from two operators
    Concerns from three companies
      Unclear potential solution, scenario and task for each WG
Moderator’s proposal
  Offline discussion to address the concern above
    A motivation paper is available (RP-180879, Huawei)… online discussion would also help the progress
  Update the SID, if necessary
  Ask RAN to treat this SID when it is ready

## Slide 7: eUL - Current objective of the SID (for information)
To study techniques for enhancing the uplink of stationary UEs, including the specification impact (RAN1, RAN2, RAN4)
  [Enhanced uplink SU/MU MIMO schemes for capacity enhancements such as codebook extension and non-codebook-based precoding. ]
  [More accurate uplink channel measurement and uplink CSI acquisition]
  [Overhead reduction of uplink reference signals for slow-varying channels ]
  [Special improvement for the users with poor link quality, such as enhancements to inter-cell coordination techniques]
Both types of UEs with and without high power are assumed. For high power UEs, 26 dB Tx power is assumed

## Slide 8: HRLLC enhancements

## Slide 9: HRLLC enhancement – motivation & goal
Motivation and Goal : not confirmed
  No consensus achieved because each company has each own view

## Slide 10: HRLLC enhancement – identified issues
Identified issues during email discussion
  IMT-2020 requirement
    Whether or not IMT-2020 requirement is fully satisfied by Rel-15 HRLLC (e.g. TDD)
    Whether or not Rel-15 HRLLC features need to be enhanced to make them more useful
  Beyond IMT-2020 requirement
    Whether or not LTE need to satisfy (part of) URLLC requirement beyond IMT-2020 (i.e. defined by SA)
      See next slide for more detail

## Slide 11: HRLLC enhancement – identified issues
  LTE HRLLC beyond IMT-2020 requirement
  It is a common understanding that the requrements are mainly achieved/served by NR. The LTE HRLLC could be as subset/comprement of NR URLLC.
  The question is to what extent LTE should satisfy the URLLC requirement beyond IMT-2020.
  Through the email discussion, no company has provided information to justify the necessity, for instance:
    (1) Constraint to deploy NR URLLC to a certain localized/specialized area,
    (2) Necessary functionality to satisfy the requrement, and
    (3) The achievable benefit (gain) and the specification impact especially on the lower layer
    (4) Urgency to specify something in Rel-16

## Slide 12: HRLLC enhancement – moderator’s proposal
Moderator’s proposal
  The interested compapnies are encouraged:
    to input their individual contributions to RAN#80 to address the issues above, and
    to continue offline difcussion aiming at the progress and WI/SI approval in RAN#81.
   Tdocs are available for this meeting
    RP-181031 from Ericsson (different A.I)
    RP-180882, RP-180883 from Huawei
    RP-181184, RP-181185 from Vodafone

## Slide 13: Aerial VEHICLES

## Slide 14: Aerial – motivation & goal
Motivation and Goal are not confirmed
  No consensus achieved because each company has each own view
Issues to be resolved
  (1) Commonarity between LTE and NR to support aerial UEs, and the possibitity to have a joint discussion
    Features for drone operaton: e.g. subscription based identification, height event based reporting of height/location, indication of airborne status
    Harmonisation of NR and LTE signal designs
  (2) Whether to follow the conclusion of SI (TR36.777) or also address the additional problems
  (3) commonarity with aerial network and MBB network v.s. dedicated network for aerials

## Slide 15: Aerial – motivation & goal
Issues to be resolved (Cont’d)
  (4) Urgency/necessity for the LTE enhancements for aerial UEs on top of Rel-15 enhancements
  (5) Necessity of additional performance study and the identification of futher enhancements
  (6) Handling of mobility issue, which is a continuation/enhancement of Rel-15 work, while the solution should not be limited to aeria UEs
Moderator’s proposal
  Continue offline or contribution based discussion
    LTE: RP-181046, RP-181049 Ericsson (different A.I)
    NR: RP-181070, RP-181071 Ericsson(different A.I)

## Slide 16: Aerial – Additional notes
Joint (email) discussion for LTE & NR
  RAN could make a decision whether we have a joint discussion, or keep separate discussion
Support of HAPS
  The potential new WI/SI for aerial UEs will not include HAPS use case
  Moderator’s recommendation: to submit a separate WID/SID and motivation paper to draw companies’ attention
   No contribution in this meeting
Operators’ interest
  Only one operator joined this email discussion
  Need more number of operators to move forward!

## Slide 17: even further mobility enhancement

## Slide 18: efMobEnh – motivation & goal
Motivation - confirmed through the email discussion
  Considering the new use cases such as URLLC, it is desired that “close to 0ms“ handover could be supported for as many scenarios as possible.
  In addition, mobility robustness related issues have not been addressed in Rel-15.
Goal - confirmed through the email discussion
  Study and identify the cases/scenarios which cannot utilize existing 0ms interruption handover solution, and specify necessary functionalities.
  Furthermore, study mobility robustness improvement related solutions.
Additional note
  This item can be WI if consensus is reached

## Slide 19: efMobEnh – moderator’s proposal
Draft WID
  Interested companies had a discussion in Busan, and agree to go directly to WI (with study phase)
  The WID seems to be “almost” stable
    No negative comment
    One comment to modify a component, but no time to review
Moderator’s proposal
  Check online if the proposed change is agreeable

## Slide 20: efMobEnh - Current objective of the WID (for information)
<Core part>
Specify further enhancements to achieve following targets,
  reduce user data interruption during handover, which targets as close as possible to 0ms, i.e. relaxed requirements could be considered.
  improve the robustness during handover,
Specify necessary core requirements for the identified solutions
The work is split into two phases,
  [Study Phase, to evaluate the proposed solutions, e.g. DC based handover, conditional handover and enhancements to make-before-break, including support of carrier aggregation in source/target eNB during handover, and do down selection or merger, if necessary. ]
  Work Phase, to specify the chosen solution(s)
Note: The following cases are considered in above objectives.
  Inter and intra frequency handover
  Inter and intra eNB handover
  Sync and async deployments
  dual Rx/dual Tx, dual Rx/single Tx, and single Rx/Tx options
  low and high velocity
<performance part>
Specify necessary requirement for the core requirements for introduced mobility enhancement solutions.

## Slide 21: Advanced receivers for LTE V2X

## Slide 22: V2X_AdvRX – motivation & goal
Motivation - confirmed through the email discussion
  For V2X scenarios, it is preferred to improve the demodulation performance and coverage in both noise and interference limited scenarios
Goal- confirmed through the email discussion
  Study the feasibility to improve the LTE sidelink V2X performance by advanced receiver, which potentially have a standardization impact (e.g. UE performance requirements or core specification)
Additional note
  There was a comment that the proposed techniques don’t require specification support.

## Slide 23: V2X_AdvRX – moderator’s proposal
Draft SID
  No positive comment was provided
  No negative comment was provided
  Thus, no square bracket is added in the draft SID
Moderators proposal
  The proposed SID is considered as stable, i.e. no wording discussion is necessary
  Discuss if this SI is approved or not (i.e. hard decision)

## Slide 24: V2X_AdvRX - Current objective of the SID (for information)
The general purpose of the SI is to study feasibility of using advanced LTE V2X receivers for Sidelink including:
  LMMSE-IRC receivers;
  Decoding of multiple PSSCH/PSSCH packets transmitted in the overlapping resources;
  Both 2RX and 4RX antennas receivers.
The study item has the following objectives:
Identify and agree on the target scenarios and assumptions including at least
  Realistic deployment scenarios (based on Rel-14 RAN1 work)
  Simulation assumptions for link-level evaluations
  Interference models for link-level evaluations
Identify reference advanced LTE V2X receiver structures and evaluate their performance/complexity trade-off and implementation feasibility including at least
  Investigate feasibility of the following receiver structures
    LMMSE-IRC with single PSCCH/PSSCH decoding (i.e. no decoding of multiple overlapping PSCCH/PSSCH transmissions)
    LMMSE-IRC with multiple PSCCH/PSSCH decodings (i.e. decoding of multiple overlapping PSCCH/PSSCH transmissions)
  Investigate feasibility of receiver structures with 2RX and 4RX antennas
    Note: The first priority for 2RX antennas and the second priority for 4RX antennas
Evaluate advanced LTE V2X receivers performance benefits over baseline Rel-14/15 V2X receiver
  Baseline receiver: LMMSE-MRC with single PSCCH/PSSCH decoding and 2RX antennas
Identify impact on the UE performance requirements or other specification impacts

## Slide 25: High speed scenario

## Slide 26: High_speed – motivation & goal
Motivation - confirmed through the email discussion
  Though the enhancements for high-speed scenario were performed so far, the earlier releases were not able to cover all the possible scenarios such as following:
    UE speed up to 500km/h
    Carrier aggregation scenario
Goal- confirmed through the email discussion
  Introduce further enhancements for missing high-speed scenario(s)
  The impact on physical layer and the existing network/deployment are minimized

## Slide 27: High speed – moderator’s proposal
Draft WID
  The WID is close to stable
  However, some companies have concern on particular components
Moderators proposal
  Resolve the identified issues during RAN#80 (online or offline)
  See the following 5 slides for the details

## Slide 28: High_speed - Current objective of the WID (for information)
<Core Part>
1) Extend the RRM/demodulation enhancement to CA scenario
  [1-1) Extend Rel-14 RRM/demodulation enhancement to CA case at least]
  [1-2) Other solutions are not precluded.]
2) The following new scenario are considered
  2-1) The target speed is 500km/h
  2-2) The bands include up to 3.5GHz
  2-3) SFN scenario defined in TS36.101 and TR36.878 with bidirectional coverage for tunnel and open space
  2-4) SFN scenario defined in TS36.878 with unidirectional coverage for tunnel and open space
  2-5) More discussion on how to specify the general unidirectional antenna pattern
  2-6) In addition to SFN scenarios, other deployment scenarios are not precluded
      Reason: unclear and ambiguous
      Option 1: keep this components as it is (assuming the concern is solved by offline discussion)
      Option 2: Add clear explanation what 1-1) means, and what other solution in 1-2) is

## Slide 29: High_speed - Current objective of the WID (for information)
[3) Investigate the downlink and uplink demodulation performance, and identify and specify the solutions to enhance the UL/DL demodulation performance under the above scenarios
  3-1) For uplink enhancement, the denser reference signals defined for V2V can be considered
  3-2) For downlink enhancement, the NR PT-RS like reference signal can be considered, and the schemes captured in TR36.878 can also be considered.
  3-3) Other solutions are not precluded, e.g., sTTI based solution and/or DMRS based solution.]
      Reason: Impact to PHY layer signal
      Option 1: Remove this component, i.e. no new physical layer signals are defined
      Option 2: Set priorities of study, i.e. 1st priority is to investigate LTE CRS/DMRS-based solution.

## Slide 30: High_speed - Current objective of the WID (for information)
4) Investigate the RRM measurement performance, and identify and specify the solutions to enhance the RRM measurement performance under the above scenarios, if needed
  [4-1) The schemes captured in TR36.878 can be considered.
    4-1-1) Candidate solution 1: UEs would need to perform ****
    4-1-2) Candidate solution 2: Enhance cell identification ****
    4-1-3) Candidate solution 3: Trigger the active measurements, e.g., ****
    4-1-4) Candidate solution 4: Network provides the assistant information ****
    4-1-5) Candidate solution 5: Enhanced RRM requirements are defined up to ****
    4-1-6) Candidate solution 6: Enhance RRM requirements based on ****
    4-1-7) Candidate solution 7: Reduce RLM (out of sync monitoring) window and ****
  4-2) Other solutions are not precluded.]
      Reason: Rel-14 mechanism should be reused
      Option 1: Keep all the options, i.e. 4-1-1) to 4-1-7) and 4-2)
      Option 2: Change the sentence such as “Investigate the RRM measurement performance, and identify and specify the solutions to enhance the RRM measurement performance under the above scenarios as long as RAN4 identifies non-necessity of the new RRM requirements”
      Option 3: Remove 4-1-1) to 4-1-7) and 4-2), and add a sentence such as “RRM requirements defined in Rel-14 is applied”

## Slide 31: High_speed - Current objective of the WID (for information)
[5) Improve the robustness for RLM in the high speed scenario]
[6) Investigate and improve issues in existing high speed scenario which has already been defined in each spec, if any.
  6-1) For example, SFN scenario with UE velocity up to 350km/h.]
      Reason: Reuse Rel-14 mechanism
      Option 1: Keep the current sentence
      Option 2: Change the sentence such as “Improve the robustness for RLM in the high speed scenario as long as RAN4 identifies non-necessity of the new RLM requirements”
      Reason: The scenario is not clear.
      Option 1: Keep the current sentence
      Option 2: Remove this component

## Slide 32: High_speed - Current objective of the WID (for information)
<Performance part>
[10) Specify the necessary RRM test cases]
11) Specify the necessary UE demodulation performance requirements, and CSI reporting requirements if any
12) Specify the necessary BS demodulation performance requirements
      Come-back after other parts are stable

## Slide 33: Low Complexity 4Rx

## Slide 34: LC_4Rx – motivation & goal
Proposed Motivation
  While there is a growing demand on the higher order diversity UEs, the implementation on such UEs are not easy, e.g. 4 or 8 receivers with CA
Proposed Goal
  Introduce a new UE capability to allow the simplification of additional diversity receivers, i.e. no RF filters before LNA, while minimizing the performance impact
Email discussion result
  The same discussion was repeated, i.e. some companies showed their concern – e.g. impact to the network
  The moderator encouraged to have an offline discussion to seek a compromise until phase-2 email discussion

## Slide 35: LC_4Rx – moderator’s proposal
Draft SID/WID
  Not provided by the contact company
  Hence, no email discussion
Moderators proposal
  No consensus in this meeting
  Continue offline discussion (i.e. no official email discussion necessary)

## Slide 36: References – for information
Tdoc No | Source | Title
RP-180757 | SoftBank (Email discussion moderator) | Summary of email discussion on LTE enhancements (other than IoT, MIMO, broadcast)
RP-180758 |  | Detail of email discussion on LTE enhancements (other than IoT, MIMO, broadcast) – guidance and structure
RP-180759 |  | Detail of email discussion on LTE enhancements (other than IoT, MIMO, broadcast) – phase 1
RP-180760 |  | Detail of email discussion on LTE enhancements (other than IoT, MIMO, broadcast) – phase 2
RP-180761 |  | New Study Item on LTE uplink enhancements for WTTc
RP-180762 |  | New Work Item on even further Mobility enhancement in E-UTRAN
RP-180763 |  | New Study Item on Study on Advanced Receivers for LTE V2X
RP-180764 |  | New Work Item on Further performance enhancement for LTE in high speed scenario