## Slide 1: Motivation for NR mixed mode broadcast/multicast

## Slide 2: Motivation
In REL-14 study on LTE V2X, it has been identified that small area broadcast is much beneficial than large area broadcast and unicast transmissions.
  Large area broadcast requires high resource capacity to broadcast V2X messages in a range of several hundreds of meters from a source UE
  Many small clusters of MBSFN areas should be configured to provide V2V service over MBMS
In addition, offloading PTP traffic to PTM traffic is beneficial in a hot spot during prime time, e.g. at Football/Baseball stadium or for IoT use cases
It is beneficial to use MBMS for support of V2X over Uu, IoT and eMBB in hot spot.

## Slide 3: Proposal for REL-16 NR MBMS
NR MBMS can be initially supported from SCG part of EN-DC in REL-16 with little impact, potentially after March 2019.
  RAN1 is expected to have only small work for small area broadcast/multicast
    REL-15 L1 design on NR PDSCH can be used to support broadcast/multicast with minimum impact.
  LTE V2X can be supported via SCG NR resources for UE in EN-DC.
  NR MBMS in SgNB can leverage LTE MeNB based on the existing EPC MBMS architecture supporting LTE V2X.
  RAN2 can lead this work to support NR MBMS via SCG transmission of EN-DC.
NR MBMS for standalone NR could be considered after REL-16, with impact on system architecture and protocols.
  Support of MBMS in NR standalone is expected to have big impact on system architecture and protocols.