## Slide 1: Discussion on UE feature for DL 4-layer MIMO
China Unicom, British Telecom, CHTTL, Deutsche Telekom, Huawei, HiSilicon, LGUPLUS, NTT DOCOMO, Orange, Sprint, Telecom Italia, Telefonica, [Telia Company], Telstra
3GPP TSG RAN Meeting #80
La Jolla, USA, June 11 - 14, 2018
Agenda: 9.8
RP-181299

## Slide 2: Background
In RAN#78, the agreement on mandating 4Rx was reached in RP-172788
  For NR Bands n7, n38, n41, n77, n78, and n79 the UE shall be equipped with 4Rx ports as a baseline.
There was no agreement on mandatory or optional for the feature group of DL MIMO layers in working groups.
It is prerequisite to have 4Rx to support DL 4-layer for a NR UE. And support of DL 4-layer MIMO can improve the peak data rate.

## Slide 3: Proposals
Mandate support of DL 4-layer MIMO on the bands, where the UE shall be equipped with 4Rx ports as a baseline at least for single carrier operation mode
  NR Bands n7, n38, n41, n77, n78, and n79
  Applicability to other NR bands is FFS according to the progress for 4Rx in future