## Slide 1: WF on remaining parts of RAN4 feature list
NTT DOCOMO
GPP TSG RAN Meeting #80 RP-181379
La Jolla, USA, June 11 - 14, 2018
Agenda Item: 9.8
Document for: Approval

## Slide 2: Agreements in RAN#80
60kHz of subcarrier spacing for FR1 (feature 1-1)
  Agree to be optional as follows:
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-1 | 60kHz of subcarrier spacing for FR1 | 1) 60kHz subcarrier spacing for data channel in FR1 |  | Yes | UE does not support 60kHz of subcarrier spacing for data channel in FR1 | Type 4 | No Need | Applicable only to FR1 |  |  | RAN4 | TBD | Optional

## Slide 3: Agreements in RAN#80
SUL and LTE-NR coexistence related (feature 1-10, 1-11)
  Agree to update “Components” of 1-10 and “TSG-RAN decision” as follows:
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-10 | Support of EN-DC with LTE-NR coexistence in UL sharing from UE perspective | 1) LTE and NR UL Transmission in the shared carrier via TDM only 2) LTE and NR UL Transmission in the shared carrier via FDM only 3) LTE and NR UL transmission in the shared carrier via FDM or TDM |  | Yes | UE does not support of EN-DC with LTE-NR coexistence in UL sharing from UE perspective | Type 3 (per band combination) | No Need | Applicable only to FR1 |  |  | RAN4 | Optional | Optional
1-11 | Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective | Support of switching type between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective. Type 1: ~0us Type 2: <20us | 1-10 | Yes | UE does not support UL subcarrier alignment between LTE and NR for EN-DC with LTE-NR coexistence in UL | Type 3 (per band combination) | No Need | Applicable only to FR1 |  | This feature is the switching time between LTE UL and NR UL in the same carrier Per band combination signalling (Type 3) UE Capability signalling elements. 1: ~0us switching type. 2: <20us switching type. | RAN4 | TBD | Mandatory to report switching time type 1 or type 2 if UE reports its capability in 1-10 as 1) LTE and NR UL Transmission in the shared carrier via TDM only, or 3) LTE and NR UL transmission in the shared carrier via FDM or TDM

## Slide 4: Agreements in RAN#80
“Recommendation for TSG-RAN” is agreed as “TSG-RAN decision” except for the following features:
  Pi/2 BPSK (feature 1-6, 1-7) for FR2
  Simultaneous reception or transmission with same or different numerologies in CA (feature 2-2)
  Almost contiguous UL CP-OFDM (feature 2-7)
  PA calibration gap (feature 2-8)

## Slide 5: Agreements in RAN#80
Pi/2 BPSK (feature 1-6, 1-7)
  RAN4 agreements on “Recommendation for TSG-RAN”:
    Optional for FR1, TBD for FR2
  Agree mandatory with capability for FR2
    This means to introduce IOdT bits for Pi/2 BPSK for FR2
Simultaneous reception or transmission with same or different numerologies in CA (feature 2-2)
  RAN4 agreements in R4-1803551:
    Same numerology for intra-band NR CA including both continuous and non-continuous is mandatory support for Rel15
    If a UE supports inter-band NR CA including both FR1 band(s) and FR2 band(s), the UE shall support two mixed numerologies between FR1 band(s) and FR2 band(s) in DL and UL with or without capability signaling
  Agree the following for “TSG-RAN decision” :
    Same numerology for intra-band NR CA including both continuous and non-continuous is mandatory with capability in both FR1 and FR2. Two mixed numerologies between FR1 band(s) and FR2 band(s) in DL and UL are mandatory with capability if UE supports inter-band NR CA including both FR1 band(s) and FR2 band(s). Optional for other cases.

## Slide 6: Remaining parts of RAN4 feature list
Almost contiguous UL CP-OFDM (feature 2-7)
  Definition of almost contiguouis is not yet decided in RAN4
PA calibration gap (feature 2-8)
  Definition of PA calibration gap is not yet decided in RAN4