## Slide 1: Motivation of Work Item for NR NOMA
3GPP TSG RAN #81
Gold Coast, Australia, September 10-13, 2018
Agenda Item: 9.1
ZTE, …
RP-181718

## Slide 2: Motivation
  The study of NOMA techniques as part of NOMA SID showed that:
    NOMA can significantly improve the system capacity in terms of system loading compared to baseline OFDM contention based multiple access, for mMTC, URLLC and eMBB small data scenarios
    Advanced receivers, e.g., MMSE-SIC require only moderate complexity increase compared to legacy MMSE-IRC receiver, while delivering significantly better performance in NOMA
    Enhanced preamble/DMRS can be used for UL transmission detection and to support more number of multiplexed users, in both RRC_connected and RRC_inactive states
  In order to realize the observed performance benefit of NOMA for 5G commercial deployment, it is proposed to start the work item phase to specify necessary mechanisms

## Slide 3: Scope of NOMA Techniques
  Transmitter side signal processing schemes
    Modulation and symbol level processing
    Bit-level processing
  NOMA receivers
    Typical type of receivers
    Performance and complexity trade-off
  Related procedures
    UL transmission detection
    Misc. , e.g., HARQ, link adaptation, …
  Performance evaluation
    Link level, and PHY abstraction
    System level

## Slide 4: Transmitter Side Signal Processing for NOMA
Bit level scrambler/interleaver as MA signature to differentiate users
  Small specification impact
Symbol level spreading as MA signature to differentiate users
  Moderate specification impact
Multi-branch to improve per user spectral efficiency
  Can be commonly applied to many schemes
To use legacy channel coding, modulation and resource mapping which are not used for user differentiation
Channel encoder
Modulator
Symbol Spreading
Resource mapping
Bit Scrambler/ Interleaver
ith user data

## Slide 5: Sub-types of Spreading Sequences
  Sub-type 1: Welch-bound equality (WBE) approaching sequences
    Nested sequences whose elements correspond to QAM constellation (MUSA)
    Grassmanian sequences (quantized)
    Equiangular tight frames (ETF) or harmonic ETF sequences
    Generalized WBE with unequal power constraint
    Chirp sequences whose continuous-time function has closed-form formula
  Sub-type 2: Computer generated sequences with desired cross-correlation
    Also low peak-to-power-ratio (PAPR)
  Sub-type 3: Pseudo-random (PN) sequences, e.g., Gold code
  Sub-type 4: Sequences with uneven diversity orders/sparsity

## Slide 6: Typical NOMA Receivers
Receiver type | Typical Tx scheme category | Performance | Complexity | Compatible to legacy gNB receiver impl.
MMSE-SIC | Symbol level spreading | Moderate | Low | Same architecture
ESE + SISO dec | Bit level processing | Moderate | Medium | Different arch.
EPA + SISO dec | Symbol level spreading | High | High | Different arch.
Different sequences of symbol level spreading achieve the similar link performance, under the similar-complexity receivers
  Different sub-types of sequences may have different “sweet” point of operation and pool sizes
Spreading and bit level processing achieve the similar link performance, when MMSE-SIC and ESE+SISO receivers are used, respectively
  MMSE-SIC is more compatible to legacy MMSE-IRC receiver for gNB

## Slide 7: Candidate Channel Structures
Preamble + data
Preamble + data + DMRS
DMRS + data
Preamble/DMRS and their enhanced version can be used for UL transmission detection
  Preamble/DMRS and payload of message can also be used for UE identification
(Preamble/DMRS + data) channel structure provide physical layer support for RRC_inactive and 2-step RACH
  Contention based
  Support asynchronous operation

## Slide 8: Characteristics of NOMA Grant-free Scenarios
RRC-connected:
Tight synchronization in time & freq
Tight power control, equal avg SNR
No MA signature collision
Support of low or medium number of simultaneous users
Closer to grant-based
Further away from grant-based
RRC-INACTIVE/2-step RACH:
Potentially asynchronous
Loose power control, un-equal avg. SNR
Potential MA signature collision
Support of a large number of simultaneous users

## Slide 9: Progress of 2-step RACH
RAN1:
Companies proposed to enhance 4-step RACH [1][2][3][4][5][6][7]
  It seems 4-step RACH could be baseline for NR-U
The same companies also believe 2-step RACH is beneficial for NR-U, but without any agreement
  To reduce delay and improve reliability for initial access due to necessary LBT operation
Not many details of 2-step RACH were discussed
  Msg1 may contain preamble and data (e.g. the Msg3 contents) and this is all that was put on the table
  Details of how to resolve collisions and ensure good quality of detection/decoding at the receiver are essential , but not yet discussed under this agenda item
    Note that these aspects are highly related to the NOMA SID
RAN2 :
Is also working on 4-step RACH enhancement
The assumption is that a generic 2-step RACH (not NR-U specific) will be studied further
  One email discussion is arranged till next meeting
  And discussion on how to proceed with such generic 2-step RACH is invited for the RAN plenary meeting
[1] R1-1809480, Qualcomm [2] R1-1808769, Samsung [3] R1-1808336, Sony [4] R1-1808508, LGE
[5] R1-1808686, Intel [6] R1-1808062, Huawei [7] R1-1809205, Ericsson

## Slide 10: How to proceed with 2-step RACH
The main building block for the 2-Step RACH will be the transmission scheme and channel being currently studied under NOMA SID in RAN1
  Specifically, enabling transmission of payload in Msg1 using NOMA based schemes
  For both synchronous and asynchronous operations
So, given the above dependence in the scope, it makes sense to specify the details of 2-Step RACH as part of NOMA WID to avoid duplication of work in different work items
Hence, we propose the following work split:
  Study aspects of 2-Step RACH – until December (Rel-15):
    RAN2 issues can be progressed as part of NR-U (Rel-15 SID)
    RAN1 issues can be progressed as part of NOMA (Rel-15 SID)
  Normative work (i.e. specification of 2-step RACH in Rel-16) – all under NOMA (WID)
    RAN1 will specifiy the payload and L1 aspects of spreading etc depending on the NOMA scheme selected as part of the NOMA WID (Rel-16)
    RAN2 will specify the higher layer aspects as part of the RAN2 objectives for NOMA WID (Rel-16)
    The specified frame work for 2-step RACH under NOMA WID would also be reused for NR-U WID in Rel-16

## Slide 11: Scope of NOMA WID
Symbol level spreading [RAN1]
  Spreading sequence harmonization to facilitate the scalable design and support diverse spectral efficiency per user, overloading capability, sequence pool size, PAPR requirement, performance robustness
  Bit-level scrambling/interleaving as a subset of the design with limited specification impact
2-step RACH [RAN1, RAN2]
  Preamble enhancements and channel structure
  2-step RACH procedure in both PHY and MAC layer
Data transmission [RAN1, RAN2]
  In both RRC-CONNECTED and RRC-INACTIVE state
  Both grant-based and grant-free transmission

## Slide 12: Thank you