## Slide 1
3GPP TSG RAN meeting #81 RP-181721
Gold Coast, Australia, September 10 – 13, 2018
Agenda Item: 9.3.16
Source: ZTE
Title: Considerations on NR SI for beyond 52.6 GHz
Document for Discussion

## Slide 2: Introduction
In RAN#80, A new SI, Study on NR beyond 52.6 GHz (800090, FS_NR_beyond_52GHz) has been approved in RP-181435
Based on its SID, objectives including
  Available Spectrum
  Requirements
In the contribution, ITU-R spectrum allocation and some survey of regulatory requirements in China are shared, and finally some requirements we concerned are given.

## Slide 3: ITU-R
WRC-19 1.13 Items[1] (for high frequency bands of IMT-2020)
  ITU-R will conduct and complete in time for WRC-19 the appropriate studies to determine the spectrum needs for the terrestrial component of IMT in the frequency range between 24.25 GHz and 86 GHz, taking into account
  In 2016, ITU-R SG5 built Task Group 5/1 (TG5/1) to be responsible for the development of spectrum conditions of candidate bands.
Candidate frequency bands | candidate frequency bands of requirement additional conditions
24.25-27.5 GHz | 31.8-33.4 GHz,
37-40.5 GHz | 40.5-42.5 GHz
42.5-43.5 GHz | 47-47.2 GHz
45.5-47 GHz | 
47.2-50.2 GHz | 
50.4-52.6 GHz | 
66-76 GHz | 
81-86 GHz | 
[1] RESOLUTION 238 (WRC-15),Studies on frequency-related matters for International Mobile Telecommunications identification including possible additional allocations to the mobile services on a primary basis in portion(s) of the frequency range between 24.25 and 86 GHz for the future development of International Mobile Telecommunications for 2020 and beyond

## Slide 4: Survey of regulatory requirements in China
low transmission power and short distant unlicensed applications
  Frequency range: 59-64 GHz
  Specific requirements can be referenced from 38.805
Vehicle Radar ranging application since 2005 [1]
  Frequency range: 76-77GHz
  Peak EIRP: 55dBm
Amateur Radio [2]
  Frequency range: 75.5-76GHz, 76-81GHz:
[1]《关于发布〈微功率(短距离)无线电设备的技术要求〉的通知》(信部无〔2005〕423号)
423# notification on technical requirements of low transmission power (short distant) in 2005
[2] (82)无发文53号：关于颁发《业余无线电管理暂行规定》的通知
53# issue on temporary provisions of amateur radio management

## Slide 5: China
Frequency Allocations in Radio Regulations from 52.6GHz to 100GHz
Service | The Frequency Band (GHz)
MOBILE | 59.3-64, 65-66, 66-71, 71-74, 74-76 81-84, 84-86, 92-94, 94.1-95, 95-100
FIXED | 59.3-64, 64-65, 65-66, 71-74, 74-76 81-84, 84-86, 92-94, 94.1-95, 95-100
Broadcast | 74-76
RADIOLOCATION | 59.3-64, 66-71, 76-77.5, 77.5-78, 78-79, 79-81, 92-94, 94-94.1, 94.1-95, 95-100
Other services including SPACE RESEARCH, RADIONAVIGATION, SATELLITE related services, Amateur, RADIO ASTRONOMY | 
China current allotment
ITU-R WRC-19 1.13

## Slide 6: Proposal
Proposal 1, In the Chapter 1, ITU-R TG5/1 defined some methods&conditions and regulatory measures of candidate frequency bands of IMT-2020 in CPM text, both 66-76 GHz and 81-86 GHz should be considered in the report.
Proposal 2, In the Chapter 1, Regulatory requirements in some specific countries, such as China, EU, US and so on, can be reflected.

## Slide 7: Thank you