## Slide 1: Views on DL MIMO efficiency enhancements for LTE
3GPP TSG RAN Meeting #81 RP-181732
Gold Coast, Australia, Sept 10 - 13, 2018
Agenda item: 10.7.4
Document for: Discussion
ZTE

## Slide 2: Current RAN1 scope and TU allocation
Enhance SRS capacity and coverage [RAN1] [1][2]
  Introduce more than one symbol for SRS for one UE or for multiple UEs on a UL normal subframe
    Baseline: the minimum SRS resource allocation granularity for a cell is one slot, when more than one symbol in a normal subframe is allocated for SRS for the cell
    Enhancements on PUCCH and PUSCH are not in scope
  Introduce virtual cell ID for SRS
 | 2018H2 |  |  | 2019H1 |  |  | 2019H2 |  | 
Meeting | 94 | 94bis | 95 | 96 | 96bis | 97 | 98 | 98bis | 99
TU | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Observation: TUs of 9 meetings are occupied by a small scope

## Slide 3: Issue #1: Unclear description
The baseline defined in RAN1 scope for multi-symbol SRS does not exist in LTE
  LTE: only the last symbol of a normal UL subframe can be used for SRS for cell
  Current baseline: a whole slot in a normal UL subframe can be used for SRS for cell
Companies in RAN1 are confused by the baseline description
It’s desirable to use an existed scheme as baseline
Proposal 1: Revise the baseline in the scope for multi-symbol SRS as “Use current LTE SRS configuration in a normal UL subframe as baseline”.
LTE
Baseline ??

## Slide 4: Issue #2: Regarding CSI enhancement
LTE Rel-13 and Rel-14 have enhanced the CSI feedback by introducing 2D-beam codebook and 2-beam combination, which haven’t been deployed yet
  Need for further enhancement is not urgent
Introducing more than 2 beam combination will consume much higher overhead and UE processing complexity
  The CSI overhead can be as large as more than 400 bits to support more than 2 beam combination
    Different ranks can have about 200 bit overhead difference, which causes significant issue for BS UL resource allocation
    In NR Rel-15, flexible PUSCH RA, CSI coding mechanism, flexible CSI report band configuration and dynamic partial CSI omission can help to solve the overhead issue. These are not supported in LTE.
  Tremendous discussion time consumption is expected to solve the above overhead issue in LTE
Proposal 2: Do not include CSI enhancement in Rel-16 LTE MIMO WI.
 | Rank 1 | Rank 2
Estimated overhead for 4-beam combination in [3] | >200 bits | >400 bits

## Slide 5: Issue #3: TU allocation
Based on the above observation and proposals, the current TU allocation is more than required by the current scope.
  The allocated time in RAN1 #94 is even not fully utilized
Our estimation of a more proper TU allocation is given as follows.
Proposal 3: Reduce the TU per meeting from 1 to 0 for LTE Rel-16 MIMO from RAN1 #97 to RAN1 #99.
 | 2018H2 |  |  | 2019H1 |  |  | 2019H2 |  | 
Meeting | 94 | 94bis | 95 | 96 | 96bis | 97 | 98 | 98bis | 99
TU | 1 | 1 | 1 | 1 | 1 | 1 -> 0 | 1-> 0 | 1-> 0 | 1-> 0

## Slide 6: Conclusion
We have the following proposals for LTE Rel-16 MIMO
  Revise the baseline in the scope for multi-symbol SRS as “Use current LTE SRS configuration in a normal UL subframe as baseline”
  Do not include CSI enhancement in Rel-16 LTE MIMO WI
  Reduce the TU per meeting from 1 to 0 for LTE Rel-16 MIMO from RAN1 #97 to RAN1 #99

## Slide 7: References
[1] RP-181491, Draft Report of 3GPP TSG RAN meeting #80
[2] RP-181485, DL MIMO efficiency enhancements for LTE
[3] RP-181481, DL MIMO efficiency enhancements for LTE