## Slide 1
Views on NRU WID scope
vivo
3GPP TSG RAN Meeting #82 RP-182465
Sorrento, Italy, December 10-13, 2018
Agenda Item: 9.1.1

## Slide 2
Highlights
  Frequency band and deployments
  Numerology options
  Wider bandwidth operation
  Channel access schemes
  DL channel/signals
  UL channel/signals
  Initial access and mobility
  Higher layer aspects

## Slide 3
Frequency bands
  Target a band agnostic design applicable to unlicensed spectrum in 1 GHz ~7.125 GHz
Deployment scenarios
  Licensed assisted NRU operation
    CA between NR licensed Pcell and NRU Scell
    DC between NR licensed Pcell and NRU PScell
    DC between LTE licensed Pcell and NRU Pscell
  Standalone NRU operation
Numerology options
  Single numerology operation for all DL/UL signal/channels for a given carrier and for at least intra-band CA on serving cells on unlicensed bands
    15KHz and 30KHz are supported
    Single SSB numerology per band is assumed by UE

## Slide 4
Channel access
  Support LBE based operation
  Support FBE based operation
  Specify channel access priority classes
DL Signals/Channels
  Support NR-U DRS containing at least SS/PBCH block burst set transmission and possibly associated CSI-RS, RMSI-CORESET(s)+PDSCH(s), OSI and paging
  Support dynamic change of the time domain instances in which the UE is expected to receive PDCCH
  Support PDSCH design to not require the gNB to change a pre-determined TBS for a PDSCH transmission depending on the LBT outcome

## Slide 5
UL Signals/Channels
  Support PRB-based block-interlace for PUSCH/PUCCH/SRS/PRACH allocation
  Support Rel-15 resource allocation for PUSCH/PUCCH/SRS/PRACH
  Support PUSCH design to not require the UE to change a granted TBS for a PUSCH transmission depending on the LBT outcome
  Support CP-OFDM
  Support PUSCH transmission with configured grant using Rel-15 NR type-1 and type-2 configured grant as the baseline with necessary modifications
  Support enhanced UCI transmission including HARQ-ACK, SR due to potential LBT failure

## Slide 6
Initial access and mobility
  Modifications to SS/PBCH blocks, SI, paging transmissions due to potential LBT failure.
  Support enhanced 4-step RACH and 2-step RACH
  Modifications to RLM/RRM procedures due to reduced transmission opportunities for DL signals and channels due to LBT failure
  Enhanced RRM measurements including RSSI measurement/reporting
  Modifications to synchronization raster
Higher layer aspects
  Support Inactive and Idle mode procedures
  Support camp on non-best cell if the PLMN of the strongest cell is not the R/E-PLMN
  Support mobility among standalone NR unlicensed and licensed cells

## Slide 7
Thanks