## Slide 1: Motivation of Work Item for NR NOMA
3GPP TSG RAN #82
Sorrento, Italy, December 10-13, 2018
Agenda Item: 9.1.1
ZTE, Sanechips
RP-182469

## Slide 2: Overall System-level Performance of NOMA
The NOMA study shows that NOMA schemes can significantly improve the system capacity and spectrum efficiency compared to baseline
  Link and system level performance evaluated under realistic modelling of Tx/Rx impairment, incl. channel estimation error, power control inaccuracy, etc
  System capacity = packet arrival rate @ 1% packet drop rate, or %UEs satisfying URLLC requirement
  Capacity gain observed for mMTC, URLLC and eMBB scenarios for configured grant
  Physical resource occupation in baseline can be the same or different from NOMA
  Several types of receivers are used, but the performance comparison between the baseline and NOMA usually assumes the same type of receiver

## Slide 3: System-level Performance Gains
Source | Gain (%) for eMBB | Gain (%) for mMTC | Gain (%) for uRLLC
R1-1814073 | For MMSE-IRC: 150% - 275%, For MMSE-hard PIC: 67%-150% | For MMSE-IRC: 100% For MMSE-hard PIC: 71%-150% | 140% - 300%
R1-1813922 /3923/3924 | 0% | 0% | 0%
R1-1812969 | 91% | 88% | N/A
R1-1813159 | N/A | 100% for low packet arrival rate | N/A
R1-1814341 | N/A | 46% | N/A
R1-1812612 | 19% for MUSA, 43% for PDMA | N/A | 42% for MUSA, 55% for PDMA
R1-1814149 | 4% for 95 percentile, 18% for 50 percentile, 72% for 5 percentile | 67% | N/A
R1-1814077 | 20% |  | 

## Slide 4: Performance Gain for mMTC (with baseline Config. 1)
R1-1812969
R1-1814073
R1-1813159
R1-1814149

## Slide 5: Performance Gain for mMTC (with baseline Config. 2)
R1-1813922
R1-1814073

## Slide 6: Performance Gain for URLLC (with baseline Config. 1)
R1-1812612
R1-1814073

## Slide 7: Performance Gain for URLLC (with baseline Config. 2)
R1-1813923
R1-1814073

## Slide 8: Performance Gain for eMBB (with baseline Config. 1)
R1-1814073
R1-1812969
R1-1812612
R1-1814149

## Slide 9: Performance Gain for eMBB (with baseline Config. 2)
R1-1814077
R1-1813924
R1-1814073

## Slide 10: Transmitter Side Signal Processing for NOMA
Bit level scrambler/interleaver as MA signature to differentiate users
  Small specification impact
Symbol level spreading as MA signature to differentiate users
  Moderate specification impact
Multi-branch & power assignment can be commonly applied to NOMA schemes
Legacy channel coding, modulation and resource mapping are reused
Channel encoder
Modulator
Symbol Spreading
Resource mapping
Bit Scrambler/ Interleaver
ith user data

## Slide 11: NOMA Receivers
Detector:
  Single-user
  Parallel multi-user
Channel decoder:
  Hard output
  Soft-input-soft-output (SISO)
Interference cancellation resides in detector for SISO type receiver.
Receiver type | Typical Tx scheme | Link-level performance | Complexity | Compatible to legacy gNB receiver impl.
MMSE-hard IC | Symbol level spreading | Moderate | Moderate | Same architecture
ESE + SISO dec | Bit level processing | Moderate | High | Different arch.
EPA + SISO dec | Symbol level spreading | High | High | Different arch.
Channel decoder
Interference cancellation
Detector
Received signal

## Slide 12: Candidate Channel Structures
DMRS capacity enhancement is considered in many LLS
  In SLS up to 18 simultaneous users are observed (95%CDF)
  Necessary to support up to 24DMRS ports within one slot
(Preamble + data) channel structure
  Contention based
  Support asynchronous operation
DMRS + data
For configured grant
For grant-free transmission and 2-step RACH
Preamble + Data
Preamble + Data + DMRS

## Slide 13: System-level Performance for (preamble + data)
Asynchronous operation
Preamble/spreading sequence randomly selected from the pool of size 64
For NOMA simulation, spreading is applied to the data part in frequency domain;
For baseline, LCRS is assumed
NOMA can double the system capacity compared to the baseline

## Slide 14: Transmission scheme to apply NOMA solution
RRC_CONNECTED state:
  Configured grant for both type1 and type2
  Some signaling is needed to allocate MA signature and DMRS
  More users can be accommodated i.e. spectrum efficiency is improved
RRC_INACTIVE state:
  Grant-free transmission i.e. transmission is done by random selection of radio resource including MA signature and feedback in L1 is expected
All RRC states:
  2-step RACH for both triggers for 4-step RACH.
  For both control plane and user plane
  For both licensed spectrum and unlicensed spectrum

## Slide 15: Benefit of grant-free transmission and 2-step RACH
MSG1:Preamble
MSG2: RAR
MSG3
MSG4
Preamble+payload
L1 feedback
MSGA:Preamble+payload
MSGB
Benefit of grant-free transmission and 2-step RACH:
  Less signaling overhead
  Less power consumption for transmission/receiving
  Less delay for both control plane and user plane
    Control plane delay for NR system initial access could be reduced significantly
  Smoother mobility
    HO interruption time could be further reduced

## Slide 16: Justification of Specifying 2-step RACH in NOMA WI
Key building blocks at PHY layer to support 2-step RACH were studied under NOMA
  (preamble + data) channel structure is the key enabler of 2-step RACH
    For data part NOMA scheme will be applied
  The impact of MA signature or DMRS/preamble collision was studied as part of NOMA
  Link and system level simulations for asynchronous operation with random selection of MA signatures has also been investigated
Higher layer aspects of 2-step RACH are common to a number of applications
  2-step RACH is beneficial for NR operation both in licensed and unlicensed spectrum and also for other use cases such as the non-terrestrial networks
  Triggers for 4-step RACH can be applied for 2-step RACH
    i.e. it is a general procedure for both control plane and user plane covering all RRC states
    Data from INACTIVE state will be an additional trigger for 2-step RACH
RAN#81 provides the guidance on 2-step RACH in the endorsed WF (RP-182126)
  A common 2-step RACH design for various use cases is desirable
  2-step RACH can be included in a later Rel-16 WI, per normal approval process

## Slide 17: NOMA for Non-terrestrial Networks (NTN)
Massive coverage for NTN and large number of devices in a given cell require mechanisms to enable low signaling overhead
  Diameter of one NTN cell by the foot-print of one beam for LEO is up to 400 km
  Huge number of mobile devices and IoT devices
  Typical NTN application, e.g., internet application, asset tracking, data sensing/reporting triggered by sporadic external events or periodic status reporting with small amounts of data
Necessity of grant-free transmission for NTN
  Excessive propagation delay compared to typical terrestrial networks
  Tight control from gNB is not efficient, e.g., closed-loop link adaptation, etc. are questionable
  Expensive radio resource for NTN -> Unnecessary signaling should be minimized
  Maximizing battery life of NTN terminals for various IoT applications e.g.
    Utilizing meter readings for electricity, oil, gas and chemical storage tanks
    Reporting of flow, temperature, pressure, leakage, corrosion, for oil and gas pipelines
    Monitoring and control of remote voltage regulators, capacitors, valves
    …

## Slide 18: Working scope of NOMA WID
Transmitter side processing
  Configurable between LCRS (SF=1) and symbol level linear spreading (SF>1)
  DMRS enhancement up to 24 ports within one slot
NOMA related procedures
  Signaling for configured grant (both type1 and type2)
  Grant-free transmission
2-Step RACH
  Both RAN1 and RAN2 part
  Both licensed and unlicensed part
Small data transmission in RRC_INACTIVE
  Based on grant free transmission or 2-step RACH

## Slide 19: Thank you