## Slide 1: Harmonization Proposal on Technology Icons Indication
Verizon, AT&T, KT Corp., CHTTL, [China Telecom], [CMCC], [KDDI], SK Telecom, TELUS, Asia Pacific Telecom, LG Uplus, Bell Mobility
3GPP TSG RAN #82
Sorrento, Italy, Dec. 10 – 13, 2018
RP-182538

## Slide 2: Background I:
To indicate difference access technologies
    3GPP 5G includes several access technologies. In the simplest case, one can classify Rel. 15 into several different types of 5G systems, e.g. 5G LTE (3GPP LTE R15 and beyond), NR (FR1/FR2), NB-IoT/eMTC and so on.
To indicate different user experiences or services availabilities
    An operator may choose to classify their network tied to user experiences, for instance, based on different throughputs or latencies, e.g., 5G Gigabyte networks, 5G low latency networks. E.g. VR/AR may only be available at low latency network while HD Video may only be available in gigabyte networks or hotspot scenarios only.
Support of different verticals with distinct network and UE capabilities
    5G is required to support different verticals and offers different network infrastructure capabilities (Infrastructure, Platform, Network) as a Service- the so called IaaS, PaaS or NaaS. As a result, operators will need to indicate different network capabilities and services availabilities, e.g. an Industrial IOT enabled platform vs. general purposed eMBB infrastructure vs. V2X network for the automobiles. Different icons may be needed for different verticals or network capabilities.

## Slide 3: Background 3GPP Discussion
RP-182013 Considerations on 5G icons
  Verizon, AT&T, KT Corp, CHTTL, China Telecom, CMCC, KDDI, SK Telecom, TELUS, Asia Pacific Telecom, LG Uplus
  Proposal: Expand the 1-bit UpperLayerIndication IE to a 3-bit string so that UE AS layer can provide different indications to the upper layer.
RP-181597 Operator Views on 5G Indicator
  T-Mobile USA, Deutsche Telekom, Telecom Italia, Orange, Sprint, BT, Vodafone
  “Any expansion of the UpperLayerIndication Information Element occurring at this time would risk interim action with the undefined extra bits, subsequently risking adverse effects on roaming and UE behaviour in visited networks”

## Slide 4: GSMA LS (to up updated)
RP-182125 LS on 5G Indicator (to: GSMA; cc: -; contact: RAN chairman (Nokia)) RAN
  TSG-RAN would like to point out the main aspects raised at RAN#81:
    The meaning of the “upperLayerIndication” would be defined by each operator individually. Hence, it is unclear how an “upperLayerIndication” would work, especially considering the case of:
      A device roaming into a visited network;
      Open-market devices.
    Extending the “upperLayerIndication” makes the above issues more complex.
    To mitigate the above issues it was suggested to have GSMA (as a 3GPP MRP) define any necessary value(s) to be encoded by 3GPP.
On going discussion in GSMA 5GSI, no agreement or consensus has been reached yet.

## Slide 5: Harmonization Proposal:
Keep the 1-bit UpperLayerIndicator and the indication is provided to the upper layers in both home network and visited network, allowing incorporating any decisions out of GSMA.
3GPP RAN to agree on adding a new 3 bits to SIB2
  uli-HPLMNonly
  Indication to be provided to upper layers only when UE is in home network (HPLMN).
Allow operators to indicate to the own subscribers in their home network of various services availabilities, e.g. 5G NB-IoT, V2X, Industrial IOT, URLLC, AR/VR, 5G eMBB
No impact on roaming UEs, similar approach has been used in LTE, e.g. acdc-HPLMNonly