## Slide 1
Way forward for data forwarding on inter-system HO
Samsung, KT Corp., ZTE, CATT, ETRI, Huawei, Google, Nokia, Nokia Shanghai Bell, LG Electronics Inc., CMCC, China Unicom
3GPP TSG RAN #82 10-13 December 2018
Sorrento, Italy
RP-182543

## Slide 2: Background
Data forwarding for inter-system HO was discussed for a long time in RAN3. The main controversial part is per PDU session tunnel (Option 2) or per E-RAB tunnel(Option 3) between NG-RAN and UPF.
The brief summary of the discussion history in RAN3:
  In RAN3#97 (August 2017), RAN3 agreed Per PDU session tunnel. This agreement was reflected to RAN3 TS38.413 and TS38.300.
  RAN3 has sent the agreement to SA2 in R3-174226 (LS). After discussion in SA2, SA2 agreed the mechanism in S2-177938 to TS23.502.
  During the end marker discussion, there was a proposal to revert the previous agreement by using per E-RAB tunnel while there was no evidence that the pervious agreement had a critical technical problem.
  RAN3 compared the two solutions again, the co-signing companies realized that per E-RAB tunnel bring issues to NG-RAN:
    Opt3 forbidden to use RQI. This means special handling by NG-RAN.
    Additional effort for DRB configuration when receiving Handover Request message.
    Additional effort for remapping/reconfiguring UE with pain but no gain
    Data transmission interruption between forwarded data and fresh data due to reconfiguration/remapping
    For intra-sys HO, the target has flexibility for DRB configuration and mapping. For inter-system, the target must follow the source mapping for option 3.
    NG-RAN and UPF support E-RAB concept.
  With all above, RAN3 agreed Option 2 as the working agreement.
  Also a majority of companies opposed to introduce both options.

## Slide 3: Summary and way forward
The topic has been discussed sufficiently in RAN3.
RAN3 working agreement follows the previous RAN3/SA2 agreement (summarized in the annex for information). Option 3 doesn’t.
Data forwarding is an important feature for SA. Continuing the discussion in RAN3 after December 2018 would cause delay in standardization as well as deployment of SA .
Therefore, the co-sourcing companies propose to approve the CR in RP-182670 which is aligned with RAN3 working agreement.

## Slide 4: Annex: Agreements in TS38.300
5G -> 4G
9.3.2.4 Data Forwarding
The inter-System data forwarding follows the following key principles:
- Only indirect data forwarding is supported.
- PDU session information at the serving NG-RAN node contains mapping information per QoS Flow to a corresponding E-RAB.
- At handover preparation, the source NG-RAN node shall decide which mapped E-RABs are proposed to be subject to data forwarding and provide this information in the source-to-target container to the target eNB.
- The target eNB assigns forwarding TEID/TNL address(es) for the E-RAB(s) for which it accepts data forwarding.
- A single data forwarding tunnel is established between the source NG-RAN node and UPF per PDU session for which at least data for a single QoS Flow is subject to data forwarding. For the QoS flow(s) accepted for data forwarding, the NG-RAN node initiates data forwarding to the UPF by the corresponding PDU session data forwarding tunnel(s). Then the UPF maps data received from the per PDU session data forwarding tunnel(s) to the mapped EPS bearer(s).

## Slide 5: Annex: Agreements in TS38.300
4G -> 5G
9.3.3.1 Data Forwarding
The inter-System data forwarding from EPS to 5GS follows the following key principles:
- Only indirect data forwarding is supported.
- The target NG-RAN node receives in the Handover Request message the mapping between E-RAB ID(s) and QoS Flow ID(s). It decides whether to accept the data forwarding for E-RAB IDs proposed for forwarding within the source to target container. It assigns a TEID/TNL address for each PDU session for which at least one QoS flow is involved in the accepted forwarding.
- The target NG-RAN node sends the Handover Request Acknowledge message in which it indicates the list of PDU sessions and QoS flows for which it has accepted the forwarding.
- The source eNB receives in the Handover Command message the list of E-RAB IDs for which the target NG-RAN node has accepted the forwarding of corresponding PDU sessions and QoS flows.
- For each E-RAB accepted for data forwarding, the source eNB forwards data to the SGW in the corresponding E-RAB tunnel and the SGW forwards the received data to the UPF in the E-RAB tunnel. Then the UPF maps the data received from an E-RAB tunnel to the corresponding mapped PDU session tunnel. The target NG-RAN node prioritizes the forwarded packets over the fresh packets for those QoS flows which are involved in the accepted forwarding.

## Slide 6: Annex: Agreements in TS23.502
5G -> 4G
4.11.1
11. The AMF sends the Handover Command to the source NG-RAN (Transparent container (radio aspect parameters that the target eNB has set-up in the preparation phase), CN tunnel info for data forwarding per PDU Session, QoS flows for Data Forwarding). The source NG-RAN commands the UE to handover to the target access network by sending the HO Command. The UE correlates the ongoing QoS Flows with the indicated EPS Bearer IDs to be setup in the HO command. The UE locally deletes the PDU Session if the QoS Flow associated with the default QoS rule in the PDU Session does not have an EPS Bearer ID assigned. If the QoS Flow associated with the default QoS rule has an EPS Bearer ID assigned, the UE keeps the PDU Session (PDN connection) and for the remaining QoS Flow(s) that do not have EPS bearer ID(s) assigned, the UE locally deletes the QoS rule(s) and the QoS Flow level QoS parameters if any associated with those QoS Flow(s). The UE deletes any UE derived QoS rules. The EPS Bearer ID that was assigned for the QoS flow of the default QoS rule in the PDU Session becomes the EPS Bearer ID of the default bearer in the corresponding PDN connection.
For the QoS Flows indicated in the "QoS Flows for Data Forwarding", NG-RAN initiate data forwarding via to the PGW-U+UPF based on the CN Tunnel Info for Data Forwarding per PDU Session. Then the PGW-U+UPF maps data received from the data forwarding tunnel(s) in the 5GS to the data forwarding tunnel(s) in EPS, and sends the data to the target eNodeB via the Serving GW.

## Slide 7: Annex: Agreements in TS23.502
4G -> 5G
4.11.1.2.2.2
    10. The NG-RAN sends a Handover Request Acknowledge (Target to Source Transparent Container, N2 SM response (PDU Session ID, list of accepted QFI(s) and AN Tunnel Info), T-RAN SM N3 forwarding info list (PDU Session ID, N3 Tunnel Info for data forwarding)) message to the AMF. The NG-RAN includes one assigned TEID/TNL address per PDU Session (for which there is at least one QoS flow for which it has accepted the forwarding) within the SM Info container. It also includes the list of QoS flows for which it has accepted the forwarding. If one EPS bearer in EPS is mapped to multiple QoS flows in 5GS, all such QoS flows need to be accepted to support indirect data forwarding during EPS to 5GS mobility. Otherwise, the NG RAN rejects the indirect data forwarding for the QoS flows which are mapped to the EPS bearer.
4.11.1.2.2.3
    3. Handover Confirm: the UE confirms handover to the NG-RAN.
    The UE moves from the E-UTRAN and synchronizes with the target NG-RAN. The UE may resume the uplink transmission of user plane data only for those QFIs and Session IDs for which there are radio resources allocated in the NG-RAN.
    The E-UTRAN performs indirect data forwarding via the SGW and the v-UPF. The v-UPF forwards the data packets to the NG-RAN using the N3 Tunnel Info for data forwarding, adding the QFI information. The target NG-RAN prioritizes the forwarded packets over the fresh packets for those QoS flows for which it had accepted data forwarding.

## Slide 8: Thank you