## Slide 1: NOMA and advanced receivers at g-Node B
ORANGE
3GPP TSG RAN#82 10-13 December 2018 Sorrento, Italy | TDoc RP-182624 Agenda Item 9.3.4

## Slide 2: Background
NOMA is a study item which investigates Non Orthogonal Transmission Schemes together with advanced receivers. The scope of the NOMA SI is very wide since it considers eMBB, mMTC and URLLC services, however, the evaluation was mainly focused on UL transmission with configured grant in the synchronous case.
RAN1#95 was the last meeting of the SI
NOMA evaluation efforts suffered from the beginning of a lack of clearly defined baseline (called OMA reference) and receiver benchmarks [1]
  The huge simulation effort of the NOMA SI is difficult to exploit since the different companies were neither able to agree on the reference OMA baseline nor on the receiver architecture benchmark(s)

## Slide 3: Background
In order to discriminate between the performance gains that come from modifying the Rel. 15 transmission scheme and the advanced receiver, it is fair to consider as OMA reference schemes techniques that do not impact the NR Rel. 15 standard (i.e. UE transparent) and that use the same receiver benchmarks as for NOMA schemes.
Two main classes of receiver architecture were considered (at least for the synch case) based on linear filters with Interference Cancellation (IC)
  Low complexity: hard-IC (hard L-CWIC)
  Medium complexity: Hybrid-IC (mixing hard-IC and soft-IC/turbo L-CWIC)

## Slide 4: Background
It was shown by one company that Rel. 15 transmission schemes, for instance the Low Coding Rate Spreading (LCRS) NOMA candidate, can yield similar system level performance to the other candidates under hard-IC and Hybrid-IC receiver types, and no restriction on resource allocation, Some companies consider that the NOMA reference should not allow more collisions than the number of available orthogonal resources including the number of receive antennas (i.e., no overloading)
  This restriction seems artificial if the receiver benchmarks can deal with overloading without impacting Rel. 15 transmission scheme
  It was shown from Link Level Simulations that LCRS yields similar performance to the other schemes
This comes down to stating that the base station receiver side plays the most important role and that there is maybe no need to introduce new transmission schemes and modify the RAN1 specifications
  For NOMA (which includes MU-MIMO in the uplink) Interference Cancellation (IC) at the receiver side is a key functionality
As a result, the advanced receiver functionality should be made “visible” within the industry independently of the NOMA SI outcome

## Slide 5: Background
Interest of advanced receivers in base station with specified performance requirements:
  For Operators: advanced receivers in the base stations and their associated performance requirements are important to operators to optimize spectral efficiency and network cost.
  For Infra Vendors: they can propose different receiver type to the operators referring to the 3GPP specifications, with well understood minimum performance requirements
  This approach was followed for LTE-Rel. 15 for hard–IC (CWIC receiver) MU-MIMO [2]

## Slide 6: Proposals
Based on the findings of NOMA SI, 3GPP should tackle the definition and performance requirements of several receiver types at the g-Node B in RAN4 specification (TR38.104) in addition to the LMMSE-IRC Rel. 15 reference
  RAN4 WI to consider two receiver types at g-Node B for MU-MIMO with configured grant (e.g., mMTC, URLLC) or dynamic grant (e.g., eMBB)
    Hard-IC
    Hybrid-IC
Continue to investigate the interest of non spec transparent NOMA schemes in a SI follow up with well agreed OMA reference and receiver benchmark(s)
  OMA reference: Rel. 15 scheme with same receiver benchmark as NOMA
  Receiver benchmarks: Hard-IC and Hybrid-IC
The synch and asynch NOMA should be dealt in separate SI since the scenarios and use cases as well as the maturity of these two cases are not the same:
  Asynchronous case to be considered together with RRC Inactive transmission

## Slide 7: References
[1] R1-1813544 ,On receiver architecture benchmarks for OMA and NOMA, Orange, RAN1#95
[2] 3GPP TS 36.104 V15.4.0 (2018-09) Section 8.2.9