## Slide 1: Proposed Way Forward on NOMA
3GPP TSG RAN Meeting #82
Sorrento, Italy, Dec 10 – 13, 2018
Source: Intel Corporation
Agenda item: 9.3.4
Document for: Discussion, Decision
RP-182752
(Revision of RP-182487)

## Slide 2: Introduction
  Throughout this contribution, “NOMA” refers to grant-free (or configured grant) UL NOMA, where multiple UEs autonomously transmit data without explicit grant from gNB over time/freq (T/F) resource pool commonly used by multiple UEs.
  UL MU-MIMO vs. NOMA.
  UL MU-MIMO: Typically assume that #UEs assigned to (or transmitting on) the same T/F resources is equal to or less than #Rx antennas at the gNB. Not well fit into grant-free UL transmissions.
  UL NOMA: #UEs assigned to (or transmitting on) the same T/F resources assumed to be much larger than #Rx antennas. In general, advanced “NOMA” receivers, e.g., SIC or other type of multi-user detector, are assumed for NOMA operation. Conventional MU-MIMO receivers would not work well for NOMA in many cases.
  NOMA receiver procedure at a given point of time for given T/F NOMA resource pool is, comprised of the following two steps:
  Step 1, UE identification. Identify the a set of UEs that are simultaneously transmitting. This is common and prerequisite to all NOMA schemes due to the nature of “grant-free” transmission.
  Step 2, Multi-user decoding. Decode the packets from the set of UEs identified in Step 1. Advanced receivers such as MMSE-SIC/PIC and EPA are generally assumed to maximize the NOMA gain.
.
.
.
UL grant-free Tx over common time/freq resource pool
UL NOMA

## Slide 3: key Takeaways from The Study during Rel-14 to 16
  Significant NOMA gain over OMA (inc. MU-MIMO). NOMA can substantially improve the system performance over OMA (including MU-MIMO) for small packet transmissions for all the use cases studied, eMBB, URLLC, and mMTC.
  Observation from the study in Rel-14 (TR 38.802)
    SLS results show that all simulated NOMA schemes provide significant capacity gain in terms of packets arrivals rate at a given system outage.
  Observation from the study in Rel-15 & 16 (TR 38.812)
    NOMA gain observed is 10% - 150%, 42%-250%, and 46%-150%, for eMBB, URLLC, and mMTC, respectively.
  Little performance difference among NOMA proposals including LCRS. Spreading is key in NOMA to tackle interference from other UEs. LCRS (Low Code Rate Spreading) is a NOMA proposal from Intel, where spreading is realized by employing low code rate, not requiring any spec changes from Rel-15 PUSCH. LLS/SLS results show little performance difference among all NOMA schemes including LCRS under fair/realistic assumptions
  This implies that the NOMA gain can be mostly achieved by employing advanced receivers (little gain from modifications to Rel-15 PUSCH). Indeed, this is aligned with Information-theoretic insight from “the capacity region of multiple access channel with Gaussian noise”, where the achievability can be proved by successive cancellation receiver w/ no change at the Tx side.
  Still some areas that need to be improved, e.g., DMRS for Step 1 (UE identification) and HARQ.
  To be elaborated on next slides.

## Slide 4: areas of Normative Work: DMRS enhancement
DMRS is assumed to be used for Step 1 execution (UE identification). Once a DMRS collision occurs, gNB is not able to exactly identify the set of UEs transmitting, and thereby unlikely to decode the corresponding packets.
  Most companies have assumed in their simulations DMRS capacity larger than supported by Rel-15
  Simulation results on the bottom show
  DMRS capacity increase from Rel-15 can significantly reduce the DMRS antenna port (AP) collision probability
  DMRS capacity increase can substantially improve the performance

## Slide 5: areas of Normative Work: Explicit HARQ Feedback
For UL transmission without dynamic grant, Rel-15 supports only a timer based approach for HARQ ACK response, i.e., UE assumes ACK if the timer expires.
However, for configured grant NOMA transmission, the implicit HARQ-ACK feedback mechanism is not sufficient when multiple UEs transmit data in a shared time/frequency resource.
  gNB may miss detect some of the packets  according to Rel-15 mechanism, UE assumes ACK response when the timer expires.
  To ensure a common understanding between gNB and UE, support of explicit HARQ-ACK feedback is critical for configured grant NOMA.
During the SI phase, support of explicit HARQ feedback was proposed by multiple companies including Ericsson (R1-1813256), ZTE (R1-1812174), vivo (R1-1812295), Samsung (R1-1808762), and Intel (R1-1812477).

## Slide 6: areas of Normative Work: “Preamble + Data” in 2-step RACH
  Enabling “preamble + data” transmission in 2-step RACH can substantially improve the system performance in terms of capacity, latency, and UE power consumption.
  Preamble + data transmission in 2-step RACH  by nature, grant-free NOMA (i.e., multiple UEs are allowed to transmit over the same T/F resources)  technically, reasonable to develop 2-step RACH under NOMA WI taking into account NONA receiver.
  Potential objectives
  Develop linkage between PRACH preamble and DMRS and/or scrambling sequences of data channel, multiplexing of 2-step RACH and 4-step RACH, and details of Msg-B (Msg-2+Msg-4), fallback of 4-step to 2-step RACH
  Applicable for all UE modes, RRC_IDLE, RRC_INACTIVE, and RRC_CONNECTED, but the main target would be RRC_INACTIVE.
  2-step RACH can be also beneficial for positioning including mmWave based positioning depending on NR positioning study.

## Slide 7: Proposed WF on NOMA
  Approve a NOMA WID with the following scope
  No change in data part (i.e., reusing NR Rel-15 PUSCH) for NOMA
  DMRS enhancements considering NOMA performance improvement
    Assume NOMA receiver, e.g., MMSE-SIC/PIC, EPA, etc.
  Support of explicit HARQ Feedback for grant-fee NOMA including 2-step RACH
  2-step RACH allowing “preamble and data” transmission at the first step, taking into account “NOMA” receivers.
    Mainly targeting RRC_INACTIVE
    Develop linkage between PRACH preamble and DMRS and/or scrambling sequences of data channel, multiplexing of 2-step RACH and 4-step RACH, and details of Msg-B (Msg-2+Msg-4), fallback of 4-step to 2-step RACH, etc., where enhanced DMRS can be assumed.