## Slide 1: Motivation for correction to aperiodic CSI-RS triggering with different numerology between PDCCH and CSI-RS
3GPP TSG RAN Meeting#82
Sorrento, Italy, December 10-13, 2018
Agenda Item: 9.2.1
Source: Ericsson
Document for: Discussion, Decision
RP-182834

## Slide 2: Background
In Inter-band CA between low band and high-band:
  Channel measurements for high-band are crucial for meaningful DL throughput on high-band.
  Uplink coverage in high-band is limited
  For Inter-band CA operation between low band and high band, channel measurements on high-band should be reported via low band.
Low band
HB (UL)
High band (HB)
Low band (LB)
DL
UL
HB (DL)

## Slide 3: Background
Cross-carrier scheduling with mixed numerologies
  At RAN plenary #81, cross-carrier scheduling with mixed numerologies was postponed to Rel-16 (RP-182014)
“Cross-carrier scheduling with different numerologies is postponed to Rel-16. Already-agreed functionality for cross-carrier scheduling with different numerologies will not be removed from the Rel-15 specs, but will have a note added that the behaviour does not apply in this release.”
UL
PUSCH
DCI
Self-scheduling PUSCH (Supported in Rel-15)
Carrier X (µ1)
Cross-carrier scheduling PUSCH (not supported in Rel-15)
PUSCH
Carrier Y (µ2)
µ1≠µ2

## Slide 4: Background
In RAN1#92bis, open issues for CSI measurement for the following scenario were discussed:
  DCI on Carrier X scheduling PUSCH on Carrier X with aperiodic CSI report for Carrier Y based on aperiodic CSI-RS
In that discussion, the RAN plenary agreement was mis-interpreted due to the use of incorrect terminologies and incorrect association of measurement features to scheduling features
  Triggering measurement resources on a different carrier was mis-interpreted as scheduling on a different carrier
Hence, the following was concluded:
  “Triggering A-CSI reports whose measurement resources are with different numerology from that with PDCCH is not supported in Rel-15. “
Carrier Y (µ2)
UL
PUSCH
DCI
Carrier X (µ1)
µ1≠µ2
A-CSI report
CSI-RS

## Slide 5: Triggering and Scheduling Clarifications
In this scenario, the DCI achieves the following
  Self-carrier scheduling: DCI on Carrier X schedules PUSCH on Carrier X to carry “A-CSI report”
  Triggering “A-CSI report”: Provides link to a CSI-RS configuration for measurements
    Occasion of CSI-RS is obtained from the configuration (DL BWP and Offset)
This scenario does not involve “cross-carrier scheduling”
UL
PUSCH
DCI
Self -scheduling PUSCH with A-CSI report
Carrier X (µ1)
Carrier Y (µ2)
µ1≠µ2
A-CSI report
CSI-RS resources for measurement obtained from configuration
CSI-RS

## Slide 6: Limitation to avoid excessive UE buffering
In order to not require UE to buffer data for slots in a higher numerology in anticipation of potential aperiodic CSI-RS trigger from a lower numerology, it is reasonable to limit possible CSI-RS triggering offsets to only occur later slots than the last slot overlapping the PDCCH slot
UL
DCI
CSI-RS trigger offset
Carrier X (µ1)
Carrier Y (µ2)
µ1≠µ2

## Slide 7: Other relaxation
The CR only applicable when the SCS of the carrier with PDCCH is smaller than the one with CSI-RS.
In case of mixed numerology, additional d symbols to Y is included to provide additional relaxation for decoding PDCCH and beam switching time
  Y is the beamSwitchingTiming
The feature is proposed to be an optional feature per UE (Type 2).
UL
PUSCH
DCI
Self -scheduling PUSCH with A-CSI report
Carrier X (µ1)
Carrier Y (µ2)
µ1≠µ2
A-CSI report
CSI-RS resources for measurement obtained from configuration
CSI-RS
d+Y

## Slide 8: Proposals
Adopt the following proposals
Proposal:
  Clarify that scheduling PUSCH on Carrier X carrying an aperiodic CSI report for Carrier Y with carriers X and Y having different numerologies is not considered cross-carrier scheduling
    This feature should not be excluded from Rel-15.
Proposal:
  Adopt the companion CR (RP-182833) aligning the procedure for determining CSI-RS resource for measurement with already existing behavior in Rel-15 (e.g. PDCCH and PUCCH with different numerologies)
Proposal:
  Scheduling PUSCH on Carrier X carrying an aperiodic CSI report for Carrier Y with carriers X and Y having different numerologies is an optional UE feature of Type 3 capability in Rel-15.

## Slide 9: CR for Determination of CSI-RS Resource (RP-182833)
Determination of the CSI-RS resource needs clarification on the reference slot from which the slot offset obtained from CSI-RS configuration is to be applied
The CR aligns the procedure for determining the reference slot with the already existing behaviour in Rel-15 (e.g. PDCCH and PUCCH with different numerologies)
  The reference slot on the carrier with CSI-RS resources is the latest slot that overlaps with the slot containing DCI.
  The slot offset is based on the numerology of the carrier with CSI-RS.
UL
PUSCH
DCI
Self -scheduling PUSCH with A-CSI report
Carrier X (µ1)
Carrier Y (µ2)
µ1≠µ2
A-CSI report
CSI-RS resources for measurement obtained from configuration
CSI-RS
Reference Slot